## Slide 1: MAC calibration results comparison
Date: 2014-09-10
Authors:

## Slide 4: Summary
This contribution provides result comparison of MAC calibration of test 1-3 from variety of companies [1][2][3]
This contribution also proposes a criteria for result alignment
There are some parameter setting in the simulation scenario document that may generate different interpretation, this contribution clarifies these parameter settings

## Slide 5: Status Overview
Status √: aligned, −: No need to provide
Calibration | Box 3 – MAC Calibration |  |  |  |  |  |  |  |  |  |  |  | 
Simulation Scenarios | Test 1a |  |  |  | Test 1b |  |  |  | Test 2a |  | Test 2b | Test 3 | Test 4
Scenario Names | MAC overhead w/out RTS/CTS |  |  |  | MAC overhead w RTS/CTS |  |  |  | Deferral Test 1 |  | Deferral Test 2 | NAV deferral | Deferral Test for 20 and 40MHz BSSs
Configurations | MCS = [0] | MCS = [0] | MCS = [8] | MCS = [8] | MCS = [0] | MCS = [0] | MCS = [8] | MCS = [8] | RTS/CTS [OFF] | RTS/CTS [ON] | RTS/CTS [OFF] | RTS/CTS [ON] | 
Metrics | MAC Tput | Check Points | MAC Tput | Check Points | MAC Tput | Check Points | MAC Tput | Check Points | MAC Tput | MAC Tput | MAC Tput | MAC Tput | 
LG | √ | √ | √ | − | √ | √ | √ | − | √ | √ | √ | √ | 
Huawei | √ | √ | √ | − | √ | √ | √ | − | √ | √ | √ | √ | 
Qualcomm | √ | √ |  | − | √ | √ |  | − | √ | √ | √ | √ | 
MediaTek | √ | √ | √ | − | √ | √ | √ | − |  | √ |  | √ | 
Intel | √ | √ | √ | − | √ | √ | √ | − | √ | √ | √ | √ | 
Ericsson | √ | √ | √ | − | √ | √ | √ | − | √ | √ | √ | √ | 
Nokia | √ |  | √ | − | √ |  | √ | − | √ | √ |  |  | 
NTT | √ |  | √ | − | √ |  | √ | − | √ | √ | √ | √ | 
Samsung | √ |  | √ | − | √ |  | √ | − | √ | √ | √ | √ | 
Broadcom | √ |  | √ | − | √ |  | √ |  | √ | √ | √ |  | 
ZTE | √ |  | √ |  | √ |  | √ |  | √ | √ |  | √ | 
Toshiba | √ | √ | √ | − | √ | √ | √ | − | √ | √ | √ | √ | 
Criteria:
  Make average over most close three companies as the baseline to compare
  If the performance value intended for calibration is within 5% deviation, it is marked as aligned

## Slide 6: Test 1a
AP1
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.79 | 5.55 | 5.84 | 6.00 | 21.98 | 34.91 | 43.24 | 48.67
LGE | 4.81 | 5.55 | 5.84 | 5.99 | 22.4 | 35.2 | 43.25 | 48.9
Qualcomm | 4.76 | 5.53 | 5.82 | 5.98 | 23.92 | 37.25 | 45.55 | 50.81
MediaTek | 4.76 | 5.53 | 5.82 | 5.98 | 21.71 | 34.65 | 42.71 | 48.15
Intel | 4.76 | 5.53 | 5.82 | 5.98 | 21.53 | 34.46 | 42.58 | 48.14
Ericsson | 4.75 | 5.52 | 5.82 | 5.97 | 21.53 | 34.47 | 42.57 | 48.09
Nokia | 4.76 | 5.52 | 5.83 | 5.97 | 21.19 | 34.22 | 41.93 | 47.74
NTT | 4.79 | 5.54 | 5.84 | 6.00 | 22.00 | 35.00 | 43.20 | 48.40
Samsung | 4.76 | 5.53 | 5.82 | 5.97 | 21.54 | 34.48 | 42.60 | 48.15
Broadcom | 4.76 | 5.53 | 5.83 | 5.98 | 21.4 | 34.2 | 42.5 | 48.0
ZTE | 4.76 | 5.53 | 5.82 | 5.98 | 21.42 | 34.23 | 42.55 | 48.01
Toshiba | 4.79 | 5.54 | 5.83 | 5.99 | 21.94 | 34.87 | 43.19 | 48.62

## Slide 7: Test 1b
AP1
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 27.07 | 34.97 | 40.61
LGE | 4.45 | 5.31 | 5.66 | 5.86 | 16.2 | 27.3 | 35 | 40.8
Qualcomm | 4.4 | 5.29 | 5.64 | 5.84 | 18.64 | 30.75 | 38.94 | 44.51
MediaTek | 4.40 | 5.29 | 5.64 | 5.84 | 15.79 | 26.90 | 34.62 | 40.24
Intel | 4.4 | 5.29 | 5.64 | 5.84 | 15.7 | 26.8 | 34.55 | 40.26
Ericsson | 4.36 | 5.26 | 5.62 | 5.82 | 15.36 | 26.33 | 34.02 | 40.45
Nokia | 4.40 | 5.28 | 5.64 | 5.83 | 15.52 | 26.66 | 34.12 | 39.96
NTT | 4.42 | 5.30 | 5.67 | 5.85 | 16.00 | 27.10 | 34.97 | 40.40
Samsung | 4.40 | 5.28 | 5.63 | 5.83 | 15.94 | 27.09 | 34.59 | 40.35
Broadcom | 4.40 | 5.29 | 5.65 | 5.84 | 15.6 | 26.7 | 34.5 | 40.14
ZTE | 4.39 | 5.28 | 5.64 | 5.83 | 15.61 | 26.61 | 34.45 | 40.08
Toshiba | 4.42 | 5.30 | 5.65 | 5.85 | 15.92 | 27.04 | 34.94 | 40.58

## Slide 8: Test 2a
AP1
Configurations | Without RTS/CTS |  |  |  | With RTS/CTS |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.56 | 5.25 | 5.51 | 5.66 | 4.46 | 5.33 | 5.68 | 5.87
LGE | 4.62 | 5.28 | 5.54 | 5.66 | 4.5 | 5.34 | 5.68 | 5.88
Qualcomm | 4.57 | 5.26 | 5.53 | 5.67 | 4.45 | 5.32 | 5.67 | 5.86
MediaTek | 4.71 | 5.48 | 5.78 | 5.94 | 4.35 | 5.24 | 5.62 | 5.81
Intel | 4.52 | 5.22 | 5.48 | 5.62 | 4.44 | 5.31 | 5.67 | 5.86
Ericsson | 4.53 | 5.21 | 5.48 | 5.63 | 4.42 | 5.30 | 5.65 | 5.85
Nokia | 4.58 | 5.29 | 5.56 | 5.71 | 4.48 | 5.32 | 5.67 | 5.85
NTT | 4.58 | 5.25 | 5.45 | 5.66 | 4.49 | 5.35 | 5.70 | 5.88
Samsung | 4.58 | 5.27 | 5.53 | 5.67 | 4.45 | 5.31 | 5.67 | 5.86
Broadcom | 4.52 | 5.23 | 5.47 | 5.61 | 4.44 | 5.32 | 5.67 | 5.86
ZTE | 4.56 | 5.25 | 5.51 | 5.65 | 4.39 | 5.29 | 5.63 | 5.82
Toshiba | 4.52 | 5.21 | 5.48 | 5.62 | 4.42 | 5.30 | 5.66 | 5.85

## Slide 9: Test 2b results
L4 Tputs with MPDU Frame Aggregation (FA)
Scenarios | MCS0 |  | MCS8 | 
 | noFA | FA | noFA | FA
Huawei | 1.62 | 1.01 | 26.54 | 34.75
LGE | 1.7 | 1.02 | 26.8 | 35.0
Qualcomm |  | 0.98 |  | 
MediaTek |  | 0.03631 |  | 
Intel | 1.61 | 1.01 | 26.66 | 35.20
Ericsson | 1.78 | 1.22 | 25,49 | 33,52
Nokia |  | 1.20 |  | 35.66
NTT | 1.71 | 1.06 | 26.77 | 35.27
Samsung |  | 1.01 |  | 37.22
Broadcom |  | 1.05 |  | 34.30
ZTE |  | 1.2 |  | 
Toshiba |  | 1.01 |  | 35.11

## Slide 10: Test 3 results
L4 Tputs with MPDU Frame Aggregation (FA)
Scenarios | MCS0 |  | MCS8 | 
 | noFA | FA | noFA | FA
Huawei | 5.15 | 5.58 | 22.04 | 34.05
LGE | 5.14 | 5.58 | 22.4 | 34.2
Qualcomm |  | 5.55 |  | 
MediaTek |  | 5.63933 |  | 
Intel | 5.06 | 5.57 | 20.35 | 31.93
Ericsson | 5.21 | 5.63 | 22.84 | 34.41
Nokia |  | 5.59 |  | 31.35
NTT | 5.18 | 5.60 | 22.10 | 34.01
Samsung |  | 5.41 |  | 33.55
Broadcom |  | 5.32 |  | 30.45
ZTE |  | 5.58 |  | 
Toshiba |  | 5.61 |  | 33.81

## Slide 11: Summary
The functional test results from different parties are generally aligned.
  MAC/PHY Framing aligned very well
  Deferral in light collision case aligned very well
  Deferral in intensive collision case (with hidden node) is not so well aligned.
But we shall reduce the gap among different parties to allow the simulator could be still pretty well aligned when more functions are added and applied to more general performance test scenarios.

## Slide 12: Reference
[1]11-14-1230-00-00ax-mac-calibration-result.pptx
[2]11-14-1192-00-00ax-comparing-mac-calibration-results.pptx
[3] NTT UPDATE 11-14-1192-03-00ax-comparing-mac-calibration-results.pptx
[4] ZTE-UPDATE 11-14-1192-04-00ax-comparing-mac-calibration-results.pptx
[5] Intel UPDATE 11-14-1192-04-00ax-comparing-mac-calibration-results.pptx
[6] Broadcom UPDATE 11-14-1192-04-00ax-comparing-mac-calibration-results.pptx
[7] Ericsson UPDATE 11-14-1192-04-00ax-comparing-mac-calibration-results.pptx
[8] Samsung UPDATE 11-14-1192-04-00ax-comparing-mac-calibration-results.pptx
[9] Toshiba UPDATE 11-14-1192-04-00ax-comparing-mac-calibration-results_43991_r1.pptx