## Slide 1: Considerations on CCA for OBSS Opearation in 802.11ax
Date: 2014-09-11
Authors:

## Slide 2: Introduction
802.11ax aims at providing good performance in dense environments . This can be achieved by introducing features that mitigate interferences and improve operation in overlapping BSSs (OBSS).
  Various mechanisms based on CCA adjustments have shown good potential for increasing effective area throughput due to increasing simultaneous transmission opportunities[1-5].
In this submission, we present:
  Simulation results from our integrated SLS using CCA adjustment
  Other considerations on CCA

## Slide 3: Global CCA Adjustment
  Similar to other contributions[1-5], our simulation results and analysis show that the mean STA throughout varies with global CCA adjustments, but is hard to achieve an optimal CCA setting to improve performance of edge STAs.
 | Integrated SS
Optimal CCA for mean | -60
Optimal CCA for 5% | -70
Mean STA throughput
Edge STA throughput
Integrated SLS
Integrated SLS
Simulation scenario 3: 100 apartments, 20 per floor (2x10), 5 floors. 10x10x3m dimensions;
Frequency: 2.4 GHz, each BSS randomly picks 1 of 3 20 MHz channels; Zero ACI;
Traffic: DL/UL mixed

## Slide 4: Further Considerations on CCA(1)
CCA adjustment with AP coordination
  CCA may be influenced by interference level of neighboring BSSs, especially in dense OBSS scenarios
  Coordinated information sharing between APs may improve the performance resulting from CCA adjustment
Complexity of the CCA algorithm
  Per-STA dynamic algorithm may sacrifice the efficiency and increase overhead
  Per-BSS CCA adjustment(e.g. semi-static) may simplify the algorithm and reduce complexity on implementation, compared with per-STA CCA adjustment

## Slide 5: Further Considerations on CCA(2)
How to perform CCA in OFDMA BSS?
  In OFDM case, one transmitter and one receiver can clear its channel with RTS/CTS exchange
  OFDMA is now introduced in 11ax. AP winning the channel(e.g. with CTS) can not guarantee all scheduled STAs are clear to transmit or receive.
  CCAs setting mechanism for OFDMA STAs should be investigated and introduced in 11ax.
AP1
STA
AP2

## Slide 6: Further Considerations on CCA(3)
For beamforming case, omni-directional CCA may not accurate for channel assessment
  The channel in the beam direction may be clear, even omni-directional CCA is indicated busy
Adaptive CCA for beamformed devices
  Directional CCA to assist beamforming
  Different CCA threshold setting for directional CCA

## Slide 7: Further Considerations on CCA(4)
How to do CCA on multiple channels?
  Current 11ac CCA detection mechanism based on primary channel is not efficient for large BW transmission[10]
  High efficient and flexible CCA thresholds and mechanism should be designed for 11ax
    can be independent to the CCA of the primary channel
    flexible for large BW channels
    …

## Slide 8: Reference
  [1] 11-14/0861, “Impact of CCA adaptation on spatial reuse in dense residential scenario”, Nokia
  [2] 11-14/0833, “Residential Scenario Sensitivity and Transmit Power Control Simulation Results”, InterDigital
  [3] 11-14/0872, “A Protocol Framework for Dynamic CCA”, Realtek
  [4] 11-14/0868, “UL & DL DSC and TPC MAC simulations”, Ericsson
  [5] 11-14/0880, “Increased Network Throughput with TX Channel Width Related CCA and Rules”, Mediatek