## Slide 1: OFDMA Performance Analysis
Date: 2014-09-15
Authors:
Name | Affiliations | Address | Phone | Email
Tianyu Wu | Mediatek | San Jose, CA, USA |  | tianyu.wu@mediatek.com
Jianhan Liu | Mediatek | San Jose, CA, USA |  | jianhan.liu@mediatek.com
James Wang | Mediatek |  |  | james.wang@mediatek.com
Thomas Pare | Mediatek | San Jose, CA, USA |  | thomas.pare@mediatek.com

## Slide 2: Background
OFDMA is a promising technology to increase the area throughput
From PHY POV, OFDMA can benefit from diversity gain
  By assigning each resource blocks (RBs)* to the STA with highest SINR, OFDMA can benefit from multi user diversity and frequency diversity gain.
  System complexity and OFDMA throughput is a tradeoff:
    More active STAs participating in the OFDMA transmission will bring higher throughput gain but lead to larger scheduling/grouping complexity.
    On frequency selective fading channels, smaller RB size will bring higher throughput gain but lead to larger signaling and scheduling/grouping complexity
In this contribution, we study the OFDMA performance on frequency selective fading channels
*Note: RB is considered as a number of subcarriers on all symbols of the packet. Do not consider time domain granularity in this contribution.

## Slide 3: OFDMA performance
OFDMA PHY throughput depends on:
  Number of active STAs participating OFDMA transmission
    Affect the multi-user diversity gain
  Size of resource blocks(RB)
    Affect the frequency diversity gain
  Channel model
    Different channel model will have different coherence BW and lead to different RB size requirement
  Scheduling scheme.
    Simple throughput maximizing scheduling is used in the analysis
  Power allocation etc.
    For simplicity, we do equal power allocation on all RBs.

## Slide 4: OFDMA throughput vs Number of STAs
More active STAs achieve higher throughput gain
The number of active STAs restricted by delay and overhead
10-20 active STAs can achieve quite good throughput gain
We use 10 active STAs in the following simulations.

## Slide 5: Coherence BW for Channel models
Coherence BW can be calculated from RMS delay spread.
RB size selected within the coherence BW shall bring little OFDMA throughput loss
  However, the coherence BW is quite small especially for outdoor channels
  How RB size affect the OFDMA throughput will be studied in the following simulations.
Channel model | RMS delay spread (ns) | Coherence BW (MHz, 0.5 ) | Sub-carriers for 1x OFDMA | Sub-carriers for 4x OFDMA
B | 15 | 13.3 | 43 | 170
C | 30 | 6.7 | 21 | 86
D | 50 | 4 | 13 | 51
Umi LOS | 103 | 1.9 | 6 | 24
Umi NLOS | 217 | 0.9 | 3 | 12

## Slide 6: Simulation settings
Assume 10 active STAs with traffic for a BSS
  Assuming same long term fading (path loss + shadowing 100db) for all STAs
  Small scale fading between AP and STAs follow channel model D and Umi NLOS
Scheduling scheme: AP assign each RB to the STA with highest average SINR
Simulation on DL OFDMA with fixed Tx power 20dbm
  The PHY throughput shall be same for UL as long as sum Tx power from all transmitting OFDMA STAs are 20dbm and equally allocated on all SCs.
We compare the OFDM throughput averaged over all STAs, OFDM throughput of max AP to STA pair and OFDMA throughput with different size of resource blocks.
  Genie MCS: MCS to achieve highest throughput
  80MHz total BW, LDPC for all links
  All the sub carriers are treated as data subcarriers for simplicity

## Slide 7: Performance comparison for Umi Ch
With RB = 1sc, 130% throughput gain over OFDM average and 60% gain over OFDM max can be achieved.
To achieve over 90% of the optimal throughput, max RB size will be 8 sub carriers (2.5 Mhz).
4x OFDMA symbol has similar results as 1x OFDMA symbol.
1x OFDMA symbol
4x OFDMA symbol

## Slide 8: Performance comparison for channel D
With RB = 1sc, 130% throughput gain over OFDM average and 75% gain over OFDM max can be achieved.
To achieve over 90% of the optimal throughput, max RB size will be 16 sub carriers (5 Mhz).

## Slide 9: SNR distribution comparison
The SNR distribution comparison supports the OFDMA throughput gain.
Within coherence BW, the SNR distribution is very close.
UMI channels
Channel D

## Slide 10: Comparison on different channel models
On Umi channel, the OFDMA performance drops faster than channel D.
  Within coherence BW, the OFDMA performance is close to the max throughput (> 95%)
RB size around 5MHz can achieve >90% throughput for indoor channels and close to 90% for outdoor channel models.

## Slide 11: Conclusions
With more active STAs participating in the OFDMA transmission, larger throughput gain can be achieved
  With 10-20 active STAs, the throughput gain is already quite good
RB size shall be selected as a balance of OFDMA throughput gain and overhead.
  RB size of 5MHz can achieve over 90% gain on channel D and close to 90% gain on Umi channel
  Overhead depends on PHY and MAC design details and is hard to numerically evaluate at this stage.
  OFDMA design shall targeting at supporting smaller RB size (<= 5MHz) to benefit from higher frequency diversity gain.