## Slide 1: Issues on 256-FFT per 20MHz
Date: 2014-09-14
Authors:

## Slide 2: Background (1)
For 11ax, throughput improvement and outdoor operation are required as in PAR.
In [1] and [2], 256-subcarrier in 20MHz BW was considered for longer CP and more number of available subcarriers.
To change the OFDM symbol structure, i.e., CP and subcarrier spacing, the performance and compatibility issues should be addressed.

## Slide 3: Background (2)
Check points in changing OFDM symbol structure
  PAPR problem
  Mid-packet CCA in secondary channels for 11ac legacy devices
  CFO and SFO tracking (after estimation and compensation)
  Phase noise
  Effects of longer symbol duration especially in outdoor channels with high Doppler frequency. (fixed allocation or travelling pilot)
In this contribution, issues which should be considered to change the OFDM symbol structure are addressed.

## Slide 4: PAPR issue (1)
  Due to the total power constraint, the power spectral density of 20MHz packets is (1/4) lower than 80MHz packets.
  Then, the coverage of BSS is determined by 20MHz transmission coverage.
f
PSD of 20MHz BW mode
PSD of 80MHz BW mode
PSD of AWGN

## Slide 5: PAPR issue (2)
The coverage of BSS is the range of a beacon frame with legacy format.
Packets with 266FFT in 20MHz have 6dB higher PAPR. (Rule of Thumb)
Then 6dB more backoff is required for the same linearity of transmit signal.
  This means a 20MHz-256FFT packet has shorter range than a legacy 20MHz packet.
The high PAPR cause the lower energy efficiency in general.

## Slide 6: PAPR (3)
Throughput loss caused by lower transmit power due to the additional back-off can be higher than throughput gain due to longer OFDM symbol duration with 256FFT.
We have to choose FFT size carefully with a consideration of PAPR.

## Slide 7: Mid-packet CCA (1)
11ac used mid-packet detection for secondary channel CCA
  Intension: detect an OBSS transmissions not occupying Primary 20MHz (CCA level is -72dBm which is10dB higher than preamble detect levels)
  In some contributions, CP correlation method was mentioned for mid-packet CCA.
11ah also adopts mid-packet CCA to detect the secondary transmission.
  In 11ah, the CP correlation is used for mid-packet CCA.

## Slide 8: Mid-packet CCA (2)
Examples where mid-packet CCA is issued.
  OBSS with non-aligned primary channel
    After receiving a packet from own BSS, detect the a packet from OBSS occupying secondary CH.
  OBSS with aligned primary channel
    After waiting for end of an OBSS packet, detect the packet from own BSS occupying secondary CH.
Packet from own BSS
Packet from BSS
Primary CH of own BSS
Primary CH of OBSS
This data part should be detected.
Packet from OBSS
Packet from own BSS
Primary CH of two BSSs
This data part should be detected.

## Slide 9: Mid-packet CCA (2)
If OFDMA (simultaneous TX in frequency domain) is adopted in 11ax, the secondary channel transmission can be very frequent even in single BSS condition.
The miss-detection of secondary channels by 11ac devices can cause very harmful effects to 11ax operation.
11ax, CCA for secondary channels is as important as that for primary channel.

## Slide 10: CFO, SFO and phase noise (1)
In [1] and [2], CFO estimation and compensation is considered for performance evaluation. However, tracking with pilots is not included.
As the subcarrier spacing is reduced, the performance is more vulnerable to residual CFO, SFO and phase noise.
These impairments will cause the inter-subcarrier interference which is difficult to track with pilots.
  As OFDM symbol duration increases, the more phase shift occurs between consecutive symbols.
  Then tracking is more difficult.

## Slide 11: Conclusions
To change the OFDM symbol structure, we have to check PAPR, mid-packet CCA and tracking issues.
Longer OFDM symbol structure
  Higher PAPR => lower energy efficiency, coverage, throughput
  Mid-packet CCA => non-compatible with 11ac devices
  Lower tracking performance
If 11ax needs to change the OFDM symbol structure, PAPR is also considered.
Mid-packet CCA issue can be partially resolved by limiting the operating channels.
The tracking performance is also checked.

## Slide 12: References
Jinsoo Choi, “Envisioning 11ax PHY Structure - Part I,” doc. num. 11-14/0804r1, July 2014.
Dongguk Lim, “Envisioning 11ax PHY Structure - Part II,” doc. num. 11-14/0801r0, July 2014.
Youhan Kim, “Enhanced CCA for Non-Primary Channels Using Guard Interval,” doc. Num. 11-10/0012r1, Jan. 2010.