## Slide 1: Issues on 256-FFT per 20MHz
Date: 2014-11-03
Authors:

## Slide 2: Background (1)
For 11ax, throughput improvement and outdoor operation are required as in PAR.
In [1] and [2], 256-subcarrier in 20MHz BW was considered for longer CP and more number of available subcarriers.
To change the OFDM symbol structure, i.e., CP and subcarrier spacing, the performance and compatibility issues should be addressed.
Heejung Yu, Yeungnam Univ./NEWRACOM

## Slide 3: Background (2)
Check points in changing OFDM symbol structure
  Mid-packet CCA in secondary channels
  PAPR problem
  Residual CFO (after estimation and compensation), SFO, phase noise tracking
In this contribution, issues which should be considered to change the OFDM symbol structure are addressed.

## Slide 4: Mid-packet CCA (1)
11ac used mid-packet detection for secondary channel CCA
  Intension: detect an OBSS OFDM(non-HT, HT, VHT) transmissions not occupying Primary 20MHz (CCA level is -72dBm which is10dB higher than preamble detect levels within aCCAMidTime(25us))
  Simplest method to detect mid-packet detection is CP correlation of OFDM symbols

## Slide 5: Mid-packet CCA (2)
We assume 11ax devices use the same time requirement as 11ac devices for mid-packet CCA detection.
This value is 25usec which is >6x OFDM symbol duration of 4usec.
Therefore, 11ac devices can use minimum of 5 consecutive symbols for normal CP and short CP cases.
25usec
time
CP
4 usec
(OFDM symbol duration)

## Slide 6: Mid-packet CCA (3)
In the worst case the 25usec detection window may not fully cover even a single OFDM symbol duration. (See the below figures).
12.8usec
3.2usec
12.8usec
0.8usec
3.2usec
0.8usec
OFDM symbol duration
CP
CP
12.8usec
CP
CP
12.8usec
OFDM symbol duration
time
Detection Window 25usec
Detection Window 25usec

## Slide 7: Mid-packet CCA (4)
Three potential fixes also have problems of their own
  longer aMidCCATime can be adopted.
    longer aMidCCATime results in 11ax devices sensing secondary channels to have lower priority in the use of the secondary channels.
  For mid-packet CCA, use other feature of an OFDM packet, e.g. pilot pattern.
    The possible sensing level should be checked.
    More restriction on the design of pilot.
  Do not support a separate mid-packet CCA rules (for OFDM packet and for other any signal) in 11ax, i.e., perform only energy detection.
    Fairness of usage of the secondary channels is compromised.

## Slide 8: Mid-packet CCA (5)
Examples where mid-packet CCA is issued.
  OBSS with non-aligned primary channel
    After receiving a packet from own BSS, detect the a packet from OBSS occupying secondary CH.
  The miss-detection of secondary channels by 11ac devices can cause very harmful effects to 11ax operation.
Packet from own BSS
(11ac device)
Packet from BSS
(11ax device)
Primary CH of own BSS
Primary CH of OBSS
This data part should be detected.

## Slide 9: Mid-packet CCA (5)
In this contribution, we assume that 11ac devices use a CP correlation method for mid-packet CCA.
However, other mid-packet CCA can be considered.
  ED can be used, but ED cannot verify that the signal is a WiFi signal or not.
  Pilot structure and other features of WiFi signals can be used.

## Slide 10: PAPR (1)
The coverage of BSS is governed by the range of a beacon frame with legacy format.
Packets with 256FFT in 20MHz have higher PAPR than 64FFT.
Higher backoff may be required.
  Potentially a smaller coverage with a 20MHz-256FFT packet
High PAPR leads to lower PA efficiency.

## Slide 11: CDF of PAPR
20 OFDM symbol (only data part) (BPSK)
8x oversampling
20000 packets
At CDF of 99%, 256FFT packets show 1dB higher PAPR than 64FFT packet.

## Slide 12: CFO, SFO and phase noise (1)
In [1] anCFO, SFO and phase noise (1)
d [2], CFO estimation and compensation is considered for performance evaluation. However, tracking with pilots is not included.
As the subcarrier spacing is reduced, the performance is more vulnerable to residual CFO, SFO and phase noise.
These impairments will cause the inter-subcarrier interference which is difficult to track with pilots.
  As OFDM symbol duration increases, high frequency phase noise cannot be compensated.
  Then the tracking capability with pilots is degraded.

## Slide 13: CFO, SFO and phase noise (2)
11ac adopted use of pilots even within VHT-LTF symbols, such that phase compensation can be performed on the LTF symbols themselves.
The motivation was that phase drift (either from residual frequency offset or PLL phase noise) on the LTF symbols spanning 1 to 8 OFDM symbols was significant enough to cause performance issues.
OFDM symbol duration from a 256 FFT can span 4x times the existing OFDM symbol duration, which may get affected by phase drift issue even within a single OFDM symbol.

## Slide 14: CFO, SFO and phase noise (3)
To investigate the effects of phase noise, we have to determine the phase noise model for simulation scenario.
  In 11n, the phase noise model (LPF output of white noise) was used.
To verify the performance considering CFO, SFO and phase noise, the pilot structure is also determined.

## Slide 15: Conclusions
To change the OFDM symbol structure, we should address the following issues: PAPR, mid-packet CCA and phase tracking.
To fully evaluate affect of the changes in the FFT size, we would need PHY simulation results including PAPR effects, CFO, SFO, phase noise, and system level evaluation regarding mid-packet CCA.

## Slide 16: References
Jinsoo Choi, “Envisioning 11ax PHY Structure - Part I,” doc. num. 11-14/0804r1, July 2014.
Dongguk Lim, “Envisioning 11ax PHY Structure - Part II,” doc. num. 11-14/0801r0, July 2014.
Youhan Kim, “Enhanced CCA for Non-Primary Channels Using Guard Interval,” doc. Num. 11-10/0012r1, Jan. 2010.