## Slide 1: Dynamic OFDM Symbol Duration
Date: 2014-09-15
Authors:

## Slide 2: Background and Objectives
4x OFDM symbol duration may enhance efficiency for longer payloads and may have benefit of less CP overhead and finer frequency granularity [1][2] .
Relative to 4x OFDM symbol duration, current 1x OFDM symbol duration may have less padding bits and shorter payload duration for short packets.
Methods for supporting dynamic OFDM symbol duration may result in greater overall efficiency.

## Slide 3: Method 1 (Per Packet Based)
Define one bit Symbol_duration in SIG-A to specify
  Symbol_duration = 0 : OFDM symbol duration 3.2us
  Symbol_duration = 1 : OFDM symbol duration 12.8us
CP ratio
  Specify 4x mode CP ratio
    Normal GI : 1/4 (TBD)
    Short GI : 1/32 (TBD)
  Define 2 bits of CP_ratio in SIG-A to specify the CP ratio and remove SGI indication
    CP_ratio = 0 : 1/4
    CP_ratio = 1 : 1/8
    CP_ratio = 2 : 1/16
    CP_ratio = 3 : 1/32

## Slide 4: Method 2 (NAV protected)
With clock scale down ¼ can reuse the design to get
  1/4 frequency granularity
  4x CP length in time
For example, the 80MHz OFDM packet with clock scale down ¼ can be used in each 20MHz BW
This operation can be protected by new MAC protocol, e.g. use CTS-to-self with indication bit(s)
  AP send CTS-to-self to reserve TXOP for legacy devices
  11ax devices decode the indication bit(s) to override normal CTS-to-self operation and decode the packet

## Slide 5: Summary
Two methods to enable dynamic 1x/4x OFDM symbol duration are proposed.
Method 1 modifies per-packet PHY preamble and enables dynamic switching between 1x and 4x OFDM symbol duration.
Method 2 enable 4x OFDM symbol duration in NAV protected periods. With 1/4 clock scale down from wider bandwidth mode, it is possible for design reuse.

## Slide 6: Reference
11-14/0801, “envisioning 11ax phy structure part ii”, Dongguk Lim(LG Electronics)
11-14/0804, “Envisioning 11ax phy structure part-I”, Jinsoo Choi (LG Electronics)
11-14/0839, “Discussion on OFDMA in IEEE 802.11ax”, Jinsoo Ahn (Yonsei Univ)
11-14/0855, “Techniques for Short Downlink Frames”, Brian Hart (Cisco Systems)
11-14/0858, “on Frequency Sensitive Multiplexing in WLAN Systems”, Kaushik Josiam (Samsung)
11-13/1057 , “Legacy support on hew frame structure”, Jinyoung Chun(LG Electronics)