## Slide 1: PADP Req/Resp using different SIHes
Date: 2014-9-14
Authors:

## Slide 2: Abstract
Service Identifier Hash(SIH) is introduced in Pre-Association Discovery Protocol(PADP). It is mentioned that multiple SIHes can be derived from a Service ID. But how to use these SIHs in PADP Request and PADP Response is not well explained.
This document propose using different SIHes, instead of same SIH in PADP Request and PADP Response, and the detailed text change can be found in a separate word submission.

## Slide 3
Background
In 11aq draft, same Service Identifier Hash (SIH) is used in PADP Request/response message exchange.
In AQ1.2, it is mentioned that there may be collisions as the SIH is only 6 octets length.
In AQ1.2, it is also mentioned that multiple SIHes can be created from the same Unique Service Identifier.
But it is not clear how to use the multiple SIHes for a Service?And the details of how SIH is being used by STA and AP are not described.

## Slide 4
PADP Request/Response using same SIH
Use same SIH in PADP Request/Response exchange (now in D0.01)
  AP indicates in PADP Capabilities element of using same service hash
  STA sends a PADP Request to AP using SIH1 for a given service
  AP responds with a PADP Response with the same SIH1 to indicate the availability of the service
  When STA receives the PADP Response with SIH1, it decides the requesting service is available in the AP.
STA
AP
Beacon/Probe Response [using same Service Hash]
PADP Request [SIH1]
PADP Response[SIH1]

## Slide 5
PADP Request/Response using different SIHes
Use different SIHes in PADP Request/Response exchange
  AP indicates in PADP Capabilities element of using different service hash
  STA sends a PADP Request to AP using SIHreq for a given service
  AP responds with a PADP Response with SIHrsp indicating the availability of the service (SIHrsp corresponds to SIHreq for the requesting service)
  When STA receives the PADP Response with SIHrsp, it decides that the requesting service is available in the AP
STA
AP
Beacon/Probe Response [using different service hash]
PADP Request [SIHreq]
PADP Response[SIHrsp]

## Slide 6: Different SIHes vs. Same SIH[1]
Multiple SIHes can be formed from the same USID
  USID = first 16 octets of SHA-256(Service Name)
  SIHreq = 1st 6 octets of USID SIHrsp = 2nd 6 octets of USID
Different SIHes vs Same SIH
  Collisions
    Same SIH for req/rsp of 6 octets has 1 in 17 million collisions (2^24)
    Different SIH for req/rsp has 1 in 2.8 E+14,collision probability (2^48) -> much better
  Different SIHes for req/rsp has interesting privacy properties
    More difficult to correlate SIHreq to SIHrsp

## Slide 7
Conclusion
Propose using different SIHes instead of same SIH for a given service in PADP Request/Response

## Slide 8: References
  11-13-0893-00-00aq-service-discovery-proposal.pptx