## Slide 1: Service Identifiers and Bloom Filters
Date: 2014-9-15
Authors:
Based on previous proposals 802.11-12/0706 and 802.11-13/0893
Intended to complement 802.11-14/0877 Generic Service Discovery Proposal: Dynamic Bloom Filter Operation
Sept 2014

## Slide 2: Definitions
Service Name – an octet string created by the developer of the service that provides a unique identification of the service. For unprotected services, the octet string is human readable.
Unique Service Identifier (USID) – the first 128 bits of the SHA-256 hash of an octet string identifying the service (Service Name).
Service Id (SID)– An identifier formed by truncating a Unique Service Identifier (USID). Usually truncated to 6 octets.
6 octets (48 bits) is a convenient size for a Service Id in IEEE 802.11 applications.

## Slide 3: Process to define Service Identifiers
Definition of “foo” Service Name
Definition of “bar” Service Name
Hash Function
Hash Function
“foo” Service Id
“bar” Service Id
Any group can get together and define a service
Each service needs to define an appropriate string (text or octets) to define there service
A cryptographic hash is used to create a unique identifier and may be a truncated version of the full hash
Resulting identifiers are unique and any device that recognizes the identifier will have knowledge of it’s usage

## Slide 4: USID and UUIDs
A USID (Universal Service Identifier) is a type of UUID (Universally Unique Identifier)
UUIDs are:
  16-octet (128-bit) numbers
  Defined by ISO/IEC 11578:1990, X.667, ISO/IEC 9834-9:2005 and RFC 4122
  Note that RFC 4122 uses SHA-1 which is no longer recommended for new applications
USID as defined herein:
  Are 16-octet (128-bit) numbers
  Based on SHA256 hash

## Slide 5: Service Identifiers
Service Identifiers are a ‘short form’ of a USID that provide an efficient representation of a service (e.g. 6 octets)
Service Identifiers are unique enough for discovery, but any secure usage or authentication can readily use the full USID in any integrity of authentication checks.

## Slide 6: Bloom Filters and Service Ids
Bloom filters offer a means to efficiently indicate membership of a large number of items.
  IEEE 11-14/0877r2 “Generic Service Discovery Proposal: Dynamic Bloom Filter Operation”
Bloom filters need ‘k’ hash calculations to map a service into k bits of a vector of length ‘m’ in bits
A USID, SID or any hash based UUID already has created a large ‘strong’ hash to create the indenters
This larger hash can be reused to provide and efficient processing of multiple bloom hash calculations

## Slide 7: Proposed Bloom Hash Calculations
Assuming that USID is formed as:
  USID = SHA256(service_name) or
  USID = SHA256(service_name)[0:16} truncated to 16 octets (128 bits )
  The bloom filter is of length ‘m’ in bits
  ‘k’ hashes are required for the filter
Each bloom hashi (for i 0 to k-1) is calculated as:
  16 bit little-endian Integer value of SHA256(service_name)[2*i:2*(i+1) modulo m
  The above is just the hash taken two bytes at a time mapped (modulo m) into the bit vector as an index of the bit to set.
  The SHA256 value or USID is simply retained for a service and is NOT calculated on each usage

## Slide 8: Example USID, SID and Bloom Hash
Service Name: ‘service.name.example’
SHA256: e3b0c44298fc1c149afbf4c8996fb924 27ae41e4649b934ca495991b7852b855
USID: e3b0c44298fc1c149afbf4c8996fb924
SID: e3b0c44298fc
Bloom Filter Hash Calculation(m=128bits k=3)
H0 -> e3b0 –to int-> 45283 – mod 128 -> 227 H1 -> c442 –to int-> 17092 – mod 128 -> 196 H3 -> 98fc –to int-> 64664 – mod 128 -> 152
Bloom Filter (in hex): 00000008000000100000000001000000 00000000000000000000000000000000