## Slide 1: Multicast Scenarios for MAC Calibration
Date: 9/10/2014
Authors:
Name | Affiliations | Address | Phone | Email
Igor Kim | ETRI | Korea | +82-42-860-5525 | ikim@etri.re.kr
Gwangzeen Ko | ETRI | Korea | +82-42-860-4862 | gogogo@etri.re.kr
Hyunduk Kang | ETRI | Korea | +82-42-860-1074 | henry@etri.re.kr
Myung-Sun Song | ETRI | Korea | +82-42-860-5046 | mssong@etri.re.kr

## Slide 2: Summary
In [1], [2] simulation scenarios and evaluation methods for MAC simulator are described
Video distribution in dense environments could be one of the main use cases in 11ax
Multicasting is known to be one of the most efficient ways to deliver the same multimedia content to multiple users
Scenario 3 (Indoor Small BSSs) of [1] describes multicast scenario
MAC calibration with simple multicast tests is necessary
In this document we propose two simple tests for MAC calibration considering multicasting

## Slide 3: Proposed Test 6. Multicast in Single BSS
Goal
  Verify the operation of multicast frame exchange and control frame overhead is correctly computed
Configuration
  Basic parameters are same as described in [1]
  Topology is derived from Test 1a
  Different multicasts could be considered
    Legacy (No feedback, only MCS0)
    11aa Groupcast with retry (GCR)
      Unsolicited retry (similar to legacy but with N retries)
      Block ACK (BAR/BA exchange)
    11v Directed Multicast Service (DMS)
Output
  Multicast throughput
  Simulation time trace
STA 1
AP1
STA 2
STA 3

## Slide 4: Proposed Test 6. Check Points (1)
Legacy multicasting check points
  CP1, CP2: MPDU1 Tx
  CP2, CP3: RIFS duration
  CP3, CP4: MPDU2 Tx at CP3, CP4
Numerical throughput
  TMPDU – MPDU Tx time
  Tbackoff – average backoff time
  Dsize – application data size (bytes)
  TPUT = Dsize * 8 * 2 / (DIFS + Tbackoff + 2*TMPDU + RIFS)
DIFS
Backoff
MPDU1
MPDU2
RIFS
Checkpoints for Legacy Multicasting
CP1
CP2
CP3
CP4

## Slide 5: Proposed Test 6. Check Points (2)
GCR unsolicited retry multicasting check points
  CP1, CP2: MPDU1 Tx
  CP2, CP3: RIFS duration
  CP3, CP4: MPDU1 re-Tx at CP3, CP4
Numerical throughput
  TMPDU – MPDU Tx time
  Tbackoff – average backoff time
  Dsize – application data size (bytes)
  TPUT = Dsize * 8 / (DIFS + Tbackoff + 2*TMPDU + RIFS)
DIFS
Backoff
MPDU1
MPDU1
RIFS
Checkpoints for unsolicited retry Multicasting
CP1
CP2
CP3
CP4

## Slide 6: Proposed Test 6. Check Points (3)
GCR Block ACK multicasting check points
  CP1, CP2: RIFS duration
  CP2, CP3: BAR1 Tx
  CP3, CP4: SIFS duration
  CP4, CP5: BA1 Tx
  Similarly, verify BAR/BA exchange with other STAs
DIFS
Backoff
MPDU1
MPDU2
RIFS
RIFS
BAR1
SIFS
BA1
SIFS
BAR2
SIFS
BA2
SIFS
BAR3
SIFS
BA3
Checkpoints for GCR Block ACK Multicasting
CP4
CP2
CP3
CP1
CP5
CP6
CP7
CP8
CP9
CP10
CP11
CP12
CP13

## Slide 7: Proposed Test 7: Multicast in Simple OBSS
Goal
  Verify multicasting operation, including frame retransmissions, in simple interference scenario with hidden nodes
Configuration
  Configurations are same as in Test 6
  Topology is derived from Test 2b
Output
  Per-STA multicast throughput
  Simulation time trace
STA 3
AP 2
AP1
STA 6
STA 1
STA 2
STA 5
STA 4

## Slide 8: Proposed Test 7: Check Points
GCR Block ACK multicasting check points
  CP1, CP2: RIFS duration
  CP2, CP3: BAR3 transmission to STA3
  CP3, CP4: SIFS duration
  CP4, CP5: BA3 transmission from STA3
Checkpoints for GCR Block ACK Multicasting
DIFS
Backoff
MPDU1
MPDU2
RIFS
RIFS
BAR3
SIFS
BA3
CP4
CP2
CP3
CP1
CP5
Retransmitted MPDUs

## Slide 9: Conclusion
Proposed two tests for multicasting
  Test 6 for verifying multicasting frame exchange and measure control overhead
  Test 7 for validation of multicasting in simple interference scenario

## Slide 10: Straw Poll
Do you agree to include the proposed tests into the scenarios for MAC simulator calibration?
  Yes
  No
  Abstain

## Slide 11: Reference
[1] 11-14-0980-04-00ax-simulation-scenarios
[2] 11-14-0571-05-00ax-evaluation-methodology