## Slide 1
Shiwen He, Haiming Wang
Preamble Sequence for IEEE 802.11aj (45GHz)
Authors/contributors:
Date: 2014-11-5
Presenter: Haiming Wang

## Slide 2
Shiwen He, Haiming Wang
Slide 2
Common preamble introduction
Preamble is the beginning part of a PPDU—used for packet detection, AGC, frequency/timing synchronizations and channel estimation.
The SC and OFDM systems for both 540MHz and 1080MHz bandwidth share a common preamble:
  Better support of the coexistence between various types of devices.
  Each device, especially Dual-Mode device (the device which supports SC mode and OFDM mode), needs to achieve packet detection/ synchronization/channel estimation for SIG mechanism only once .
  Appropriate re-sampling mechanism is required.
    Given that OFDM and SC Data portions use different sampling rates.
Notes: 2

## Slide 3
Shiwen He, Haiming Wang
Slide 3
Common preamble requirements
Low peak side lobe of periodic auto-correlation and low maximum value of periodic cross-correlation.
  to accurate the timing synchronization
Large zero correlation zone of periodic auto-correlation and periodic cross-correlation.
  11aj maximum multipath delay spread: 100ns
  The time of zero correlation zone should be larger than 100ns to eliminate interference of multipath delay.
The elements of preamble sequence should belong to finite collection of symbols, and low-complexity periodic correlator is needed.
  to simplify transmitter/receiver processing and reduce the power consumption
Preamble sequence set should contain several sequences.
  to implement the MIMO technology
Notes: 3

## Slide 4
Shiwen He, Haiming Wang
Slide 4
Definition of ZCZ sequence set
The sequence set is called Zero Correlation Zone (ZCZ) sequence set when the following formula is satisfied:
where, denotes the periodic correlation between and , denotes the energy of the sequence, denotes the ZCZ length, denotes the number of ZCZ sequences.
Notes: 4

## Slide 5
Shiwen He, Haiming Wang
Slide 5
Proposed Generator for ZCZ sequence set
The initial mutually orthogonal aperiodic sequence sets:
The iteration method:
where denotes the length of the column vector ,
and denotes identity matrix and zero matrix of the size ,
, denotes the diagonal matrix with diagonal element , is element of the Discrete Fourier Transform (DFT) matrix, is element of the coefficient matrix, denotes all 1 column vector, denotes Kronecker product.
Notes: 5

## Slide 6
Shiwen He, Haiming Wang
Slide 6
Properties of ZCZ sequence set
ZCZ sequence set :
  denotes the length of ZCZ sequence, denotes the number of ZCZ sequence, denotes zero correlation zone of ZCZ sequence.
The large length of periodic zero correlation zone:
  The coefficient matrix is variable.
  Changing the coefficient matrix to search optimized ZCZ sequence set with low PSL and CL.
The elements of ZCZ sequence set belong to the finite alphabet set.
Notes: 6

## Slide 7
Shiwen He, Haiming Wang
Slide 7
Example of ZCZ sequence set
A kind of is designed to be 802.11aj preamble sequence .
The peak side lobe of normalized periodic auto-correlation is 0.1976 and the maximum value of normalized periodic cross-correlation is 0.3125.
  enhance the robustness of time synchronization
The length of zero correlation zone is 56.
  the time of zero correlation zone:
  eliminate interference of multipath delay
Quadriphase sequences:
  simplify receiver processing
The generation parameters of and are detailed in annex.
Notes: 7

## Slide 8
Shiwen He, Haiming Wang
Slide 8
Common preamble frame format
Q-band training field (QTF) is composed of 14 repetitions of ZCZ sequences which are denoted as .
  Chip-level π/2-QPSK modulation.
  The antenna transmits QTF .
  Using 14 repetitions of is a good tradeoff between PPDU efficiency, preamble detection/synchronization sensitivity and channel estimation accuracy.
    Preamble det/sync SNR sensitivity matches those for decoding Payload with MCS0
Notes: 8

## Slide 9
Shiwen He, Haiming Wang
Slide 9
Packet detection algorithm
Delay correlation algorithm:
where denotes receiving QTF, denotes the length of ZCZ sequence, denotes
delay correlation of QTF , denotes energy of ZCZ sequence, denotes decision
value.
  If is greater than the certain threshold, and lasts for a certain period, then the packet is detected.
  3 repetitions of ZCZ sequence are used for packet detection and AGC convergence.
Notes: 9

## Slide 10
Shiwen He, Haiming Wang
Slide 10
Frequency synchronization algorithm
Frequency synchronization algorithm:
where denotes receiving QTF without frequency offset, denotes the sampling interval, denotes frequency offset, denotes the angle of .
  The simulation shows that 6 repetitions of ZCZ sequence are a good tradeoff between PPDU efficiency and frequency synchronization sensitivity.
Notes: 10

## Slide 11
Shiwen He, Haiming Wang
Slide 11
Timing synchronization algorithm
Local correlation algorithm:
where denotes local ZCZ sequence element, denotes timing synchronization position.
  Timing synchronization is performed coherently with channel estimation.
Notes: 11

## Slide 12
Shiwen He, Haiming Wang
Slide 12
Channel estimation algorithm
Linear least square (LS) estimation algorithm
where denotes time domain channel with 56 multipath, is a column vector which denotes the local ZCZ sequence, denotes chips circular shift of , denotes the receiving sequences with chips.
  The simulation shows that 5 repetitions of ZCZ sequence are a good tradeoff between PPDU efficiency and channel estimation sensitivity.
Notes: 12

## Slide 13
Shiwen He, Haiming Wang
Slide 13
Conclusion
ZCZ sequence set and its fast periodic correlator are applied in preamble to simplify receiver processing.
A common preamble is proposed for different PHY modes.
  SC and OFDM MCSs share the same preamble structure.
Notes: 13

## Slide 14
Shiwen He, Haiming Wang
Slide 14
Annex
1. Generator of ZCZ sequence set
2. Generation parameters of
3. Generation parameters of
4. Simulation of correlation
5. Simulation of packet detection
6. Simulation of frequency offset estimation
7. Simulation of channel estimation
Notes: 14

## Slide 15
Shiwen He, Haiming Wang
Slide 15
Generator of ZCZ sequence set
Notes: 15

## Slide 16
Shiwen He, Haiming Wang
Slide 16
Generation parameters of .
Finite collection of symbols:
Initial mutually orthogonal aperiodic sequence sets:
DFT matrix:
Coefficient matrix:
Notes: 16

## Slide 17
Shiwen He, Haiming Wang
Slide 17
Generation parameters of .
Finite collection of symbols:
Initial mutually orthogonal aperiodic sequence sets:
DFT matrix:
Coefficient matrix:
Notes: 17

## Slide 18
Shiwen He, Haiming Wang
Slide 18
Correlation of .
Notes: 18

## Slide 19
Shiwen He, Haiming Wang
Slide 19
Packet detection (1)
It is shown that threshold 0.2 is a better choice to satisfy the demand of packet detection sensitivity.
Notes: 19

## Slide 20
Shiwen He, Haiming Wang
Slide 20
Packet detection (2)
It is shown that threshold 0.2 is a better choice to satisfy the demand of packet detection sensitivity.
Notes: 20

## Slide 21
Shiwen He, Haiming Wang
Slide 21
Packet detection (3)
It is shown that threshold 0.2 is a better choice to satisfy the demand of packet detection sensitivity.
Notes: 21

## Slide 22
Shiwen He, Haiming Wang
Slide 22
Frequency offset estimation
It is shown that 6 repetitions of ZCZ sequence satisfy the demand of frequency synchronization sensitivity.
F denotes the number of frames in simulation, denotes real frequency offset, denotes estimated frequency offset.
Notes: 22

## Slide 23
Shiwen He, Haiming Wang
Slide 23
Channel estimation
It is shown that 5 repetitions of ZCZ sequence satisfy the demand of channel estimation sensitivity.
Notes: 23

## Slide 24
Shiwen He, Haiming Wang
Slide 24
Thanks for Your Attention.
Notes: 24