## Slide 1
CSI Feedback for MIMO-OFDM Transmission in IEEE 802.11aj (45 GHz)
Authors/contributors:
Date: 2014-11-5
Presenter: Haiming Wang

## Slide 2
Abstract
This presentation proposes CSI feedback schemes for transmit beamforming in IEEE 802.11aj (45 GHz).

## Slide 3
Introduction (1/2)
Beamforming can improve the performance of system, including
  Enhance throughput in IEEE 802.11n/ac
  Quasi-ML detection performance can be achieved with a low-complexity receiving structure.
  Expand coverage in IEEE 802.11ad
  By focusing transmitting power on a specific direction, signals can be transmitted to a longer distance.
Compressed beamforming matrix feedback based on Givens Rotation has been used in IEEE 802.11n/ac, due to
  Reduced feedback overhead
  Low complexity

## Slide 4
Introduction (2/2)
The number of bits used for angle quantization in IEEE 802.11n and IEEE 802.11ac
  802.11n supports (3,1), (4,2), (5,3) or (6,4) bits to quantize angle (ϕ, ψ).
  802.11ac supports (4,2) or (6,4) bits to quantize angle (ϕ, ψ) for single user, and (7,5) or (9,7) bits to quantize angle (ϕ, ψ) for multi-user.
Subcarrier grouping has been applied in IEEE 802.11n and IEEE 802.11ac to further reduce feedback amount
  11n and 11ac both support to combine 2 or 4 subcarriers into one group.
  Appropriate interpolation method is needed to reconstruct beamforming matrices.

## Slide 5
Feedback scheme
Explicit feedback is proposed for beamforming to 802.11aj (45 GHz), including
  CSI feedback
    Channel matrix H
  Noncompressed Beamforming Matrix feedback
    Right singular matrix of H
  Compressed Beamforming Matrix feedback
    Compressed right singular matrix of H

## Slide 6
Angle Quantization
For compressed beamforming matrix feedback based on Givens Rotation , angles ψ and ϕ are quantized as
where and are the number of bits used to quantize ψ and ϕ respectively.
  After quantization, angle ϕ is quantized between 0 and 2π, angle ψ is quantized between 0 and π/2.
  is more than by 2 bits.

## Slide 7
Subcarrier Grouping
For subcarrier grouping, the group size should satisfy
where is subcarrier frequency spacing, is the coherent bandwidth of the channel.
  The RMS delay spread of 802.11aj (45 GHz) channel is 10 ns, and
  , , .
  Since the number of effective subcarriers is 176/352, which is even, so optional set is {2, 4, 6}.

## Slide 8
Frame Format of NDP
Propose to use the same NDP sounding mechanism as 11ac, and the NDP format is shown as follows.
  QTF is composed of 14 ZCZ sequences
  MCTF is used to estimate channel, and N depends on the dimension of channel matrices to be estimated.

## Slide 9
Frame Format of NDP
QMG NDP Announcement frame format
Feedback Type | Set to 0 for SU; Set to 1 for MU.
Nc Index | If the Feedback Type field indicate MU, then Nc Index indicates the number of columns Nc of feedback matrix: Set to 0 \1\2\3 to request Nc = 1\2\3\4 Reserved if the Feedback Type field indicates SU.

## Slide 10: Frame Format of MIMO Control
QMG CSI/Beamforming frame format
QMG MIMO Control field
Order | Information
1 | Category
2 | QMG Action
3 | QMG MIMO Control
4 | QMG CSI/Beamforming Report
5 | MU Exclusive Noncompressed /Compressed Beamforming Report
  The Category field is set to 22 for QMG Action
The QMG Action field is set to 0 for QMG CSI, set to 1 for QMG Noncompressed Beamforming, set to 2 for QMG Compressed Beamforming.
The MU Exclusive Noncompressed/Compressed Beamforming Report present when the Feedback Type is MU.

## Slide 11: Description of MIMO Control Field
QMG MIMO Control field description
Nc Index | Indicates the number of columns of V matrix: Set to 0\1\2\3 for Nc=1\2\3\4
Nr Index | Indicates the number of rows of V matrix: Set to 0\1\2\3 for Nr=1\2\3\4
Channel Width | Indicates the channel width: Set to 0\1 for 540\1080 MHz
Grouping | Indicates the number of carriers grouped into one: Set to 0\1\2\3 for Ng=1\2\4\6
Codebook Information | Indicates the number of bits in the representation of the real and imaginary parts of each element in the matrix for QMG CSI feedback and QMG Noncompressed Beamforming feedback, or indicates the size of codebook entries for Compressed Beamforming feedback： For CSI feedback: Set to 0\1\2\3 for Nb = 4\5\6\8 For Noncompressed Beamforming feedback: Set 0\1\2\3 for Nb = 4\3\6\8 For compressed Beamforming feedback: If Feedback Type is SU: If Feedback Type is MU: Set to 0 for 2 bits for ψ, 4 bits for ϕ Set to 0 for 5 bits for ψ, 7 bits for ϕ Set to 1 for 3 bits for ψ, 5 bits for ϕ Set to 1 for 7 bits for ψ, 9 bits for ϕ

## Slide 12: Simulation Settings
Channel model: 802.11aj (45 GHz) channel
Number of distinguishable paths: 25
Maximum/RMS delay spread: 100 ns/10 ns
Channel bandwidth: 540 MHz
Packet length: 4096 bytes
Number of channel realizations: 3000
Simulation antennas: 2×1, 4×1 for 1ss, 3×2, 4×2, 4×4 for 2ss, 4×3 for 3ss.
Modulation and code rate: {QPSK ½},{64QAM ⅝}
Single user, LS channel estimation, without STBC.
Actual channel estimation for receiving sounding NDP is added.
Linear spherical interpolation is applied for subcarrier grouping, and use 7 bits to quantize ϕ, 5 bits to quantize ψ.

## Slide 13: Simulation Results
For Givens Rotation based angle quantization, simulation show that
  Using 5 bits to quantize ϕ, 3 bits to quantize ψ could achieve the performance of perfect beamforming matrix.
  Using 4 bits to quantize ϕ, 2 bits to quantize ψ could also achieve the performance close to perfect beamforming matrix, with performance loss less than 0.4 dB.
For subcarrier grouping, simulations show that
  For , the maximum performance loss is 1.8 dB
  For , the maximum performance loss is 2 dB
  For , the maximum performance loss is 2.5 dB
  For , the maximum performance loss is 3.4 dB

## Slide 14: Conclusions
Two type of angle quantization are proposed to IEEE 802.11aj (45 GHz) , including
  4 bits to quantize ϕ, 2 bits to quantize ψ .
  5 bits to quantize ϕ, 3 bits to quantize ψ .
Optional group size set {1, 2, 4, 6} is proposed for subcarrier grouping in IEEE 802.11aj (45 GHz).

## Slide 15
Reference
[1] “11-10-0332-00-00ac-csi-report-for-explicit-feedback-beamforming-in-downlink-mu-mimo”, Koichi Ishihara et al.
[2] “11-10-0806-01-00ac-csi-feedback-scheme-using-dct-for-explicit-beamforming”, Koichi Ishihara et al.
[3] “11-11-1539-00-00ah-beamforming-for-11ah”,Minho Cheong et al.
[4]“11-05-1645-02-000n-preambles-beamforming-wwise-proposal”,Christopher J. Hansen et al.
[5]"11-07-0612-02-000n-comment-resolution-csi-uncompressed-steering-matrix-feedback-bitwidth-nb",Hongyuan Zhang et al.
[6]"11-10-0586-01-00ac-time-domain-csi-report-for-explicit-feedback ", Laurent Cariou et al.
[7]"11-10-1131-00-00ac-time-domain-csi-compression-schemes-for-explicit-beamforming-in-mu-mimo",Koichi Ishihara et al.
[8]"Draft P802.11REVmc_D1.5"
[9]"Draft-802.11ac_D5.1"

## Slide 16
APPENDIX A:
Simulation Results for Angle Quantization

## Slide 17
can achieve performance
close to unquantized angles, with 0.1 dB performance loss.

## Slide 18
can achieve performance
close to unquantized angles, with 0.1 dB performance loss.

## Slide 19
can achieve performance
close to unquantized angles, with 0.1 dB performance loss.

## Slide 20
can achieve performance
close to unquantized angles, with 0.2 dB performance loss.

## Slide 21
can achieve performance
close to unquantized angles, with 0.1 dB performance loss.

## Slide 22
can achieve performance
close to unquantized angles, with 0.2 dB performance loss.

## Slide 23
can achieve performance
close to unquantized angles, with 0.1 dB performance loss.

## Slide 24
can achieve performance
close to unquantized angles, with 0.1 dB performance loss.

## Slide 25
can achieve performance
close to unquantized angles, with 0.1 dB performance loss.

## Slide 26
can achieve performance
close to unquantized angles, with 0.4 dB performance loss.

## Slide 27
APPENDIX B:
Simulation Results for Subcarrier Grouping

## Slide 28
Performance loss:
Ng=2, 0.15 dB
Ng=4, 0.2 dB
Ng=6, 0.4 dB
Ng=8, 0.8 dB

## Slide 29
Performance loss:
Ng=2, 0.2 dB
Ng=4, 0.3 dB
Ng=6, 0.5 dB
Ng=8, 0.9 dB

## Slide 30
Performance loss:
Ng=2, 0.2 dB
Ng=4, 0.3 dB
Ng=6, 0.5 dB
Ng=8, 1 dB

## Slide 31
Performance loss:
Ng=2, 0.2 dB
Ng=4, 0.2 dB
Ng=6, 0.5 dB
Ng=8, 1 dB

## Slide 32
Performance loss:
Ng=2, 0.2dB
Ng=4, 0.3 dB
Ng=6, 0.6 dB
Ng=8, 0.8 dB

## Slide 33
Performance loss:
Ng=2, 0.3 dB
Ng=4, 0.7 dB
Ng=6, 1.3 dB
Ng=8, 2 dB

## Slide 34
Performance loss:
Ng=2, 0.2 dB
Ng=4, 0.3 dB
Ng=6, 0.6 dB
Ng=8, 1 dB

## Slide 35
Performance loss:
Ng=2, 0.5 dB
Ng=4, 0.8 dB
Ng=6, 1.4 dB
Ng=8, 2.1 dB

## Slide 36
Performance loss:
Ng=2, 0.5 dB
Ng=4, 0.55 dB
Ng=6, 0.7 dB
Ng=8, 0.9 dB

## Slide 37
Performance loss:
Ng=2, 1 dB
Ng=4, 1.2 dB
Ng=6, 1.3 dB
Ng=8, 1.5 dB

## Slide 38
Performance loss:
Ng=2, 0.6 dB
Ng=4, 0.8 dB
Ng=6, 1 dB
Ng=8, 1.3 dB

## Slide 39
Performance loss:
Ng=2, 1.8 dB
Ng=4, 2 dB
Ng=6, 2.5 dB
Ng=8, 3.4 dB

## Slide 40
Thanks for Your Attention!