## Slide 1: DSC and legacy coexistence
Date: 2014-11-03
Authors:

## Slide 2: Abstract
For scenario S2 (Enterprise) we have studied the situation of legacy STAs coexisting with 802.11ax STAs that use increased CCA Threshold
  We found no significant impact on the legacy STAs

## Slide 3: Background
[2] indicates negative impact on legacy STAs from DSC STAs
  Full buffer traffic model used in Uplink in [2]
  STAs either in back-off or transmitting state
  Legacy STAs seldom discover idle wireless medium (WM)
WM less occupied with file transfer traffic model
  DSC STA do not monopolize WM usage
Mix of Uplink and Downlink file transfers used in this study
  Intended to closer resemble realistic traffic

## Slide 4: Simulation setup
Scenario 2 (Enterprise) from [1]
50% Uplink & 50% Downlink traffic
  Equal buffer (file transfer with varied intensity), file size 1 MB
  Served traffic per AP (x-axis in plots) is sum of Uplink & Downlink traffic
CWmin = 15, CWmax = 1023
STAs are
  50% Legacy with CCAT = -82 dBm
  50% 802.11ax with CCAT = -62 dBm
All APs implement 802.11ax
  All Downlink transmissions use CCAT = -62 dBm, regardless if receiver is legacy or 802.11ax
Preamble detection threshold = CCAT
Energy detection threshold = max(CCAT,-62) dBm

## Slide 5: Performance
Legacy STAs plotted with dashed red curve, 802.11ax STAs with solid red curve
In uplink, both legacy and 802.11ax STAs improve on average and in 5th percentile user throughput
In downlink, there is also improvement in 5th percentile and average throughput, 802.11ax have larger average user throughput gain
Downlink
Uplink

## Slide 6: Coexistence Scenario 2 - Downlink
CCAT -62dBm users do get reduced SINR, but for 90% of the users the delay per packet is also reduced
Legacy user’s SINR is less impacted, but they also see a reduction in packet delay

## Slide 7: Summary
Increasing the CCA threshold from -82 to -62 provides about 20-25% gain in average and 5th percentile user throughputs
Improved performance is also observed for the legacy STAs in a file transfer scenario

## Slide 8: References
[1] IEEE 802.11-14/0980r04 – Simulation Scenarios
[2] IEEE 802.11-14/0854r0 – DSC and legacy coexistence
[3] IEEE 802.11-14/0866r1 - Traffic modeling and system capacity performance measure