## Slide 1: DSC Performance
Date: 2014-11-03
Authors:

## Slide 2: Abstract
We present a study on the effect of modifying the CCA threshold (CCAT)
  Considering simulation scenarios 1-4 (S1 – S4)
Different algorithms are also evaluated in the Enterprise scenario, S2
  Throughput gains in the order of 25% are observed

## Slide 3: Background
Previously there have been several contributions presenting results from studies on the gains and effects of employing Dynamic Sensitivity Control (i.e., increasing the CCA threshold)
Achievable gains are shown to vary from high [1], [2]; through medium [3], [4]; to low [5]
Results depend on the scenario, the DSC algorithm and other factors

## Slide 4: Simulation setup - CCAT sweep
Scenarios 1 to 4 from [6]
50% Uplink (UL) & 50% Downlink (DL) traffic
  Equal buffer (file transfer with varied intensity), file size 1 MB
  Served traffic (x-axis in plots) is sum of served UL & DL traffic per AP
CWmin = 15, CWmax = 1023
Preamble detection (CCAT) varied from -82 to -52
Energy detection threshold = max(CCAT,-62) dBm

## Slide 5: CCAT sweep example - Scenario 2
Mean plotted w/o marker, 5th perc. plotted w/ marker
Significant gains in average user throughput for both DL & UL
Gains in DL 5th percentile, and in UL 5th percentile for -62dBm
Downlink
Uplink

## Slide 6: Throughput gains from increased CCAT
Evaluated in Scenarios 1-4
Traffic load point chosen for each scenario as a stable, but high-load point (i.e., approaching full buffer)
50% Uplink (UL) & 50% Downlink (DL) traffic
  Equal buffer (file transfer with varied intensity), file size 1 MB
CWmin = 15, CWmax = 1023
Preamble detection (CCAT) varied from -82 to -52
Energy detection threshold = max(CCAT,-62) dBm
Mean and 5th percentile user throughput compared

## Slide 7: Relative throughput gain Scenario 1 – 80 Mbps/AP UL & DL traffic
Downlink Uplink

## Slide 8: Relative throughput gain Scenario 2 – 100 Mbps/AP UL & DL traffic
Downlink Uplink

## Slide 9: Relative throughput gain Scenario 3 – 50 Mbps/AP UL & DL traffic
Downlink Uplink

## Slide 10: Relative throughput gain Scenario 4 – 10 Mbps/AP UL & DL traffic
Downlink Uplink

## Slide 11: Dynamic Sensitivity Control (DSC)
The next step from just changing the global CCAT is to base the DSC on the RSSI
After that the next complexity level could be to base the DSC on the SINR, here estimated through the MCS

## Slide 12: DSC principle (UL)
Increased threshold limits the number of OBSS interferers
Average number of BSS interferers
Scenario 2

## Slide 13: Simulation setup - RSS based DSC
Scenario 2 (Enterprise) from [6]
50% Uplink (UL) & 50% Downlink (DL) traffic
  Equal buffer (file transfer with varied intensity), file size 1 MB
  Served traffic (x-axis in plots) is sum of served UL & DL traffic per AP
CWmin = 15, CWmax = 1023
UL: for each STAn, CCATn = RSSn – Margin
  RSSn = Received Signal Strength for node n from serving AP [dBm]
DL: use CCATn when transmitting to STA n
Energy detection threshold = max(CCATn,-62) dBm

## Slide 14: RSSI based DSC - Scenario 2
Mean plotted w/o marker, 5th perc. plotted w/ marker
Significant gains in average user throughput for both DL & UL
Gains in UL 5th percentile, no impact on DL 5th percentile
Downlink
Uplink

## Slide 15: LA based DSC
An attempt to also capture some knowledge of the interference situation at the receiver side through the MCS index given by the link adaptation (LA)
UL: for STA n:
UL_CCATn = -82 + STEP * MCSn / MCSMax
  STEP = 30 or [40 dBm]
  MCSn = latest used MCS by STA n for UL transmission
  MCSMax = 17 (for 802.11ac)
DL: for transmission to STA k: DL_CCATk = -82 + STEP * MCSk / MCSMax
  STEP = 30 or [40 dBm]
  MCSk = latest used MCS by the AP for DL transmission to STA k
  MCSMax = 17 (for 802.11ac)

## Slide 16: Simulation setup - LA based DSC
Scenario 2 (Enterprise) from [6]
50% Uplink (UL) & 50% Downlink (DL) traffic
  Equal buffer (file transfer with varied intensity), file size 1 MB
  Served traffic (x-axis in plots) is sum of served UL & DL traffic per AP
CWmin = 15, CWmax = 1023
CCAT updated with MCS from Minstrel link adaptation algorithm according to previous slide
Energy detection threshold = max(CCATn,-62) dBm

## Slide 17: LA based DSC - Scenario 2
Mean plotted w/o marker, 5th perc. plotted w/ marker
Significant gains in average user throughput for both DL & UL
Significant gains in DL 5th percentile, some gains in UL 5th percentile
Downlink
Uplink

## Slide 18: Comparison of algorithms
Mean plotted w/o marker, 5th perc. plotted w/ marker
Similar performance for all algorithms
Downlink
Uplink

## Slide 19: User throughput comparison Scenario 2 – 100 Mbps DL & UL traffic per AP
Chart: 
| Mean | 5th percentile
Legacy | 315 | 195
CCAT -62dBm | 380 | 240
DSC 10dB margin | 380 | 235
LA -52dBm | 390 | 240
Downlink
Mbps

## Slide 20: User throughput comparison Scenario 2 – 100 Mbps DL & UL traffic per AP
Chart: 
| Mean | 5th percentile
Legacy | 320 | 180
CCAT -62dBm | 370 | 210
DSC 10dB margin | 370 | 205
LA -52dBm | 370 | 205
Uplink
Mbps

## Slide 21: Summary
Increasing the CCA threshold provides throughput gains in the order of 20-40% (depending on the load levels) in all simulation scenarios except for S4
For S2 no significant gains can be seen from using more advanced DSC algorithms
For S2 the achievable gains are in the order of 25%

## Slide 22: References
[1] IEEE 802.11-14/082r0 - Improved Spatial Reuse Feasibility - Part I
[2] IEEE 802.11-14/083r0 - Improved Spatial Reuse Feasibility - Part II
[3] IEEE 802.11-14/846r1 - CCA Study in Residential Scenario
[4] IEEE 802.11-14/861r0 - Impact of CCA adaptation on spatial reuse in dense residential scenario
[5] IEEE 802.11-14/578r0 - Residential Scenario CCA/TPC Simulation Discussion
[6] IEEE 802.11-14/0980r04 – Simulation Scenarios