## Slide 1: Clear Channel Assessment for OFDMA PHY
Date: 2014-11-01
Authors:

## Slide 2
Outline
Challenges on CCA in Single User PHY
Challenges on CCA in OFDMA PHY

## Slide 3: Challenges on CCA in Single User PHY
Single user PHY
  Single carrier transmission
  Multicarrier transmission but a single use occupying all sub-carriers
  CDMA multiuser communication to achieve high data rate at low error rate degenerates to FDMA with different spreading codes
Energy/Power detection is not reliable under spectrum sharing among heterogeneous systems

## Slide 4: Unreliable Energy Sensing
Transmitter
Receiver
Transmission can
be actually successful!
Little interference
Strong interference
to disable CCA
Receiver
Transmitter
Strong interference
to reception
CCA is clear but
transmission actually
can not be successful!

## Slide 5: Clear Channel Assessment
RSSI pin out from RF to baseband processor (no need for single chip)
  To indicate sensed energy/power inside the band
  Easy and quick to get but NOT reliable
Whether CCA can be clear must depend on the carrier locking and/or timing locking, or even estimated error rate
  That is, the entire packet has been decoded.

## Slide 6: Network Topology Not Equivalent to Sensing Topology
Hidden terminal problem
  Sensing topology is different from network topology
Transmitter senses the existence of transmission is NOT reliable
  Receiver may observe in a different way from transmitter
Access
Point
Station B
Station C
Station A
Station D
Sensing Link
Communication
Link

## Slide 7: OFDMA PHY
OFDMA is a multiuser PHY
  Carrier locking does not imply that transmissions are not allowed.
    As shown in the figure, purple radio blocks being used suggests that energy detection is on and carrier locking is on, but the transmission can still use yellow, or green radio blocks.
No. of OFDM Symbols
No. of Sub-Carriers

## Slide 8: What Was Random Access?
Random access consists of carrier sensing and collision resolution
  Therefore, it is a concept associated with physical channel(s)
    IEEE 802.11 is actually FDMA
  Both carrier sensing and collision resolution can be treated as the tree structure
OFDMA further divides a physical channel into logic channels (i.e. groups of radio blocks)

## Slide 9: Challenges on CCA in OFDMA PHY
Major Challenge: Sensing busy but may have radio blocks (logic channels) available
  Can sensing bring in availability of radio blocks? NO!
  As shown in the figure, if user j is utilizing some RBs at the grey carrier frequency, user k is possible to utilize other portion of RBs at the same grey carrier frequency, though the CCA is negative to prohibit using this carrier frequency as CSMA/CA operation.

## Slide 10
Summary
CCA and CSMA/CA might face new challenges if OFDMA PHY is adopted. Reliable CCA to deploy CSMA/CA in WLANs is still an open problem.