## Slide 1: Simulation Setting of Box5 Calibration
Date: 2014-11-03
Authors:

## Slide 2: Abstract
Box5 calibration parameters used by several interested companies are listed for reference.
Different realizations of certain MAC/PHY details among individual simulators are introduced for further .

## Slide 3: Current Calibration Progress
5 calibration Boxes are shown in the following flow chart [1].
Both Box1 long-term and Box2 short-term SINRs were calibrated in [2].
Box0 PHY abstraction result was provided in [3, 4].
Simple and basic Box3 MAC calibration was done in [5].
Box5 is being calibrated among several interested companies [6-8].
In the rest slides, we will provide reference scenario and parameters for joint calibration.

## Slide 4: Box5 Calibration Scenario
Definitely the 4 typical 11ax scenarios described in [9] are the targeted calibration scenarios.
But directly calibrating these scenarios will be very complicated and time consuming.
It is better to start the calibration from a simple scenario and 11ac SS6 – OBSS Enterprise is a good choice [10].
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association

## Slide 5: 11ac SS6 Traffic Flow Configuration
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow
DL/UL traffic assigned for each STA [10]

## Slide 6: PHY Reference Parameters
PHY parameters | 
BW | All BSSs at [5GHz , 80 MHz]
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 dB standard deviation) per link
Preamble Type | [5GHz, 11ac], duration should be considered
STA TX Power | 15 dBm per antenna with -2dBi antenna gain
AP TX Power | 20 dBm per antenna with 0dBi antenna gain
AP number of TX/RX antennas | 1/1
STA number of TX /RX antennas | 1/1
Noise Figure | 7dB
CCA threshold | -70dBm
Rx sensitivity | -82dBm (a packet with lower rx power is dropped)
Link Adaption | Fixed MCS =7
Channel estimation | Ideal
PHY abstraction | PER computed per MPDU subframe assuming RBIR and BCC [4]
Channel correlation | Same as defined in the used channel model
* Parameters will be updated and enhanced as calibration progresses

## Slide 7: MAC Reference Parameters
[
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023]
Queue length | 2000 packets length multiplied by the STA number inside AP; 2000 packets length inside STA
Traffic type | UDP CBR with rate 10^8bps
MPDU size | 1540 Bytes (1472 Data + 28 IP header + 40 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU with immediate BA], Max aggregation: 64 MPDUs with 4-byte MPDU delimiter (no pad)
Max number of retries | 10
Beacon | Disabled
RTS/CTS | Simple ON/OFF independent of packet length
Traffic direction | UL Only, DL only, Mixed DL & UL
Throughput metric | CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time)
* Iterns will be updated and enhanced as calibration progresses

## Slide 8: Potential Simulator Differences
There may be still some possible realization differences in individual simulators in the following aspects which depend on how accurate the simulator we need it be
  PHY Abstraction under asynchronous interference
  Preamble model and detection scheme
  CCA status with or without BSS color
  Detection of control frames such as RTS/CTS/ACK
  Initialization of traffic start time and contention window
  Channel estimation and link adaptation
  etc.
We will introduce these issues in the following slides so that we can discuss how to align individual simulator to speed up the calibration progress.

## Slide 9: PHY Abstraction
It is agreed that each MPDU data subframe uses PHY abstraction separately to determine a pass or fail.
There are three choices to do the PHY abstraction [11]
  Whole packet average [1]
    works well under the assumption of time-constant interference
    may discount strong interference given a short interleaver for BCC
  Weakest link
    may overestimate strong (but short) interference
  Block-wise PHY abstraction
    balance between the two method above
    more accurate under asynchronous interference [12]

## Slide 10: Preamble Detection
Do we need to model each part in the preamble explicitly?
  No, just consider the whole preamble as one special small packet
  Yes, deal with SFT, LTF, SIG individually
    Different detection metrics may be used for each part
How to decide the preamble passes or fails?
  Rx power threshold (large-scale fading)
    Any preamble with rx power higher than a predefined threshold is always correctly detected
    Interference is not considered during the preamble phase
  SINR threshold based on MCS0 (large-scale fading)
    Any preamble with rx SINR higher than the threshold is always correctly detected
  PER dependent (small-scale fading)
    PHY abstraction is required

## Slide 11: CCA Status [13-16]
If BSS color is not considered
  Any packet with rx power lower than CCA threshold is not protected, i.e., CCA is idle and no need to do preamble detection;
  CCA is busy when the rx power is higher than the CCA threshold and then the preamble is detected
    If passed,
      the destination STA should continue to decode the data subframes and later-arrived packets are considered as interference (receiver locked)
      non-destination STA defers for the entire transmission duration
    If failed,
      STA switches to receive other packets (receiver unlocked)
      STA could contention to transmit based on latest CCA result
If BSS color is applied
  MYBSS packet with rx power higher than rx sensitivity but lower than CCA threshold is protected after correctly detection
  Others are the same as in no BSS color case.

## Slide 12: Control Frame Detection
How to decide RTS/CTS/ACK reception is pass or fail?
  SINR threshold
    Pass if SINR higher than the threshold
    Fail, otherwise
  PER dependent
    PHY abstraction is also applied on control frames under corresponding MCS

## Slide 13: Traffic Initialization
It is suggested to randomize the start time of each traffic link to avoid collision storm at the beginning of the simulation, otherwise,
  certain training phase is required and longer simulation time is required

## Slide 14: Link Adaptation
One closed loop LA method could be described as below
  Compute per-tone SINR for each stream
  Compute average RBIR value per tone per stream for each modulation scheme
  Get effective SNR for each modulation scheme
  Obtain PER for each MCS
  Estimate link_rate[MCS] = Num_stream * SISO_rate[MCS] * (1-PER[MCS])
  Find MCS* = max (link_rate[MCS])
One open loop LA method could be applied based on ACK/NACK feedback
Channel estimation error model is TBD and will not be introduced at start.

## Slide 15: Summary
We defined detail simulation setting as reference for Box5 calibration among companies.
We pointed out possible differences in individual simulator realizations to facilitate the calibration progress.
We plan to decide one baseline metric for each different realization and then share individual results for calibration.

## Slide 16: Reference
[1] 11-14/0571r5 Evaluation Methodology
[2] 11-14/0800r24 Box 1 and Box 2 Calibration Results
[3] 11-14/0873r5 Discussion on PHY Abstraction for 11ax System Level Simulation
[4] 11-14/1176r0 PHY Abstraction Tables for 11ax System Level Simulation
[5] 11-14/1192r3 Comparing Mac Calibration Results
[6] 11-14/1177r3 Updated Results of Box5 Calibration
[7] 11-14/1392r0 Simulation results for Box 5 calibration
[8] 11-14/1419r0 SLS Box5 Calibration Results and Discussions
[9] 11-14/0980r4 Simulation Scenarios
[10] 11-09/0451r16 TGac Functional Requirements and Evaluation Methodology
[11] 11-14/1174r0 PHY Abstraction with Time Varying Interference
[12] 11-14/1148r1 Consideration of Asynchronous Interference in OBSS Environment
[13] 11-14/0847r1 Further Considerations on Enhanced CCA for 11ax
[14] 11-14/0861r0 Impact of CCA Adaptation on Spatial Reuse in Dense Residential Scenario
[15] 11-14/0372r2 System Level Simulations on Increased Spatial Reuse
[16] 11-14/1233r2 Adaptive CCA for 11ax