## Slide 1: Considerations on DL OFDMA control mechanism
Date: 2014-11-03
Authors:

## Slide 2: DL-UL asymmetry and DL OFDMA
DL-UL asymmetry
  Overall network performance degradation
  Same prioritized contention of AP
    Same opportunity for accessing medium: 1/(N+1)[1]
  The starvation of AP gets severer as network gets denser
DL OFDMA
  AP could deal with multiple STAs data at the same time
    Transmitting K STAs data -> mean contention period: 1/K
  Total access delay will be greatly reduced
  Overall MAC efficiency increases
    The length of data increases while the length of overhead remains the same
  Multi user diversity gain

## Slide 3: Access delay analysis of DL-OFDMA
[2]
E[D] vs. 4E[D’]

## Slide 4: Simulation parameter
Guard interval: long
Data preamble: 11ac
Bandwidth: 20, 40, 80, 160 MHz
Max retries: 10
Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
RTS/CTS & BA
Cwmin: 15
PER: 0
MSDU length: 1500, 8000 bytes
Application data size: 1464 7964 bytes
L4 – L3 header overhead: 36 bytes
SIFS: 16us, DIFS: 34us
A-MPDU size = (MSDU + MAC header + delimiter)*8 + padding + service + tail = (1500 + 30 + 4)*2*8 + 16 + 16 + 6 = 24582 bits
A-MPDU duration = ceil((FrameLength*8) /rate /OFDMsymbolduration) * OFDMsymbolduration + PHY Header = ceil(24582/6.5/4) * 4 + 40

## Slide 5: Comparison of mean access delay between 11ac widerband operation and DL-OFDMA
Contention isolation reduces greatly the total access delay for multiple user DL data

## Slide 6: DL OFDMA with basic access
Considering a dense OBSS environment
  STAs might belong to the radio range of different OBSSs
  AP and STAs might see the busy/idle state of secondary channels differently
  AP could not guarantee that DL target STAs, allocated at secondary channel, will receive data successfully
DL OFDMA might not be utilized efficiently in dense OBSS environment

## Slide 7: DL OFDMA in dense OBSS environment

## Slide 8: RTS/CTS in DL OFDMA
probability p: probability with which each secondary channel is independently busy[3]
The throughput of DL OFDMA will decreases proportionally to p
RTS/CTS does not enhance the DL throughput of AP as p varies

## Slide 9: Existing control mechanisms in DL OFDMA
AP cannot predict which STAs are able to respond RTS through secondary bands
  AP has no channel state information of STAs
Existing RTS/CTS mechanism is not suitable for multi user operation
In order to achieve the contention isolation gain from DL OFDMA, it is required to increase the probability of successful CTS transmission of STAs (p)
Further coordination might be necessary along with current RTS/CTS mechanism

## Slide 10: Simple examples of coordination for DL OFDMA
CH state feedback
RTS/CTS modification

## Slide 11: Trade off of coordination
Various solutions could be developed
Coordination will introduce additional overhead in time
Depending on the types of coordination, the coordination gain and overhead could vary
Trade off between coordination gain and overhead

## Slide 12: Expected AP throughput enhancement
With proper coordination, AP throughput can be enhanced even with a large value of coordination overhead (tco=1000 microsec)

## Slide 13: Network throughput difference
How much will the coordination overhead affect the overall network throughput?
throughputnet(coordinated) - throughputnet(non coor.)

## Slide 14: Summary
Coordination for increasing the probability of transmitting CTS(p) could be developed in various ways
  Trade off between the increment of p and coordination overhead
As network gets denser (chance of transmitting data decreases), the overhead of coordination becomes negligible in terms of AP throughput and overall network throughput

## Slide 15: Conclusion
DL-OFDMA is a promising technique in terms of contention isolation which could reduces DL-UL asymmetry problem
In dense OBSS environment, busy/idle state of secondary channels could be different by the location of STAs
Existing basic access or RTS/CTS mechanism is not a proper to control DL-OFDMA
Additional coordination might be necessary to fully utilize DL-OFDMA

## Slide 16: References
[1]11-13-1377-00-0hew-dl-efficiency-enhancement-in-high-dense-network
[2] Wang, Yunbo, Mehmet C. Vuran, and Steve Goddard. "Cross-layer analysis of the end-to-end delay distribution in wireless sensor networks." IEEE/ACM Transactions on Networking (TON) 20.1 (2012): 305-318.
[3] 11-13-1058-00-0hew-efficient-wider-bandwidth-operation