## Slide 1: Proposed Spec Framework Document for 11ax considering potential tech features
Date: 2014-11-05
Authors:

## Slide 2: Introduction
TGax agreed on the timeline [1] that starts SFD discussions from this November meeting.
We propose a skeleton of 11ax SFD considering the previous 11ac SFD[2] and the potential tech features contributed for 11ax.

## Slide 3: Recap: ToC of the 11ac SFD [2]
1 Definitions
2 Abbreviations and acronyms
3 VHT Physical Layer
4 DL MU-MIMO and Transmit Beamforming
5 Coexistence
6 MAC
DL MU-MIMO
Wide BW
256 QAM
TxBF simplification
11ac tech features
PHY
MU-MIMO
COEX
MAC
11ac Ad Hoc groups
In 11ac SFD, along with mandatory PHY & MAC sections, additional sections were allocated for newly introduced major technical features
Therefore, in order to sketch 11ax SFD skeleton properly, we need to consider potential tech. features for 11ax.
…

## Slide 4: Potential tech features for 11ax
Potential tech features | High-level agreement | On-going discussions
DL OFDMA | Support DL OFDMA | Granularity of sub-channel BW [7][19] Signaling of STA & sub-CH [14] ACK procedure [11][16][20] Channel access rules [5][6][13] OFDM symbol alignment between sub-CHs [11]
UL OFDMA/ UL MU-MIMO | - | Frequency, Time, Power Synchronization [1][2][3][5][6][10] Scheduling/Signaling [3][4][5][7][8][9][11][12]
OFDM/Outdoor | Support 256 FFT on 20MHz | CP length options for outdoor support [1][2][5][6][7] Frequency offset increase [2][3] Mid-packet CCA, PAPR problem [3] Signaling of OFDM symbol duration & CP length [4] Coping with outdoor channel variations [5]
CCA | Support increased CCA | Dynamic[1~10][40][42], Per-Link[36][39] CCA changes Use with Transmit Power Control [11][13][15][21][23][34] Adoption of 11ah’s BSS color [18][20][25][32][33][28] Legacy fairness [15][22][33][34][35] Interferences [34][41], Considering channel-width [37]
Energy Efficiency | - | Power save model for real time traffic [3] Considering Energy source model [9]
Among the various tech contributions, we think that the above features are actively discussed in 11ax (see per-feature references at the end of this slide)

## Slide 5: (Proposed) ToC for 11ax SFD
1 Definitions
2 Abbreviations and acronyms
3 HE Physical Layer
4 Multi User Support
5 Coexistence
6 MAC Layer
DL OFDMA
UL OFDMA/ UL MU-MIMO
OFDM/Outdoor
CCA
(Potential)
11ax tech features
PHY
Multiuser
Spatial Reuse
MAC
(Potential)
11ax Ad Hoc groups
By considering the potential tech features in the previous slide and the ad hoc group structure discussion in [3], we propose the above ToC for the 11ax Spec Framework Document.
Energy Efficiency
…

## Slide 6: Meeting the 11ax Func. Req. [4]
The current set of potential tech features will contribute to meet the functional requirements of 11ax
R1: 4X avg. tput per STA, power efficiency
R2: desirable latency (dense scenario)
R3: spectrum efficiency, OBSS interference mgmt.
R4: spectral efficiency with presence of legacy devices
R5: frequency reuse efficiency, interference mgmt. when high density, direct comm.
11ax Func. Req. (Performance & Efficiency)
11ax Potential Tech.
DL OFDMA
UL OFDMA/ UL MU-MIMO
OFDM/Outdoor
CCA
Energy Efficiency
…

## Slide 7: Potential Tech. Requirements for 11ax SFD
3 HE Physical Layer
  3.1 HE OFDM Modulation
    3.1.A: The draft specification shall include support of 256 FFT-based OFDM modulation for 20 MHz channel operation.
4 Multi User Support
  4.1 DL OFDMA
    R4.1.A: The draft specification shall include support of DL OFDMA.
5 Coexistence
  5.1 Spatial Reuse
    R5.1.A: The draft specification shall include support of CCA level adjustment for HE STA.
6 MAC Layer
Based on the high-level agreements for each potential tech feature, the above technical requirements can be added into SFD later.

## Slide 8: Conclusions
It is important to establish a systematic skeleton in 11ax SFD in order to contain the current technical agreements properly.
Based on the analysis of previous technical discussions, we proposed the 11ax SFD skeleton as follows
  3 HE Physical Layer
  4 Multi User Support
  5 Coexistence
  6 MAC Layer

## Slide 9: References
[1] [14/0649r1] 802.11ax Timeline Scenario (Qualcomm)
[2] [09/0992r21] 11ac Spec Framework Document
[3] [14/1184r2] TGax Ad Hoc Structure Discussion (Broadcom)
[4] [14/1009r2] 11ax Functional Requirement

## Slide 10: Ref. - DL OFDMA
OFDMA benefits
  [1] [10/0317r1] DL-OFDMA for Mixed Clients (Cisco)
  [2] [13/0871r0] Discussion on Potential Techniques for HEW (Renesas Mobile)
  [3] [14/0855r0] Techniques for Short Downlink Frames (Cisco)
OFDMA’s efficient channel usages
  [4] [13/0539r0] Efficient Frequency Spectrum Utilization (LGE)
  [5] [13/1058r0] Efficient wider bandwidth operation (LGE)
  [6] [14/1437r1] Efficient Wider Bandwidth Operation in IEEE 802.11ax (Yonsei Univ.)
Technical issues/solutions
  [7] [13/1382r0] Discussion on OFDMA in HEW (LGE)
  [8] [14/0839r1] Discussion on OFDMA in IEEE 802.11ax (Yonsei Univ.)
  [9] [14/1208r1] MAC considerations on 802.11ax OFDMA (Yonsei Univ.)
  [10] [14/1209r1] Multiple RF operation for 802.11ax OFDMA (Yonsei Univ.)
  [11] [14/1210r1] HEW PPDU Format for Supporting MIMO-OFDMA (Newracom)
  [12] [14/1211r0] Ack Procedure for OFDMA (Newracom)
  [13] [14/1417r0] HEW PPDU Transmission Discussion (Newracom)
  [14] [14/1428r0] Clear Channel Assessment for OFDMA PHY (NTU)
  [15] [14/1433r0] Protocol and signaling framework for OFDMA (Quantenna)
  [16] [14/1442r1] Considerations on DL OFDMA control mechanism (Yonsei Univ.)
Performance analysis
  [17] [14/0858r1] Analysis on Frequency Selective Multiplexing in WLAN Systems (Samsung)
  [18] [14/1169r2] Comparisons of Simultaneous Downlink Transmissions (Interdigital)
  [19] [14/1227r3] OFDMA Performance Analysis (MediaTek)
  [20] [14/1436r0] Overhead Analysis for Simultaneous Downlink Transmissions (Interdigital)
  [21] [14/1452r0] Frequency selective scheduling in OFDMA (Ericsson)

## Slide 11: Ref. - UL OFDMA/UL MU-MIMO
UL MU-MIMO
  [1] [09/0852r0] UL MU-MIMO for 11ac (Qualcomm)
  [2] [09/1036r0] Uplink MU-MIMO sensitivity to power differences and synchronization errors (Qualcomm)
  [3] [13/1388r0] UL MU-MIMO Transmissions (LGE)
Technical issues/solutions
  [4] [14/0598r0] Uplink multi-user MAC protocol for 11ax (KIT)
  [5] [14/0802r0] Consideration on UL MU transmission (LGE)
  [6] [14/0818r1] Synchronization Requirements (ZTE)
  [7] [14/1190r2] Frame Exchange Control for Uplink Multi-user transmission (ZTE)
  [8] [14/1232r1] On Multi-STA Aggregation Mechanism in 11ax (Newracom)
  [9] [14/1431r1] Issues on UL-OFDMA (Newracom)
  [10] [14/1446r0] Analysis of frequency and power requirements for UL-OFDMA (Ericsson)
Code-based Multiple Access
  [11] [14/0616r0] CSMA/CA enhancements (ZTE)
  [12] [14/1681r1] 802.11 Tgax PHY Frame Structure Discussion for Enabling New Contention Mechanism (ZTE)

## Slide 12: Ref. - OFDM/Outdoor
OFDM Numerology
  [1] [14/0804r1] Envisioning 11ax PHY Structure – Part I (LGE)
  [2] [14/0801r0] Envisioning 11ax PHY Structure – Part II (LGE)
  [3] [14/1228r2] Issues on 256-FFT per 20MHz (Newracom)
  [4] [14/1229r1] Dynamic OFDM Symbol Duration (MediaTek)
Outdoor Support
  [5] [13/0536r0] HEW SG PHY Considerations For Outdoor Environments (LGE)
  [6] [13/0843r0] Further evaluation on outdoor Wi-Fi (LGE)
  [7] [14/1439r0] Preamble Considerations in Large Channel Delay Spread Scenarios (Newracom)

## Slide 13: Ref. – CCA (1/2)
DSC & DSC simulations
  [1] [13/1012r4], [2] [13/1290r1], [3] [13/1487r2], [4] [13/1489r5], [5] [14/0045r2], [6] [14/0058r1], [7] [14/0294r0], [8] [14/0382r2], [9] [14/0635r1], [10] [14/0779r2] Dynamic Sensitivity Control (DSP Group)
  [11] [14/0523r0] MAC simulation results for DSC and TPC (Orange)
  [12] [14/0854r0] DSC and Legacy Coexistence (Sony)
  [13] [14/0868r1] UL & DL DSC and TPC MAC Simulations (Ericsson)
  [14] [14/1171r1] DSC Simulation Results for Scenario 3 (Sony)
  [15] [14/1207r1] OBSS Reuse mechanism which preserves fairness (Orange)
  [16] [14/1426r2] DSC and legacy coexistence (Ericsson)
  [17] [14/1427r2] DSC Performance (Ericsson)
CCA simulations
  [18] [14/0082r0] Improved Spatial Reuse – Part I (Broadcom)
  [19] [14/0083r0] Improved Spatial Reuse – Part II (Broadcom)
  [20] [14/0372r2] System level simulations on Increased spatial reuse (Marvell)
  [21] [14/0578r0] Residential Scenario CCA/TPC Simulation Discussion (InterDigital)
  [22] [14/0832r0] Performance Evaluation of OBSS Densification (Intel)
  [23] [14/0833r0] Residential Scenario Sensitivity and Transmit Power Control Simulation Results (InterDigital)
  [24] [14/0846r1] CCA Study in Residential Scenario (Qualcomm)
  [25] [14/0861r0] Impact of CCA adaptation on spatial reuse in dense residential scenario (Nokia)
  [26] [14/0889r3] Performance Gains from CCA Optimization (Broadcom)
  [27] [14/1199r1] CCA Study in Residential Scenario - Part 2 (Qualcomm)
  [28] [14/1403r0] Performance Analysis of BSS Color and DSC (Sony)
  [29] [14/1443r0] Adapting CCA and Receiver Sensitivity (Nokia)

## Slide 14: Ref. – CCA (2/2)
CCA measurements
  [30] [14/0629r0] Measurements on CCA Thresholds in OBSS Environments (WILUS Institute)
  [31] [14/1416r1] Observed Protocol Violations Caused by DSC for Roaming STAs (Aruba)
BSS Color concept
  [32] [13/1207r1] CID 205 BSSID Color Bits (Broadcom)
  [33] [14/0847r1] Further Considerations on Enhanced CCA for 11ax (WILUS Institute)
Technical issues/solutions
  [34] [14/0637r0] Spatial Reuse and Coexistence with Legacy Devices (MediaTek)
  [35] [14/0856r1] Evaluating Dynamic CCA/Receiver Sensitivity Algorithms (Cisco)
  [36] [14/0872r0] A Protocol Framework for Dynamic CCA (Realtek)
  [37] [14/0880r1] Increased Network Throughput with TX Channel Width Related CCA and Rules (MediaTek)
  [38] [14/1225r1] Considerations on CCA for OBSS Operation in 802.11ax (Huawei)
  [39] [14/1224r0] Link Aware CCA (Cisco)
  [40] [14/1233r2] Adaptive CCA for 11ax (Newracom)
  [41] [14/1435r0] Considerations on OBSS Spatial Reuse (MediaTek)
  [42] [14/1448r1] Considerations for Adaptive CCA (Newracom)

## Slide 15: Ref. - Energy Efficiency
PAR discussions
  [1] [13/1333r0] Power Efficiency PAR Requirements (Covariants)
  [2] [14/0026r1] thoughts on hew par (Apple)
Technical issues/solutions
  [3] [14/0352r0] Discussion on power save mode for real time traffic (LGE)
  [4] [14/0373r1] Energy Efficiency in HEW (Southeast Univ.)
  [5] [14/1454r1] Power Save Discussion (Nokia)
Evaluation Methodologies
  [6] [14/0827r3] Energy Efficiency Evaluation Methodology (Apple)
  [7] [14/1161r3] Parameters for Power Save Mechanisms (Apple)
  [8] [14/1162r1] Energy Efficiency Evaluation Methodology Follow Up (Apple)
  [9] [14/1444r1] Energy Efficiency Evaluation and Simulation Model (MediaTek)