## Slide 1: Link Budget Analysis for 40-50GHz Indoor Usage
Date: 2014-01-23
Authors:

## Slide 2: Introduction
Link budget analysis is the fundamental metric for communication system design

## Slide 3: Propagation Loss Model and Shadowing
PL[dB] = A[dB] +20*LOG10(fGHz) + 10*n*LOG10(dm) |  |  |  |  | 
Environment | LOS/NLOS | A [dB] | n | s(dB) | Env.#
LOS | LOS | 32.5 | 2.0 | 2.000 | 0
Reflection Env | LOS | 32.5 | 2.0 | 3.333 | 1
Blockage Env | LOS | 32.5 | 2.0 | 6.666 | 2
Shadowing and Link margin: (a) Shadow + Link Margin is assumed to be 3*s(dB)
(b) Reflection via wall, link margin up to 10 dB
(c) Blockage, link margin up to 20 dB

## Slide 4: Link Budget
Link Budget
  TX power: Tx_power=10dBm;
  Propagation Loss at 1 m: PL= 32.5+10*log10(45) =65.6dB
  Shadowing +link Margin: 3*s
  Rx signal Strength : Rx_power=Tx_power+Gt+Gr-PL-3*s
  Rx Noise Figure: Rx_NF=10dB
  Implementation loss=2dB
  Noise Floor for 1GHz channel: N=-174+10*log10(1e9)=-84dBm
  Rx SNR: RX_SNR= Rx_power –N-Rx_NF-Implementation loss
Tx TV/HH (Type = 1) |  |  |  | Rx STB/HH ( Type = 1) |  | 
#Antenna Elements | Tx Pwr Per ElementdBm | Element Gain (dB) | Array Loss (dB) | #Antenna Elements | Element Gain (dB) | Array Loss (dB)
1 | 10 | 0 | 0 | 1 | 0 | 0

## Slide 5: Link Budget for LOS case
PARAMETERS | Symbol | Unit
Transmitter |  | 
Modulation & coding Scheme | MCS | 
Data Rate | R | Mbps
Coding Rate | Rc | LDPC
Spreading Factor | SF | 
Center Frequency | Fc | GHz
Channel Bandwidth | BW | GHz
Tx Antenna Gain | GT | dB
Tx Transmit Power | PT | dBm
Receiver |  | 
Rx Noise Figure | NF | dB
EbN0 (0.1% PER)(3) | EbN0 | dB
SNR | SNR | dB
Rx Implementation Loss | IL | dB
Rx Antenna Gain | GR | dB
Sensitivity |  | 
Propagation Loss Index | PLI | 
Path Loss at 1m | L1 | dB
Minimum Rx Sensitivity Level | Smin | dB
Shadow/Link Margin | M | dB
Rx Power Calculations |  | 
Path Loss = (PT+GT+GR) -(PR+M) | Ld | dB
Range | d | m
QPSK |  |  | 
6 | 7 | 8 | 9
875 | 1094 | 1313 | 1421.9
1/2 | 5/8 | 3/4 | 13/16
1 | 1 | 1 | 1
45 | 45 | 45 | 45
1 | 1 | 1 | 1
0.0 | 0.0 | 0.0 | 0.0
10.0 | 10.0 | 10.0 | 10.0
10 | 10 | 10 | 10
2.8 | 3.4 | 3.9 | 4.7
2.2 | 3.8 | 5.1 | 6.2
2 | 2 | 2 | 2
0.0 | 0.0 | 0.0 | 0.0
2 | 2 | 2 | 2
65.6 | 65.6 | 65.6 | 65.6
-69.8 | -68.2 | -66.9 | -65.8
6 | 6 | 6 | 6
73.8 | 72.2 | 70.9 | 69.8
2.58 | 2.15 | 1.85 | 1.62

## Slide 6: Link Budget for NLOS case
QPSK |  |  | 
6 | 7 | 8 | 9
875 | 1094 | 1313 | 1421.9
1/2 | 5/8 | 3/4 | 13/16
1 | 1 | 1 | 1
45 | 45 | 45 | 45
1 | 1 | 1 | 1
0.0 | 0.0 | 0.0 | 0.0
10.0 | 10.0 | 10.0 | 10.0
10 | 10 | 10 | 10
2.8 | 3.4 | 3.9 | 4.7
2.2 | 3.8 | 5.1 | 6.2
2 | 2 | 2 | 2
0.0 | 0.0 | 0.0 | 0.0
2 | 2 | 2 | 2
65.6 | 65.6 | 65.6 | 65.6
-69.8 | -68.2 | -66.9 | -65.8
9.999 | 9.999 | 9.999 | 9.999
69.8 | 68.2 | 66.9 | 65.8
1.62 | 1.36 | 1.17 | 1.02
PARAMETERS | Symbol | Unit
Transmitter |  | 
Modulation & coding Scheme | MCS | 
Data Rate | R | Mbps
Coding Rate | Rc | LDPC
Spreading Factor | SF | 
Center Frequency | Fc | GHz
Channel Bandwidth | BW | GHz
Tx Antenna Gain | GT | dB
Tx Transmit Power | PT | dBm
Receiver |  | 
Rx Noise Figure | NF | dB
EbN0 (0.1% PER)(3) | EbN0 | dB
SNR | SNR | dB
Rx Implementation Loss | IL | dB
Rx Antenna Gain | GR | dB
Sensitivity |  | 
Propagation Loss Index | PLI | 
Path Loss at 1m | L1 | dB
Minimum Rx Sensitivity Level | Smin | dB
Shadow/Link Margin | M | dB
Rx Power Calculations |  | 
Path Loss = (PT+GT+GR) -(PR+M) | Ld | dB
Range | d | m

## Slide 7: Summary and Recommendations
Link budget analysis shows that without certain antenna gain provided by beamforming, 45GHz system can not work.
Recommendation: Beamforming is required for 45GHz indoor usage if the system needs to work for 10meter NLOS.