## Slide 1: Link Margin Comments on Letter Ballot 203
Date: 2014-11-04
Authors:

## Slide 2: Abstract
Letter Ballot 203 comments #3523, 3524 and 3525 address issues with the definition of the S1G Open Loop Link Margin Index element in section 8.4.3.170a of P802ah_D2.0. These comments were carried over with additional clarifications from comments on Letter Ballot 200 against D1.0. The D3.0 of this same document in Letter Ballot 205 has several revisions that improve the section, but the fundamental issues remain unresolved. This document elaborates on these comments in more detail so as to find a resolution acceptable to all parties. It also addresses comment #3526, which applies to the entire document.

## Slide 3: First Problem Open-Loop Link Margin
Draft P802.11ah_D3.0, sec. 8.4.3.170a SG1 Open-Loop Link Margin Index element
Defines “Open-Loop Link Margin ΔPLM” as:
  “the summation of transmit power Ptx and the receiver sensitivity RXsensitivity”
    ΔPLM = Ptxl + RXsensitivity
This is not an “Open Loop Link Margin”.
This is actually the Max. Link Path Loss.

## Slide 4: Link Margin
IEEE 802.11-2012 defines “Link Margin” (a.k.a. “Link Budget”) as:
  “Ratio of the received signal power to the minimum required by the station (STA).”
  (See: IEEE 802.11-2012, page 13)
Convert this to dB as follows:
  Link Margin (dB) = Received Power (dBm) – Receive Sensitivity (dBm)
    (Notice the units of each term).

## Slide 5: Link Margins in Practice
Link Margin for a successfully received packet is normally > 0 dB.
Link Margin of 0 dB means there is no margin.
  A packet may or may not be successfully received.
Link Margin < 0 dB means either:
  The packet will not be successfully received, or
  The assumption about either the received packet power or the sensitivity of the receiver are incorrect.
Functionally equivalent to “SNR margin” in Draft P802.11ah_D3.0.
  Prefer “Link Margin” instead of “SNR margin” since
  “Link Margin” already defined in IEEE 802.11-2012

## Slide 6: What Problem Are We Trying to Solve? (Shamelessly plagarised from Peter Dare, Sony Corp.)
What does TGah intend to do with this index?
Does the solution require a true Link Margin, or does it require the Max. Link Path Loss?
If it requires a true Link Margin:
  Fix the description in 8.4.3.170a to conform to the definition in IEEE 802.11-2012.
If it actually requires a Max. Link Path Loss:
  Change all instances of “Open-Loop Link Margin” in Draft to either:
    “Maximum Link Path Loss”, or
    “Open-Loop Maximum Link Path Loss”

## Slide 7: Interference
This simplistic analysis does not include interference
  But could be extended to include interference.
Does the TG wish to provide a metric that accounts for interference?

## Slide 8: Second Problem dB versus dBm
Definition of a Bel:
  Ratio of two power levels expressed in log10
  “Unit-less” scale factor
Definition of a Decibel (dB):
  dB = Bel/10
  “Unit-less” scale factor (Watts/Watts or mW/mW)
Definition of a dBm:
  Unit of power referenced to 1 mW
  Expressed in 10log10

## Slide 9: Scale Factor vs. Power Level
Example expressed in linear mWatts:
  PowerOut mW = Scale × PowerIn mW
Expressed in dB & dBm
  dBmOut = dB + dBmIn
“Link Margin” is a unit-less scale factor: dB
“Max. Link Path Loss” is a unit-less scale factor: dB
Cannot express either of these in units of dBm

## Slide 10: Third Problem Link Margin Index Definition
Draft P802.11ah_D3.0 defines the “Open-Loop Link Margin Index” (sic) as follows:
  “(-128+Dx0.5)dBm, where D is an unsigned integer number shown in Open-Loop Link Margin Index field.”
Assume, by inference, that D was intended to be the “Open-Loop Link Margin” (actually the Maximum Link Path Loss)
  Measured in dB
  Represented as a real number.
  Recommend define D in this manner
The “Index” value should be defined as “int(-128+Dx0.5)”
  Measured in units 0.5 dB
  Represented as an unsigned 8 bit integer
  Recommend define the “Index” in this manner

## Slide 11: Fourth Problem Link Margin Index Range
Range of values “Link Margin Index” in P802.11ah_D3.0:
  -128 dBm (sic) to -0.5 dBm (sic).
  Should use units of “dB”
Negative values for a “Link Margin”
  A useful Link Margin is positive. (Sometimes goes a little negative).
Negative values are meaningless for Link Free Path Loss
  Negative Link Free Path Loss is a signal “Gain”
  Power does not increase across a passive link
Choose a metric and it’s range to solve the problem
  “Link Margin” or “Max Link Path Loss”

## Slide 12: Fifth Problem “SNR margin”
Definition of “SNR margin” in P802.11ah_D3.0:
  SNRMargin = Ptx 2  OPLM + RSSI
Functionally equivalent to the definition of a “Link Margin” in IEEE 802.11-2012
Recommend replacing all instances of “SNR margin” with “Link Margin”

## Slide 13: Sixth Problem Normative Text
Most sections in this draft contain no normative text.
The few instances of normative text appear to be applied in a haphazard manner.
There is no way to determine what is a normative requirement and what is just explanatory text.
Early IEEE 802.11 documents were casual about this, but new amendments and revisions “should” (“shall”?) conform to the requirements specified in IEEE 802.11-2012, section 1.4.

## Slide 14: Conclusions
Six significant technical issues
  Impossible to interpret how to implement
Clean up terminology, normative text & units
Define what problem this section is trying to solve
  Decide whether Link Margin or Max Link Path Loss meets that requirement
  Optimize the useful range of values to use for the index in the element

## Slide 15: References
Draft P802.11ah_D1.0
Draft P802.11ah_D2.0
Draft P802.11ah_D3.0
IEEE 802.11-2012