## Slide 1: Offline Discussion Minutes of SLS Calibration
Date: 2014-11-06
Authors:

## Slide 3: Motivation & Objective
Though basic SLS evaluation methodology has been formally described, there are still many issues not clearly defined.
Companies may have different implementations of those unclear MAC/PHY features, which has exhausted so much time and effort.
To speed up the joint SLS calibration, we definitely require a common implementation (simple and reasonable) for each divergent feature.

## Slide 4: Potential Differences
  Differences depend on how accurate we’d like the SLS is
    Preamble model
    Preamble detection metric
    RBIR PHY abstraction
    Receiving procedure and CCA status
    Control frame detection
    Box5 calibration scenario
    etc.
  Discussion results for each item will be marked in red color

## Slide 5: Preamble Model
Which model do you prefer?
  Opt 1: Take the whole preamble as a standalone sub-frame
  Opt 2: Deal with SFT, LTF, SIG individually
Companies prefer Opt 1.

## Slide 6: Preamble Detection
Which method do you prefer?
  Take the whole preamble as a standalone sub-frame
    Opt 1: Preamble decoding error modeled based on SINR threshold
      Set a preamble error SINR threshold T
      If SINR < T, preamble decoding fails, otherwise, it passes;
    Opt 2: Preamble decoding modeled as a sub-frame decoding
      Take the whole preamble as a standalone sub-frame
      The PHY abstraction can be used for preamble PER prediction
      The impairments such as channel estimation error may be captured
        The CE model based on LTF is TBD
        For calibration, link adaptation and CE model are ignored temporarily
Companies prefer Opt 2.

## Slide 7: RBIR PHY Abstraction
Which RBIR-based PHY abstraction solution do you prefer for PER prediction under asynchronous and time-varying interference?
  For AMPDU, each MPDU is decoded individually
    Opt 1: Whole packet average
    Opt 2: Weakest link
    Opt 3: Block-wise PHY abstraction
    Opt 4: Simplified block-wise (aka the weakest link with the length scaled)
Most companies prefer Opt 4, but Opt 2 is also suggested by a few companies.

## Slide 8: Receiving Procedure (1)
Do you agree the following basic reception principle?
  Receiver starts a scanning window if a packet arrives, and switches the window to another packet if this packet arrives within the window and has rx power xdB higher than the current packet.
    The xdB threshold is TBD and the window size is TBD in [0, PPDU duration].
    If window size =0, that is, receiver will be locked by the first-arrived packet, and later-arrived packets are considered as interference.
      For calibration, set window size = 0
  Any packet with rx power lower than rx sensitivity is dropped, which does not impact current receiver status;
  Any packet with rx power higher than rx sensitivity will be dealt with, i.e., its preamble will be detected;
The above text is accepted by almost all the companies.

## Slide 9: Receiving Procedure (2)
Do you agree the following description?
  If preamble passes (i.e., successfully detected), the receiver continues to receive the rest part of the packet, i.e., to decode each MPDU;
    If successfully decoding of a control frame, defer for NAV;
      Apply NAV cancellation for RTS according to current std spec
    Otherwise, set CCA to busy for the entire PPDU duration if rx power higher than TBD [rx sensitivity or CCA-SD].
      For calibration, set rx sensitivity = CCA-SD
  If preamble fails, the receiver terminates current reception
    The entire PPDU fails
    The receiver is unlocked again and CCA-ED threshold is used to determine if the medium is busy.
The above text is accepted by almost all the companies.
  The above procedure could be modified correspondingly if BSS color or/and PAID is introduced later.

## Slide 10: Control Frame Detection
How to decide RTS/CTS/ACK reception is pass or fail?
  Opt 1: decoding error modeled based on SINR threshold
    Set a error SINR threshold T
    If SINR < T, decoding fails, otherwise, it passes;
  Opt 2: decoding error modeled as a sub-frame decoding
    Take the whole control frame as a standalone sub-frame
    The PHY abstraction can be used for the PER prediction
      For calibration, MCS0 is used for control frames
Almost all the companies prefer Opt 2.

## Slide 11: Box5 Calibration Scenario
Which scenario do you prefer to use for Box5 calibration?
  Opt 1: Firstly using 11ac SS6 as an easy-to-start reference scenario to solve differences among individual implementations, and then after successfully calibration, turn to calibrate more complicated 11ax scenarios;
  Opt 2: Directly calibrating more complicated and time-comsuming 11ax scenarios;
  Opt 3: Slim down one of the 4 11ax scenarios into a simplified scenario, and redefine the number and locations of the used APs/STAs; after successfully calibrating the clipped scenario, go to calibrate the full 11ax scenarios.
No consensus but several companies have already chosen Opt 1 and got initial results.

## Slide 12: Summary
A big progress was made towards SLS calibration.
Open issues will be further discussed offline.
Propose a textfile to reflect our agreement in the EMD in the next meeting.
  Firstly distribute a draft to all interested companies for a thorough offline review.