## Slide 1: Nov 802.19 Liaison Report
Date: 2014-11-06
Authors:

## Slide 2: Presentation Outline
Part 1 – Let’s Work Together
Part 2 – Lessons Learned
  IEEE 802.11
  IEEE 802.15.2
  IEEE 802.16h
  IEEE 802.22
  IEEE 802.19.1
Part 3 – Backup
  Coexistence History in IEEE 802
  Coexistence Scenarios and Metrics
  Examples of Coexistence Assurance Documents
  Coexistence Mechanisms: IEEE 802.11, 802.15.2, 802.16h, and 802.22
  Overview of 802.19.1 Standard for TVWS Coexistence
  IEEE 802 Coexistence Process
  References

## Slide 3: IEEE 802 wants to work with 3GPP to achieve consensus on 802.11/LAA sharing
IEEE 802 would like the opportunity to review the 3GPP coexistence simulation studies related to LAA and 802.11 and provide feedback
IEEE 802 would also like to review a range of documents throughout the period of the study item
Examples of information that IEEE 802 is interested in reviewing include,
  The SI schedule as it develops
  Details of the fairness criteria
  The simulation scenarios
  The LBT related parameters
  The simulation methodology
  Other coexistence mechanisms for fair sharing
Our goal is for IEEE 802 and 3GPP to build towards a consensus on the best way for LAA to fairly share the same spectrum with 802.11 systems

## Slide 4: IEEE 802.11 CSMA/CA is better suited to sharing unlicensed spectrum than TDMA-like systems
CSMA/CA works in ISM bands (such as 2.4 and 5.8 GHz band) where there is uncontrolled energy in the band
IEEE 802.11 attempted to use TDMA-like systems (PCF and HCCA), and they have failed in the marketplace for a variety of reasons
  It is impractical to coordinate access between low-cost independent systems, particularly for mobile devices moving across networks
  The performance provided by CSMA/CA has proven by its wide adoption in the marketplace to be good enough for the vast majority of use cases
License-exempt wireless systems cannot rely on the guaranteed reception of radio management and control traffic

## Slide 5: IEEE 802.16h: it is challenging to make scheduled systems, like 802.16h, compatible with 802.11 systems
Note: Of all the 802 systems, 802.16h is the closest analog to LTE in unlicensed bands
The time-synchronization requirements of 802.16h systems are incompatible with deployed 802.11 systems
Coordination access required a high-cost high-speed control channel between 802.16h and 802.11 systems, which may be impractical
Coordination of policy between 802.16h and multiple 802.11 systems is challenging since 802.11 systems are often independently managed