## Slide 1: Performance Analysis of BSS Color and DSC
Date: 2015/01/12
Authors:

## Slide 2: Abstract
Performance comparison of DSC vs. BSS Coloring has been shown through system simulation in [1]
  There is not so much gain if only BSS Coloring is used and DSC outperforms in the simulation
  When BSS Coloring is used with DSC it can increase gain when the offset of Rx sensitivity level is relatively small
  In the simulation, filtered packets by BSS color always cause BUSY until end of packets
This time, BSS coloring with a second deferral level is considered
  After filtering OBSS packets, 11ax STA can transit to IDLE depending on this 2nd deferral level
Performance of DSC vs. BSS Coloring (w/ 2nd deferral level) has been compared again in this contribution

## Slide 3: BSS Color (Updated)
A mechanism introduced in 802.11ah
Assign a different color per BSS
  How a color is selected by the AP is not defined
This color is indicated in the .11ah PHY Header
  In this simulation, the color information is assumed to be in HT/VHT-SIG without increasing number of bits of SIG
Upon reception of a PPDU from an OBSS, i.e. with a different color, packet reception procedure may be abandoned
  STA that supports this feature is abled to add and compare color
  In this simulation, CCA after abandoning depends on the signal level
Chart: 
| 10 | 5 | -5 | -10 | -5 | 5 | 10
BSS0 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
BSS1 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
BSS2 | 25.98 | 34.64 | 34.64 | 25.98 | 17.32 | 17.32 | 25.98
BSS3 | 25.98 | 34.64 | 34.64 | 25.98 | 17.32 | 17.32 | 25.98
BSS4 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
BSS5 | -25.98 | -34.64 | -34.64 | -25.98 | -17.32 | -17.32 | -25.98
BSS6 | -25.98 | -34.64 | -34.64 | -25.98 | -17.32 | -17.32 | -25.98
 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
 | 25.98 | 34.64 | 34.64 | 25.98 | 17.32 | 17.32 | 25.98
 | 51.96 | 60.62 | 60.62 | 51.96 | 43.3 | 43.3 | 51.96
 | 51.96 | 60.62 | 60.62 | 51.96 | 43.3 | 43.3 | 51.96
 | 51.96 | 60.62 | 60.62 | 51.96 | 43.3 | 43.3 | 51.96

## Slide 4: DSC Algorithm
STA: Beacon RSSI based algorithm
    Compare the RSSI of the most recently received Beacon with “Trigger Threshold” and if exceed the threshold, toggle the state of Rx Sensitivity Level to “Raised”. Otherwise toggle the state to “Default”
      In this time Trigger Threshold is set to -41dBm
    Rx sensitivity level during “Default” is fixed to -82dBm
    Rx sensitivity level during “Raised” is a parameter (A dbm)
    CCA threshold is always -62dBm
AP: Fixed
    AP’s Rx sensitivity level is always set to A dBm
    CCA threshold is always -62dBm
Raised Rx Sensitivity Lv
STA
AP
Beacon
Beacon
Default Rx Sensitivity Lv
Beacon
Beacon
-40dBm
-50dBm
-38dBm
Raised Rx Sensitivity Lv
time
-40dBm

## Slide 5: Behavior of DSC and BSS Color w/ 2nd Deferral Level
L-STF/
LTF
PSDU
OBSS STA’s Tx
(with different COLOR)
not detected at all
L&VHT
SIG
VHT-STF/
LTF/SIGB
Rx PLCP
[Note] Assume COLOR information is included in VHT-SIGA
detected
COLOR doesn’t match
-> abandon Rx and compare signal level with 2nd deferral level
- Treated as CCA_IDLE -> can continue backoff procedure
- Can receive another packet
- Treated as CCA_IDLE -> can restart backoff procedure
- Can receive another packet
STA that enables
DSC
STA that enables
COLOR filtering
 | DSC | BSS COLOR filtering
Increasing Tx opportunity | Can improve. | Can improve. (But only when the packet has COLOR)
Acquiring Rx opportunity for desired signal | Can improve. | Can improve. (But only when the packet has COLOR)
[Note] Assume signal level
of interference packet is lower than
Rx sensitivity(DSC) / 2nd deferral Level(COLOR)

## Slide 6: Simulation Conditions
Scenario-3
  19-cell model with wrap-around (Reuse=3)
Traffic model
  10 uplink UDP Flows/BSS (Full-buffer condition)
  No downlink traffic
MCS selection
  Goodput maximizing MCS based on SINR by training[3]
Sensitivity control algorithm
  Beacon RSSI based algorithm[5]
Parameters
  Method (DSC / BSS Coloring)
  Rx sensitivity level (DSC) or 2nd deferral level (BSS Coloring)
    -82dBm ~ -52dBm
See backup slide for details
30m
10m

## Slide 7: Performance Comparison
BSS Coloring w/ 2nd deferral level
15%
Up
15%
Up
11%
Up
DSC
28%
Up
60%
Up
8%
Up
BSS
Total
Tput
per
STA
Tput
165%
Up
39%
Up
104%
Up
7%
Up
27%
Up
27%
Up
4%
Up
23%
Down
49%
Down
47%
Down
16%
Up
3%
Up
red...Ave
blue...CDF5%

## Slide 8: Performance Comparison
In almost all thresholds, the gain of DSC method is higher than BSS coloring method
[Note] Definition of ”Threshold for BUSY”
DSC: Rx sensitivity level (Raised state)
BSS Color: 2nd deferral level
BSS Color method is slightly better than DSC.
The gain of BSS Color method is saturated and DSC has much gain.

## Slide 9: Analysis - Difference of Rx Procedure
S >= Rx sensitivity Lv?
IDLE
BUSY＆Rx
Is Color matched?
S >= 2nd deferral Lv?
BUSY＆Rx
BUSY
Does PLCP have no err?
IDLE
Yes
Yes
No
No
Yes
Y
Y
No(PLCP err)
In this case,
S has already
been high!
(It depends on interference
scenario)
relatively rare
No
Yes
No
BUSY
No
Yes
No
Yes
BUSY & Rx PLCP
IFS=
EIFS
IFS=
AIFS
IFS=
EIFS
S >= Rx sensitivity Lv?
BUSY & Rx PLCP
Does PLCP have no err?
S+I >=
CCA th.?
S+I >=
CCA th.?
[NOTE]
CCA th.
= CCA threshold
= -62dBm
Yes or
have no color
Yes
No(PLCP err)
BSS Coloring w/ 2nd deferral level
DSC
Packets that its signal level is lower than 2nd deferral level often have PLCP error in this simulation condition.
(Full buffer condition – very high interference level)

## Slide 10: Conclusion
Performance of BSS Coloring and DSC has been compared in SS3
In almost all thresholds, the gain of DSC method is higher than BSS color method if these methods are used individually.
One reason of different gain is PLCP error
  Other possible reason is that packets from legacy STA cannot be filtered by color.
The possibilities of these methods (including combination) in other scenarios should be considered continuously.

## Slide 11: References
Masahito Mori, Sony, 11-14-1403-00-00ax-Performance Analysis of BSS Color and DSC
William Carney, Sony, 11-14-0854-00 DSC and Legacy Coexistence
Gwen Barriac, Qualcomm, 11-14-0851-02-00ax-rate-control-for-mac-and-integrated-system-simulations
Hongyuan Zhang, Marvell, 11-14-0372-02-0hew-system-level-simulations-on-increased-spatial-reuse
Graham Smith, DSP Group, 11-13-1290-01 Dynamic Sensitivity Control for HEW
Matthew Fischer, Broadcom, 11-13-1207-01-00ah-partial-aid-color-bits

## Slide 12: Appendix

## Slide 13: Simulation Setup details
Node | (AP x 1, STA x 10) x 19 (Half of STAs are 11AX STA, and others are Legacy STA)
Num of Drops [times] | 5
Traffic Model & Load & Duration | Uplink CBR UDP 30Mbps (from all STA -> Full Buffer condition), 20sec
Access Category | AC_BE CWmin=15, CWmax=1023, AIFSN=3, TXOP limit=0
Tx Power [dBm] | AP:+23dBm(2 antennas), STA:+15dBm(1 antenna)
MCS Selection | Goodput maximizing MCS based on Training (MCS0 ~ 7)
Packet Length [byte] | (MPDU, MSDU, APP)=(1030, 1000, 972) Fixed
L2 Retry | 10
Ack Rate | Legacy 6.0Mbps
RTS/CTS | OFF
Max Aggregation Size | (A-MPDU, A-MSDU)=(8KB, NA)
NF [dB] | 7
Channel | TGn Channel D (pathloss, shadowing, fading)
Channel Setting [MHz] | (CenterFreq, BW)=(2412, 20)
Rx sensitivity level [dBm] | Parameter (-82 ~ -52: on 11ax-STAs & APs , -82 on Legacy-STAs) [NOTE] Only DSC method
2nd deferral level [dBm] | Parameter (-82 ~ -52: on 11ax-STAs & APs , -82 on Legacy-STAs) [NOTE] Only BSS Coloring method
CCA sensitivity level [dBm] | -62
Det. Cancel on PLCP err | Enable (Error performance is shown in slide#14)
DSC algorithm | See slide #4
BSS COLOR operation | AP and 11AX STA can handle COLOR information. (adding/filtering) STAs cannot filter packets that has no COLOR information (i.e. flow from Legacy STAs).

## Slide 14: Simulation Setup details