## Slide 1: Payload Symbol Size for 11ax
Date: 2015-01-12
Authors:

## Slide 2
Authors (continued)

## Slide 3
Authors (continued)

## Slide 4
Authors (continued)

## Slide 5
Authors (continued)

## Slide 6
Authors (continued)

## Slide 7
Authors (continued)

## Slide 8: Outline
The need for larger symbol size for 11ax payloads has been discussed previously
  Eg: [1] investigated the impact of CFO estimation on symbols with larger FFT sizes (256 and 512 FFT)
We have investigated several symbol durations for the payload and propose a new symbol duration
We also follow up with a proposal for the choices of CP
The proposals are verified via simulations that show
  Significant Goodput gains over 11ac symbol and CP lengths of 3.2 us and 0.8 us respectively
  Robust performance in outdoor UL OFDMA

## Slide 9: Payload Symbol & CP Sizes
We propose to replace the current payload symbol duration (3.2 us) with longer symbol duration 12.8 us in order to meet the following 11ax requirements
  Robustness in outdoor channels
  Greater tolerance to timing jitter across users in UL MU/OFDMA
  Higher indoor efficiency (by lowering CP overhead)
We also propose the three following CP sizes
  0.8 us: 11ac long GI, targeting improved efficiency in indoor settings
  1.6 us: percent-wise 11ac short GI, targeting high efficiency in outdoor channels and indoor UL MU-MIMO/OFDMA
  3.2 us: percent-wise 11ac long GI, targeting robustness in the more demanding case of outdoor UL MU-MIMO/OFDMA

## Slide 10: Channel models & implications
Outdoor channels
  UMi-LoS, UMi-NLoS, UMa-NLoS
NLoS channels have large delay spreads with significant probability
Intersymbol interference leads to high error floors
0.8 us CP leads to error floors
Need longer CPs

## Slide 11: Spectral efficiency
Assume a fixed transmission bandwidth and choose an MCS
R = code rate, bps = bits/sample (in the frequency domain. Eg. 256 QAM, bps = 8)
Nfft = symbol FFT size, Ndata = #data tones/symbol, Ncp = #CP samples
Tone utilization
Depends only on MCS
Decreases as Ncp increases
Unless we increase Nfft
Increases as Ncp increases
As PER decreases for ISI channels
For a given Ncp (dictated by channel length), increase Nfft for smaller overheads and greater spectral efficiency
Spectral Efficiency

## Slide 12: Simulation setup
Packet structure
  Payload
    1000 bytes
    FFT sizes: 64, 128, 256 FFT
    Data tones as defined for corresponding FFT sizes in 11ac
    CP sizes: 0.8 us, 1.6 us
  11ax-LTF: 1 symbol, same (FFT size, GI) as payload
  11ax-Preamble: 3 symbols, 64 FFT (precise structure undecided now, but # guided by 11ac)
  How is the preamble relevant?
    Pilots used for phase tracking, reduce CFO estimation error
20MHz bandwidth, SISO, BCC
Real processing
  Channel estimation, timing, frequency offset estimation, phase tracking, phase noise: all real
L-STF
L-LTF
L-SIG
11ax
Preamble
11ax-LTF
Payload

## Slide 13: UMi-LoS: PER for MCS 0-4
PERs with 1.6 us GI (right figure) smaller than PERs with 0.8 us GI (left figure)
Even for a given GI, increasing FFT size reduces PER (ICI corrupted samples is a smaller fraction of the total number of samples)

## Slide 14: UMi-LoS: PER for MCS 5-9
PERs with 1.6 us GI (right figure) smaller than PERs with 0.8 us GI (left figure)
Even for a given GI, increasing FFT size reduces PER (ICI corrupted samples is a smaller fraction of the total number of samples)

## Slide 15: UMi-NLoS: PER for MCS 0-4
PERs with 1.6 us GI (right figure) smaller than PERs with 0.8 us GI (left figure)
Even for a given GI, increasing FFT size reduces PER (ICI corrupted samples is a smaller fraction of the total number of samples)

## Slide 16: UMi-NLoS: PER for MCS 5-9
PERs with 1.6 us GI (right figure) smaller than PERs with 0.8 us GI (left figure)
Even for a given GI, increasing FFT size reduces PER (ICI corrupted samples is a smaller fraction of the total number of samples)

## Slide 17: Goodput metric used for comparison
Goodput = max spectral efficiency obtained by picking the best MCS (for each SNR)
For a given CP size Ncp, choose largest possible Nfft
  CP overhead decreases
For a given FFT size Nfft , there is a tradeoff in choosing Ncp
  Small Ncp : small overhead, but PER may be large
  Large Ncp : PER is small, but overhead large
  Choose the sweet spot for Ncp
Spectral Efficiency

## Slide 18: Goodput: AWGN
For best results, pick as large an FFT as possible and then pick the smallest CP
  Increasing CP has no PER benefit in AWGN, increasing FFT reduces overhead
Using (256 FFT, 0.8 us CP) gives 1.32x goodput of (64 FFT, 0.8 us CP)
Absolute Goodput
Goodput relative to (64 FFT, 0.8 us CP)

## Slide 19: Goodput: 11nD
Using (256 FFT, 0.8 us CP) gives ~1.3x goodput of (64 FFT, 0.8 us CP)
Since channels have small delay spreads, 0.8 us CP has 6-7% better throughput than 1.6 us CP (256 FFT, around 15-20 dB)
Absolute Goodput
Goodput relative to (64 FFT, 0.8 us CP)

## Slide 20: Goodput: UMi-LoS
At high SNR
  Best to use large FFT with longer CP (256 FFT, 1.6 us CP)
  (256 FFT, 1.6 us CP) gives nearly 2.2x goodput of (64 FFT, 0.8 us CP)
At small SNR
  Thermal noise dominates ISI: increasing CP doesn’t give substantial PER gains
  Stick to smaller CPs, but use larger FFTs: (256 FFT, 0.8 us CP) works best
Absolute Goodput
Goodput relative to (64 FFT, 0.8 us CP)

## Slide 21: Goodput: UMi-NLoS
Large delay spreads leads to high ISI
  Best to use large FFT with longer CP (256 FFT, 1.6 us)
  (256 FFT, 1.6 us CP) gives ~2.5x goodput of (64 FFT, 0.8 us CP) at 25 dB SNR
Absolute Goodput
Goodput relative to (64 FFT, 0.8 us CP)

## Slide 22: Challenge of UL-OFDMA
Timing jitter across users on the UL effectively increases channel delay spread. What is the impact on performance?
  Impact of intended user delay on himself
  Impact of delay of interfering users on intended user
Sources of timing jitter
  Different round trip delay
  Different timing acquisition points due to different channel delay spreads and noise
  Net timing jitter ~1.3 us (details in Appendix)

## Slide 23: Simulation setup
UL OFDMA with 4 users
Each user has one antenna, AP has 4 Rx antenna
20MHz, 256 FFT
  Each user is allocated a contiguous block of 56 tones.
  User allocations are fixed, and the second user (middle one) is the desired user (PER/Goodput are calculated for this user)
GI values considered: 1.6us, 3.2us
ITU UMi NLOS channel
1000 bytes packets
Real channel estimation from one LTF

## Slide 24: Results
Interfering users have no jitter
For intended user delay of 1.2 us
Goodput with 3.2 us GI = 1.16x Goodput with 1.6 us GI

## Slide 25: Discussion
Summary
  256 FFT consistently outperforms 11ac symbol duration
  Goodput gains range from 1.3x-2.5x depending on channel
  Use 0.8 us CP with 256 FFT for high efficiency in indoor channels
  Use 1.6 us CP with 256 FFT for greater robustness to long outdoor channels and indoor UL OFDMA/MU-MIMO
  Use 3.2 us CP with 256 FFT for robust performance in outdoor UL OFDMA/MU-MIMO
Why not even higher FFT sizes, say 512 FFT over 20 MHz?
  Implementation complexities increase with increasing FFT sizes and bandwidths
  Tones are more narrowly spaced , CFO correction needs to be very precise: challenging task [1]
  Incremental gain over 256 FFT (3-6% depending on CP size) too small for increased complexity
  256 FFT size in 20 MHz seems to be the sweet spot between performance and implementation complexities

## Slide 26: Proposal
We propose that 11ax shall have one longer payload symbol size of duration 12.8 us based on a 256 FFT in 20 MHz
  And correspondingly 512 FFT in 40 MHz, 1024 FFT in 80 MHz/80+80 MHz and 2048 FFT in 160 MHz
We also propose to use the following CP sizes: 0.8 us, 1.6 us and 3.2 us

## Slide 27: References
[1] 11-14-0801-00-00ax-envisioning-11ax-phy-structure-part-ii

## Slide 28: Straw Poll #1
Do you agree to add to the TG Specification Framework:
– 3.y.z. Data symbols in an HE PPDU shall use DFT period of 12.8 us and subcarrier spacing of 78.125 kHz.
Yes
No
Abstain

## Slide 29: Straw Poll #2
Do you agree to add to the TG Specification Framework:
– 3.y.z. Data symbols in an HE PPDU shall support guard interval durations of 0.8 us, 1.6 us and 3.2 us.
Yes
No
Abstain

## Slide 30: Appendix

## Slide 31: UMa-NLoS: PER for MCS 0-4

## Slide 32: Goodput: UMa-NLoS
Absolute Goodput
Goodput relative to (64 FFT, 0.8 us CP)

## Slide 33: Sources of timing jitter
Different round trip delays can contribute 0.6 us (~ 200 m)
Timing acquisition on DL can contribute 0.7 us jitter in UMi-NLoS channels. For example, at 10 dB in figure below, 14 samples @ 20 MHz = 0.7 us
AP has 4 antennas, STA has 1 antenna
Timing acquired from L-LTF