## Slide 1: TGax SLS MAC Calibration Test 4 Results
Date: 2015-1-12
Authors:

## Slide 2: Background
MAC Calibration is ongoing as part of SLS [1].
4 total calibration tests are included in the MAC calibration spec [2].
Test 4 is designed for scenarios where two BSSs have different channel bandwidth [2][3].
  The first BSS operates in 40 MHz channel
  The second BSS operates in a 20MHz channel which is the secondary channel of the first BSS.
  The 40MHz BSS is running full buffer.
  The 20MHz BSS is generating Poisson traffic with lamda = 100.
  MSDU size 2000 bytes.

## Slide 3: Traffic Generation
Poisson traffic generation
  OnOff application
  Off time with exponential distribution, lamda = 100 (mean=0.01).
MAC behavior
  Generated traffic will be buffered in MAC buffer.
  MAC will contend the channel and transmit with priority of AC_BE

## Slide 4: Test Results
RTS/CTS | Backoff | Aggregation | MCS | MSDU size | MAC PER | Application Throughput | Channel Occupancy
OFF | ON | ON | MCS 0 | 2000 | BSS1: 4.12% | BSS1: 8.10664 | BSS1: 65.20%
 |  |  |  |  | BSS2: 8.17% | BSS2: 1.52189 | BSS2: 27.14%
ON | ON | ON | MCS 0 | 2000 | 0 | BSS1: 7.76083 | BSS1: 73.65%
 |  |  |  |  | 0 | BSS2: 1.30356 | BSS2: 23.48%

## Slide 5: Detailed Settings
Simulation time is 10 seconds
Secondary channel CCA is assumed
A-MPDU of size 1
Traffic category, BSS1: AC_BE, BSS2: AC_BE
  MAC header 30 bytes, no HT control
  L4 header : 36 bytes
    The definition of L4 header is UDP header +IP header +LLC
SIFS= 16us
Expecting waiting time for medium is 110.5 us
  Contention window is 15

## Slide 6: Test Objectives
Airtime sharing by two BSSs with different channel bandwidth
Throughput performance under this circumstance
PER performance under this circumstance
Calibrate with other companies/simulators

## Slide 7: Conclusion
Provide the test 4 results of SLS MAC calibration
To complete the missing part of the test very soon.

## Slide 8: Reference
  [1]. Doc. IEEE 802.11-14/0571r5 11ax evaluation methodology
  [2]. Doc. IEEE 802.11-14/0621r4 / Doc. IEEE 802.11-14/0980r4 ax Simulation scenarios
  [3]. Doc. IEEE 802.11-14/0895r1 Calibration of MAC simulator with OBSS Network Scenario