## Slide 1: Evaluating Power Save Performance
Date: 2015-03-09
Authors:

## Slide 2
Authors: [Continued]

## Slide 3: Background
In [1], the concept of energy efficiency evaluation methodology was introduced in 11ax, and subsequently updated in [2, 3]
  All of these concepts [4, 5] were accepted in the TGax documents for Evaluation Methodology [6] and Simulation Scenario [7].
Since then, this topic has been in active discussions [8, 9, 11] and they have led to clarifications and updates to [6, 7]
Some companies have upgraded their system simulators with power save capabilities, and also presented calibration results for U-APSD [10, 12, 13] and PSM [10, 13]
As TGax continues to work on power save calibrations, this presentation is intended to kick off discussion on evaluating the performance of a power save mechanism

## Slide 4: Abstract
This presentation discusses two concepts to evaluate the performance of a power save mechanism:
  Power States refinement
    Separate Sleep State into two sub-states, i.e. Deep Sleep and Shallow Sleep
  Network Energy Efficiency Ratio (N-EER)
    To measure efficiency of total energy used to deliver information bits over the network
    To provide more general formula to calculate EER for one or multiple STAs

## Slide 5: Update Discussion on Power States
In [1], we have introduced two sub-states of the Sleep state (Shallow Sleep & Deep Sleep); however
  To simplify the simulations, only one Sleep state was proposed to be in use for calibration simulations [2]
Since then, we have heard many comments to distinguish more sleeping states for realistic Power Savings (PS) modeling
With this presentation, we propose two sub-states to Sleep state, Shallow Sleep and Deep Sleep, for power save evaluation methodology
  Shallow sleep has slightly higher power consumption than deep sleep, but a shorter transition time to Awake state

## Slide 6: Power State Transitions and Consumption Levels [1]
The power state transition table is used for power model calibration across System simulators
We make the assumption that these power state transitions are independent of MCS, channel bandwidth, frequency bands, etc.
We need values of power consumption for Deep/Shallow sleep states in the table for power state transition
*For Calibration, one sleep state may be used
Transmit
Receive
Listen
Shallow Sleep
Deep Sleep
Power state Transition
Sleep State*
Awake State

## Slide 7: Example of Power States and Power State Transitions during Power Save Polling Operation
AP buffers this frame since this STA is in Power Save
AP
STA1 (TIM indicated)
ACK
PS-Poll
Beacon
DATA
Beacon
STA1 starts CCA for PS-Poll
STA1 Power Sate
TX→SS
DATA
RX
RX
RX
TX
TX
LI
LI
LI
SS/DS
AP starts CCA for downlink DATA
Shallow Sleep (SS)
DS
Transmit (TX)
Receive (RX)
Deep Sleep (DS)
TX→LI→RX
RX→TX
ACK
LI
SS→LI
SS/DS
Listen (LI)
Power State Transition
Assuming there no other traffic in medium
STA2 (No TIM indicated)
LI
SS→LI
RX
STA2 Power Sate
RX
LI
SS/DS
LI
RX
Li→DS
DS→Li

## Slide 8: Modification on Power Model Parameter Table
Split Sleep state into two sub-states (Shallow Sleep and Deep Sleep) in the table [7]
  The value of current for this state is TBD
* For calibration purposes, the same number as in Deep Sleep may be used as one sleep state

## Slide 9: Modification on Power Transition Parameter Table
Define one more transition between Listen and Deep Sleep in the table [7]
  The transition values are TDS, PDS (TBD)
Average power consumption is found by average of power for two states in transition
  For example, PRT = (PT + PR)/2, based on the power model parameter table
* For calibration purposes, only one sleep state (Deep Sleep) can be considered

## Slide 10: EER Definition
[2,3,6] defined the energy efficiency ratio (EER)
For fair comparison of PS proposals, we may need clearer definition of EER under network topology, in Evaluation Methodology document

## Slide 11: Network EER Metric for Evaluation
Definition of the Network EER (N-EER) metric for evaluation

## Slide 12: Conclusion
In this presentation, we proposed the following two updates to the Evaluation Methodology [6] and Simulation Scenario [7] documents
  Two sleeping states, i.e. Shallow Sleep and Deep Sleep
  Introduced N-EER
Any PS proposal is encouraged to use the numbers in the power consumption table for EER evaluation

## Slide 13: References
[1] IEEE 11-14-0827-03, Energy Efficiency Evaluation Methodology, July 2014.
[2] IEEE 11-14-1161-03, Parameters-for-power-save-mechanisms, Sept 2014
[3] IEEE 11-14-1162-01, Energy-efficiency-evaluation-methodology-follow-up, Sept 2014
[4] IEEE 11-14-1286-03, Energy-efficiency-redline-to-simulation-scenarios, Sept 2014
[5] IEEE 11-14-1285-01, Energy-efficiency-redline-to-evaluation-methodology, Sept 2014
[6] IEEE 11-14-0571-07, Evaluation-Methodology
[7] IEEE 11-14-0980-06, Simulation-Scenarios
[8] IEEE 11-14-1444-02, Energy-efficiency-evaluation-and-simulation-model, Nov 2014 (Mediatek)
[9] IEEE 11-14-1454-01, Power-save-discussion, Nov 2014 (Nokia)
[10] IEEE 11-14-1495-00, Power-save-calibration-results, Nov 2014 (Nokia)
[11] IEEE 11-14-1496-05, Power-save-calibration-scenario, Nov 2014 (Nokia)
[12] IEEE 11-15-0072-00, U-ASPD-powser-saving-calibration-results, Jan 2015 (Huawei)
[13] IEEE 11-15-0103-00, Power-save-calibration, Jan 2015 (Nokia)

## Slide 14: Straw Poll #1
Do you support to have multiple sleeping states, depending on power consumption level and transition delay?

## Slide 15: Straw Poll #2
Do you support to define two sleeping states, i.e., Shallow Sleep and Deep Sleep?

## Slide 16: Straw Poll #3
Do you support to update the power model parameter table and the power transition parameter table as in slide 8 & 9 in [7]?

## Slide 17: Straw Poll #4
Do you support to define an EER definition in [6] under title of “Network EER” in page 25 of [6], by referring to the power model parameter table in [7]?