## Slide 1: Effective Subcarrier Assignment for DL-OFDMA
Date: 2015-03-06
Authors:

## Slide 2: Background
DL-OFDMA is one of promising technologies for better efficiency in WLAN.
DL-OFDMA PPDU will include data for plural STAs. These data have various sizes and will be sent in various MCSs for each destination.
The following slides will show how the efficiency is in an OFDMA PPDU.

## Slide 3: Assumption -1
DL-data destined to 4 STAs are assumed to be packed in an OFDMA PPDU in 20MHzBW as below:
5MHzBW is assigned for each destination.
Dest. | Data size (bytes) | MCS | MOD | Coding Rate | FFT size @20MHz | Assigned subcarrier
STA1 | 50 | 0 | BPSK | 1/2 | 256 | 52
STA2 | 50 | 7 | 64QAM | 5/6 |  | 52
STA3 | 200 | 0 | BPSK | 1/2 |  | 52
STA4 | 200 | 7 | 64QAM | 5/6 |  | 52

## Slide 4: Flame Configuration -1
There will be big differences in required symbol lengths among destinations when assigned subcarriers are 52 fixed for each destination.
16 SL
52 subcarriers
52 subcarriers
52 subcarriers
52 subcarriers
62 SL
2 SL
7 SL
padding
padding
Time
STA1 :
STA2 :
STA3 :
STA4 :
50B
MCS=0
50B
MCS=7
200B
MCS=0
200B
MCS=7
Just data part was considered.
SL (Symbol Length) = number of consecutive OFDM symbols
Padding = 65%

## Slide 5: Assumption -2
DL-data destined to 3 STAs are assumed to be packed in an OFDMA PPDU in 20MHzBW as below:
10MHzBW is assigned for STA3 in this assumption.
Dest. | Data size (bytes) | MCS | MOD | Coding Rate | FFT size @20MHz | Assigned subcarrier
STA1 | 50 | 0 | BPSK | 1/2 | 256 | 52
STA2 | 50 | 7 | 64QAM | 5/6 |  | 52
STA3 | 200 | 0 | BPSK | 1/2 |  | 104

## Slide 6: Flame Configuration -2
Padding bits are greatly reduced comparing with Assumption-1. However, differences of required symbol lengths among destinations are still big.
16 SL
52 subcarriers
52 subcarriers
104 subcarriers
31 SL
2 SL
padding
Time
STA1 :
STA2 :
STA3 :
50B
MCS=0
50B
MCS=7
200B
MCS=0
Padding = 35%

## Slide 7: Flexible Subcarrier Assignment (1) (Assumption-1)
padding
Number of subcarriers will be decided based on required OFDM symbols for data for each destination as below figure:
This scheme will achieve more efficient resource utilization.
to STA1
22 SL
37 subcarriers
to STA2
to STA3
5 subcarriers
15 subcarriers
to STA4
151 subcarriers
8 SL
STA1 :
STA2 :
STA3 :
STA4 :
50B
MCS=0
50B
MCS=7
200B
MCS=0
200B
MCS=7
Padding:
65%  4%
Required SL:
62  22

## Slide 8: Flexible Subcarrier Assignment (2)
20M | STA1 | 0 |  |  |  |  |  | 
20M | STA1 | 0 |  |  |  |  |  | 
20M | STA1 | 0 |  |  |  |  |  | pad
20M | STA1 | 0 |  |  |  |  |  | pad
20M | STA2 | 7 |  |  |  |  |  | pad
20M | STA2 | 7 |  |  |  |  | pad | pad
20M | STA3 | 0 |  |  |  |  |  | pad
20M | STA3 | 0 |  |  |  |  |  | pad
20M | STA4 | 7 |  |  |  |  |  | 
20M | STA4 | 7 |  |  |  |  |  | pad
20M | STA4 | 7 |  |  |  |  |  | pad
〜
BW
STA ID
MCS
: Read data
HE header
Data part
A STA ID is identified in HE header part of each subcarrier.

## Slide 9: Assumption -3
DL-data destined to 4 STAs are assumed.
Similar data size and MCS for 4 STAs are considered as below:
Dest. | Data size (bytes) | MCS | MOD | Coding Rate
STA1 | 100 | 2 | QPSK | 3/4
STA2 | 100 | 3 | 16QAM | 1/2
STA3 | 120 | 2 | QPSK | 3/4
STA4 | 120 | 3 | 16QAM | 1/2

## Slide 10: Comparison (Assumption-3)
Fixed SC assignment
Flexible SC assignment
pad
pad
52SC
52SC
52SC
52SC
13 SL
Padding = 24.0%
54SC
42SC
64SC
48SC
10 SL
Padding = 1.3%
(0.8us+3.2us*4) * 13 = 176.8us
(0.8us+3.2us*4) * 10 = 136.0us
11 SL
8 SL
13 SL
10 SL

## Slide 11: Pros and Cons (Subcarrier Assignment for DL-OFDMA)
 | Fixed (by 5MHz unit) | Flexible
Pros | Simple PPDU processing Simpler ACK procedure? | Shorter PPDU Minimized padding bits More than 4 destinations available in a 20MHz PPDU
Cons | Longer PPDU More padding bits Up to 4 destinations in a 20MHz PPDU | Complicated PPDU processing Complicated ACK procedure?
Flexible subcarrier assignment should be considered to meet TGax objectives.

## Slide 12: Summary
Flexible subcarrier assignment for DL-OFDMA was proposed.
This scheme will realize more effective resource utilization.
Further studies are required for detailed mechanism definitions.

## Slide 13: Straw Poll
Do you agree to add the following text into SFD?
4. Multi-user (MU) features
The amendment shall allow to assign flexible number of subcarriers for each destination in DL-OFDMA PPDU.
Y/N/A =

## Slide 14: References
11-15/0132r2, Spec Framework Document
11-15/0066r0, Downlink OFDMA Protocol Design