## Slide 1: Impact of TPC coupled to DSC for legacy unfairness issue
Date: 2015/03/09
Authors:

## Slide 2: Abstract
Legacy fairness is an important requirement for 11ax. [1]
  [TGax R9] Legacy performances shall not be significantly degraded by operation in or in proximity of 11ax network.
The uplink performance of DSC combined with BSS Coloring has been shown in [2]
  BSS Coloring can increase the gain of DSC.
  But the unfairness issue wasn’t resolved in the contribution
In this submission, TPC coupled to DSC is considered and evaluated as a solution for recovering legacy fairness.
It is shown that increasing system gain and maintaining the fairness can be satisfied simultaneously in SS3 by selecting appropriate TPC and DSC parameters.

## Slide 3: Basic Setup
AP
(BSS Color filtering enabled)
AX STA
(DSC enabled, TPC on/off)
In order to
increase Tx occasion
In order to
recover the fairness of Legacy STAs
In order to
increase desired Rx occasion
Uplink Traffic

## Slide 4: Basic Setup
AP
(BSS Color filtering enabled)
AX STA
(DSC enabled, TPC on/off)
In order to
increase Tx occasion
In order to
recover the fairness of Legacy STAs
In order to
increase desired Rx occasion
Uplink Traffic
w/o Color
filtering at AP
Rx Interference Packet
Tx to AP
Detect ->
start Rx
Not detect due to DSC ->
can transmit simultaneously
ｘ
Interference Packet from OBSS
Cannot receive no matter how large the SINR is !
time
time
AP
AX STA
Terminate Rx at PLCP ->
can wait desired packet
w/ Color
filtering at AP
Tx to AP
Not detect due to DSC ->
can transmit simultaneously
Interference Packet from OBSS
time
time
AP
AX STA
Rx desired packet
* Although using DSC at AP side also increase Rx opportunity, it’s difficult to select appropriate threshold dynamically.
* So we use only COLOR in this submission.
Why increasing desired Rx occasion is needed at AP ?
-> To avoid wasting increased Tx occasion at STA

## Slide 5: DSC Algorithm
STA: Beacon RSSI based algorithm with Margin parameter[3]
  CCA-SD = min(L, (RSSIBeacon – M))
      RSSIBeacon: RSSI of Beacon frame from associated AP [dBm]
      L: Upper Limit of CCA-SD [dB]
      M: Margin [dB]
  CCA-ED = -62dBm
AP: Not applied
  CCA-SD = -82dBm
  CCA-ED = -62dBm
[NOTE] The term “CCA-ED” represents “20 dB above the minimum modulation and coding rate sensitivity” in this material.

## Slide 6: TPC Algorithm
STA: Basically reduce TxPower by amount of raising CCA-SD by DSC
  Also adjust by parameter α.
  TxPower = min(PDefaultTx , (PDefaultTx – D + α))
      PDefaultTx: Default TxPower of STA = +15 [dBm]
      D: Amount of raising CCA-SD by DSC [dB]
        i.e. D = CCA-SDRaisedByDSC – (–82dBm)
      α: Adjustment factor [dB]
AP: Not applied
  TxPower = +23 dBm

## Slide 7: Relation of DSC/TPC parameters
AP
STA
+23dBm
(about -35dBm in this case)
-82dBm
+15dBm
Example of SS3 (2412MHz)
Beacon
TxPower
CCA-SD

## Slide 8: Relation of DSC/TPC parameters
AP
STA
+23dBm
(about -35dBm in this case)
-82dBm
+15dBm
DSC Margin
CCA-SD
D: Amount of raising CCA-SD
Example of SS3 (2412MHz)
Beacon
TxPower

## Slide 9: Relation of DSC/TPC parameters
AP
STA
+23dBm
(about -35dBm in this case)
-82dBm
+15dBm
DSC Margin
CCA-SD
D: Amount of raising CCA-SD
Reduce by D.
Example of SS3 (2412MHz)
Beacon
TxPower

## Slide 10: Relation of DSC/TPC parameters
AP
STA
+23dBm
(about -35dBm in this case)
-82dBm
+15dBm
DSC Margin
CCA-SD
Further adjust by α. (parameter)
D: Amount of raising CCA-SD
Reduce by D.
Example of SS3 (2412MHz)
Beacon
Data
TxPower
DSC Margin and Adjustment value
are varied at this time.

## Slide 11: Simulation Conditions
Scenario-3
  19-cell model with wrap-around (Reuse=3)
Traffic model
  10 uplink UDP Flows/BSS (Full-buffer condition)
  No downlink traffic
MCS selection
  Goodput maximizing MCS based on SINR by training[4]
CCA-SD control algorithm
  DSC : Beacon RSSI based algorithm[3]
TxPower control algorithm
  DSC-linked control
BSS Coloring mechanism[5]
  Enabled. (at AP and AX STAs)
Parameters
  DSC-margin and TPC-alpha
See backup slide for details
30m
10m

## Slide 12: DSC performance (w/o TPC)
Low CCA-SD High
System throughput can be improved as DSC margin decreases.
DSC also causes legacy unfairness.
BSS
total
throughput
Per
STA
throughput
(No DSC/Color)
(No DSC/Color)
The performances with TPC for
margin=35, 40
are shown in next slide.

## Slide 13: DSC performance (w/ TPC)
TPC coupled to DSC can recover fairness for Legacy STAs in return for decreasing certain system gain.
BSS
total
throughput
Per
Legacy STA
throughput
(ave.)
High TxPower Low
Original
performance
Original
performance
Increasing system gain and maintaining the fairness for Legacy STAs can be satisfied simultaneously by selecting appropriate M and α.
(e.g. M=40dB, α=5~10dB)
Remaining gain
Recovering
fairness
* When DSC margin M < 35, system gain disappears when legacy fairness is recovered in this condition.
[NOTE] M in the graph represents the margin value of DSC.

## Slide 14: Conclusion
TPC coupled to DSC is considered and evaluated as a solution for recovering legacy fairness.
  Increasing system gain and maintaining the fairness can be satisfied simultaneously in SS3 by selecting appropriate TPC and DSC parameters.
Next steps
  Further optimization of DSC/TPC control algorithm
  Evaluation of other penalty method coupled to DSC but TPC (e.g. EDCA parameter)

## Slide 15: References
Lei Wang, Marvell, 11-14-1009-02-00ax-proposed-802-11ax-functional-requirements
Masahito Mori, Sony, 11-14-1403-00-00ax-Performance Analysis of BSS Color and DSC
Graham Smith, DSP Group, 11-13-1290-01 Dynamic Sensitivity Control for HEW
Gwen Barriac, Qualcomm, 11-14-0851-02-00ax-rate-control-for-mac-and-integrated-system-simulations
Matthew Fischer, Broadcom, 11-13-1207-01-00ah-partial-aid-color-bits
William Carney, Sony, 11-14-0854-00-00ax-dsc-and-legacy-coexistence

## Slide 16: Appendix

## Slide 17: Simulation Setup details
Node | (AP x 1, STA x 10) x 19 (Half of STAs are AX STA, and others are Legacy STA)
Num of Drops [times] | 5
Traffic Model & Load & Duration | Uplink CBR UDP 30Mbps (from all STA -> Full Buffer condition), 20sec
Access Category | AC_BE CWmin=15, CWmax=1023, AIFSN=3, TXOP limit=0
Tx Power [dBm] | AP: +23, AX STA: Variable by TPC, Legacy STA: +15
MCS Selection | Goodput maximizing MCS based on Training (MCS0 ~ 7) [4]
Packet Length [byte] | (MPDU, MSDU, APP)=(1030, 1000, 972) Fixed
L2 Retry | 10
Ack Rate | Legacy 6.0Mbps
RTS/CTS | OFF
Max Aggregation Size | (A-MPDU, A-MSDU)=(8KB, NA)
NF [dB] | 7
Channel | TGn Channel D (pathloss, shadowing, fading)
Channel Setting [MHz] | (CenterFreq, BW)=(2412, 20)
CCA-SD [dBm] | AP: -82, AX STA: Variable by DSC[3], Legacy STA: -82
CCA-ED [dBm] | -62 [NOTE] The term “CCA-ED” represents “20 dB above the minimum modulation and coding rate sensitivity” in this material.
Det. Cancel on PLCP err | Enable (Error performance is shown in slide#18)
DSC / TPC algorithm | See slide #4 and #5
BSS COLOR operation | AP and AX STA can handle COLOR information. (adding/filtering) STAs cannot filter packets that has no COLOR information (i.e. flow from Legacy STAs).

## Slide 18: Simulation Setup details

## Slide 19: DSC performance (w/o TPC, 5%tile)
Low CCA-SD High
All STAs
AX/Legacy
STAs
(No DSC/Color)
(No DSC/Color)

## Slide 20: DSC performance (w/ TPC, 5%tile)
High TxPower Low
Original
performance
Original
performance
[NOTE] M in the graph represents the margin value of DSC.
All STAs
Legacy
STAs