## Slide 1: Framework for NG60 Channel Bonding
Authors:
Name | Affiliation | Address | Phone | Email
Alireza Tarighat | Broadcom |  |  | atarighat@broadcom.com
Payam Torab | Broadcom |  |  | ptorab@broadcom.com
Brima Ibrahim | Broadcom |  |  | brima@broadcom.com

## Slide 2: Contents
Channel bonding options in NG60
Implementation variations
Key comparison metrics
Summary

## Slide 3: Channel Bonding Options
0.88GHz
0Hz
2.16GHz
1.28GHz
0.4GHz
1x 11ad channel
fchip= 1.76Gsps
3.92GHz
2.2x contiguous
One contiguous 3.92GHz channel
fchip = 3.92Gsps
3.52GHz
2x contiguous
One contiguous 3.52GHz channel
fchip = 3.52Gsps
0.88GHz
0Hz
2.16GHz
1.28GHz
0.4GHz
2x aggregation
Frequency carrier aggregation
fchip = 1.76Gsps
*Only payload spectrum shown.

## Slide 4: Channel Bonding Implementations (1/2)
Single-Stream 2x-Wide RF
3.92GHz
Single-Stream 2X Wide RF
0Hz
2.16GHz
0.4GHz
2.2x contiguous
2x aggregation

## Slide 5: Channel Bonding Implementations (2/2)
Two-Stream 1x-Wide RF
0Hz
2.16Hz
Two-Stream 1x-Wide RF
0Hz
2.16Hz

## Slide 6: Key Comparison Metrics (1/2)
Bandwidth utilization
  2.2x contiguous achieves 10% higher throughput than 2x contiguous and 2x aggregation
Power density (translating to range)
  Single-stream RF: 2.2x contiguous provides better power density that 2x aggregation
  Two-stream RF: 2x aggregation provides better power density than 2.2x contiguous
RF/analog design effort
  Contiguous 2.2x requires faster converters and tighter RF impairments (flatness, IQ imbalances)
RF power consumption
  Single-stream RF consumes less current than two-stream RF
Channel sensing
  2x aggregation allows for simultaneous sensing and detection of two legacy 11ad channels

## Slide 7: Key Comparison Metrics (2/2)
Digital design effort
  Same 11ad digital blocks can be reused for 2x aggregation
  2.2x contiguous requires additional modem development
Digital power consumption
  All digital filters
    2x aggregation draws 2x current vs single 11ad
    2.2x contiguous draws >3x current vs single 11ad
  Others (to be analyzed)
Frequency dispersion in beam pattern gain @ channel edge
  Wider channel leads to more severe frequency dispersion with single-stream RF.
  2.2x contiguous could suffer ~2.5dB in link budget at channel edge compared to 2x aggregation (32 elements). Loss worsens rapidly with number of elements.
Packet frame design
  2.2x contiguous will require new format design
  Maintaining legacy STF/CE may require higher backoff (diminishing backoff advantage in single-stream RF implementation)

## Slide 8: Summary
We propose enabling 2x carrier aggregation mode in NG60, given its advantages with some RF implementations.
  Mandatory vs. optional to be discussed.
  Overhead to spec is minimal as this will be a subset (reuse) of 2x2 MIMO spatial aggregation mode.
  Beneficial to outdoor and backhaul usages.
  Same standard framework and HW designed and deployed for 2x2 MIMO can be used in this mode.
We propose enabling 2.2x or 2x contiguous mode as it is beneficial to some usages and implementations.
  Mandatory vs. optional to be discussed.
  Beneficial to short-range, CE, and low cost/power usages.
2x carrier aggregation enables noncontiguous channel bonding.
2x carrier aggregation can enable both SC and OFDM modes (no change to OFDM parameters or FFT size).