## Slide 1: Encoding for control PHY
Date: 2015-03-11
Authors:
Name | Affiliations | Address | Phone | Email
Liguang Li | ZTE Corporation | Shenzhen China |  | li.liguang9@zte.com.cn
Jun Xu | ZTE Corporation | Shenzhen China |  | xu.jun@zte.com.cn
Ke Yao | ZTE Corporation | Xi’an China |  | yao.ke5@zte.com.cn
Kaibo Tian | ZTE Corporation | Xi’an China |  | Tian,kaibo@zte.com.cn
Sun Bo | ZTE Corporation | Xi’an China |  | Sun.bo1@zte.com.cn
Shiwen HE | Southeast University (SEU) | Nanjing China |  | hesw01@seu.edu.cn
Haiming WANG | Southeast University (SEU) | Nanjing China |  | hmwang@seu.edu.cn

## Slide 2
Encoding scheme for DMG control PHY in 11ad spec
  Including header field (40 bits) and data field in DMG control PHY.
  Using rate ¾ LDPC parity check matrix with shortening, modulation of DBPSK, and spread 32 times.
  Improving transmission performance and coverage.
  Still some room for performance improvement.
New encoding scheme
  We propose a new encoding scheme, which has better transmission performance.
Background

## Slide 3
Introduction
Control PHY frame
  Header and Data
  Header with length of 40 bits, Data with variable length.
  Encoding scheme include: encoding of Header, encoding of Data.

## Slide 4
Encoding scheme
Encoding of Header
  1. The Header(40 bits) is padded with zeros to create 42 bits, and repeated once, such as .
  2. The repeated data block is padded with 252 zero bits to create 336 bits, and added with parity bits to create LDPC codeword , , such that . H is the rate 1/2 LDPC parity check matrix[2].
  3. The basic code is , then copy the basic code -1 times to create bits of header encoding block, wherein

## Slide 5: Encoding of Header

## Slide 6
Encoding scheme
Encoding of Data
  1. is the maximal number of data bits in each LDPC codeword. The number of LDPC codeword is calculated:
  2. The Data is broken into blocks of data word. The length of the first blocks is , the length of the last blocks is . Wherein
  is smallest integer which larger than or equal to real number . is modulus operation.

## Slide 7
Encoding scheme
Encoding of Data
  3. Each data word is added with 8 bits CRC sequence, then padded with zero bits to create 336 bits . Wherein, is mth data word before added CRC, is the length of mth data word after added CRC, .
  4. For each data word, 336 parity bits are added to create the LDPC codeword , such that . H is the rate 1/2 LDPC parity check matrix[2].

## Slide 8
Encoding scheme
Encoding of Data
  5. All the same index bits of the LDPC codeword are encoded of XOR to create 672 bits parity data word. That is,
  6. The zero padding bits are removed from all the LDPC codeword, then each LDPC codeword is duplicated times. Remove the padding-bit-generated bits from parity data word , then copy times, where, the padding-bit-generated bits are all generated from the zero padding bits. Wherein,

## Slide 9: Encoding of Data

## Slide 10
Encoding scheme
  Control PHY encoding data
  Combine Header encoding block with Data encoding block.
  Analysis
  Header encoding：the valid data bits of LDPC is repeated once, which relative to merging 2 columns into 1 column of LDPC parity check matrix and the matrix has more column weight. Better performance should be get.
  Data encoding：the XOR encoder turns all the LDPC codeword into a big codeword, which improve the decoder performance.

## Slide 11
Simulation
  Performance
  Header field with 5 bytes (40 bits), Data field with 410 bytes (3280 bits) and 512 bytes (4096 bits), simulation in AWGN, BPSK.

## Slide 12: Conclusion
  We proposed a new encoding process for control PHY.
The proposed encoding scheme has better performance than 11ad.

## Slide 13: References
[1]. IEEE Std 802.11ad
[2]. LDPC Coding for 45GHz(11-14-0807-01-00aj). Proposal of IEEE802.11aj(45G).