## Slide 1: Empirical Measurements of Channel Degradation Under Load
Date: 2015-03-09
Authors:

## Slide 2: Abstract
We previously reported open air multi-client throughput data for 50x1SS, 50x2SS and 50x3SS STAs (14/1513r0)
This contribution presents results for 100x1SS, 100x2SS and 100x3SS STAs in VHT20 and HT40 channels
We are reporting significant throughput degradation beyond 25 simultaneously contending STAs
The idea of “contention premium” is introduced and defined
The underlying mechanism is analyzed via pcaps. It affects both HT and VHT from different radio and client OS vendors.
We conclude that with current MAC, spectral efficiency is inversely proportional to active STAs in BSS. Simulators need to be updated.
MAC efficiency improvements may yield another path to achieving PAR requirement of 4X throughput increase
There are important implications for LAA fairness

## Slide 3: Testbed Configuration
Clients:
  Smartphone, 11ac, 1SS, 100 stations
  Laptop, 11ac, 2SS, 100 stations
  Laptop, 11ac, 3SS, 100 stations
Controller & AP:
  7220-US controller running 6.4.2.3-HDMS public code.
  Aruba AP225 (11ac 3SS)
LAN:
  Jumbo frames enabled. [BE] queue. Full buffer traffic.
Test Automation:
  IxChariot 8.1EA. Separate, dedicated machines for console and wired endpoint.
RF configuration:
  Channels - 100E (VHT80), 100+ (VHT40), 100 (VHT20).
  Exclusive use of 5490 - 5570MHz / swept daily.
essid "HDTest-5"
a-basic-rates 24
a-tx-rates 18 24 36 48 54
a-beacon-rate 24
max-tx-a-msdu-count-be 3

## Slide 4: VHT20 - 1SS, 2SS & 3SS (Aggregate - Mbps)
Chart: Clients
| 1 | 5 | 10 | 25 | 50 | 75 | 100
GS4 TCP Up | 60.7877 | 64.0295 | 63.8455 | 54.988 | 51.5021 | 34.3501 | 29.5186
GS4 TCP Bidirect | 51.4745 | 59.1183 | 61.1138 | 55.9066 | 49.9182 | 37.5516 | 34.6317
MBA TCP Up | 138.542 | 135.4546 | 140.0551 | 131.6118 | 104.0216 | 89.8765 | 56.9064
MBA TCP Bidirect | 142.8236 | 136.4111 | 130.4939 | 127.4971 | 99.3063 | 72.1534 | 51
MBP TCP Up | 220 | 201 | 208.2605 | 195.8364 | 155.651 | 110 | 84.2704
MBP TCP Bidirect | 213.0255 | 203.6975 | 199.2613 | 188.968 | 158.2689 | 118.1444 | 77.8739
Significant drop >25 STAs
1SS Phone Up
1SS Phone Bidirect
2SS Laptop Up
2SS Laptop Bidirect
3SS Laptop Up
3SS Laptop Bidirect
TCP Up, VHT20, AP Radio Vendor A

## Slide 5: VHT20 - 1SS, 2SS & 3SS (Per STA - Mbps)
Chart: Clients
| 10 | 25 | 50 | 75 | 100
GS4_VHT20_TCP Up | 6.3845 | 2.1995 | 1.03 | 0.458 | 0.29519
GS4_VHT20_TCP Bidirect | 6.1114 | 2.2363 | 0.99836 | 0.50069 | 0.34632
MBA_VHT20_TCP Up | 14 | 5.1 | 1.98 | 1.2 | 0.45
MBA_VHT20_TCP Bidirect | 13.049 | 5.09 | 1.98 | 0.962 | 0.4
MBP_VHT20_TCP Up | 20.8261 | 7.8335 | 3.113 | 1.3624 | 0.8427
MBP_VHT20_TCP Bidirect | 19.9261 | 7.5587 | 3.1654 | 1.5753 | 0.77874
1SS Phone Up
1SS Phone Bidirect
2SS Laptop Up
2SS Laptop Bidirect
3SS Laptop Up
3SS Laptop Bidirect
30 Mbps
TCP Up, VHT20, AP Radio Vendor A
Per-STA drop steady across STA range

## Slide 6: MIMO Works! (Aggregate, normalized to %3SS STA)
Chart: Clients
| 1 | 5 | 10 | 25 | 50 | 75 | 100
GS4 TCP Up | 0.27631 | 0.31855 | 0.30657 | 0.28079 | 0.33088 | 0.31227 | 0.35028
GS4 TCP Bidirect | 0.27227 | 0.29023 | 0.3067 | 0.29585 | 0.3154 | 0.31785 | 0.39808
MBA TCP Up | 0.62974 | 0.6739 | 0.6725 | 0.67205 | 0.6683 | 0.75 | 0.67528
MBA TCP Bidirect | 0.67045 | 0.66968 | 0.65489 | 0.6747 | 0.62745 | 0.61072 | 0.65491
MBP TCP Up | 1 | 1 | 1 | 1 | 1 | 1 | 1
MBP TCP Bidirect | 1 | 1 | 1 | 1 | 1 | 1 | 1
Normalized to
3SS = 1
2SS is about 66% across the range
1SS is about 33% across the range
1SS Phone Up
1SS Phone Bidirect
2SS Laptop Up
2SS Laptop Bidirect
3SS Laptop Up
3SS Laptop Bidirect
TCP Up, VHT20, AP Radio Vendor A

## Slide 7: Contention Premium (Normalized to %1 STA)
Chart: Clients
| 1 | 5 | 10 | 25 | 50 | 75 | 100
GS4 TCP Up | 1 | 1.0542 | 1.0512 | 0.90619 | 0.84819 | 0.5665 | 0.48579
GS4 TCP Bidirect | 1 | 1.0193 | 1.0537 | 0.96391 | 0.86066 | 0.64744 | 0.53448
MBA TCP Up | 1 | 0.97789 | 1.0109 | 0.95 | 0.75105 | 0.64895 | 0.41048
MBA TCP Bidirect | 1 | 0.95511 | 0.91369 | 0.89269 | 0.69533 | 0.50525 | 0.35709
MBP TCP Up | 1 | 0.91364 | 0.94664 | 0.89017 | 0.7075 | 0.5 | 0.38305
MBP TCP Bidirect | 1 | 0.95639 | 0.93591 | 0.88737 | 0.74322 | 0.55485 | 0.36557
5% - 10% contention premium
30% - 50%
50% -
60%
10% - 30%
“Contention premium” is the delta between aggregate goodput
for 1 STA as compared with a larger number of STAs.
TCP Up, VHT20, AP Radio Vendor A
1SS Phone Up
1SS Phone Bidirect
2SS Laptop Up
2SS Laptop Bidirect
3SS Laptop Up
3SS Laptop Bidirect

## Slide 8: Effect Continues Past 100 STAs & Affects UDP
Chart: Clients
| 1+1 | 5+5 | 10+10 | 25+25 | 50+50 | 75+75 | 100+100
TCP_with_new pair count Down | 349.9034 | 364.0165 | 308.8517 | 217.3559 | 156.2859 | 60.1416
200STA UDP 2.0X Down | 457.5447 | 468.5392 | 384.7048 | 271.6842 | 188.5053 | 114.95 | 47.9407
TCP_with_new pair count Up | 401.063 | 355.742 | 310.1154 | 274.9911 | 177.1156 | 72.1643
200STA UDP 2.0X Up | 583.4726 | 474.6825 | 410.8129 | 292.9265 | 210.0317 | 103.6113 | 50.2723
UDP & TCP, VHT80, AP Radio Vendor A
50% 1SS Phone +
50% 2SS Laptop
VHT80!
TCP Down
UDP Down
TCP Up
UDP Up

## Slide 9: Retries Are Normal (<10%) and Steady
Chart: 
| 1 | 25 | 50 | 75 | 100
Retry Packets | 35408 | 17239 | 10448 | 12618 | 15992
Non-Retry | 426866 | 456522 | 428051 | 412116 | 374106
2SS Laptop, TCP Up, VHT20, AP Radio Vendor A
Chart: 
| 1 | 30 | 50 | 75 | 100
Retry Packets | 20793 | 39549 | 32477 | 26519 | 26719
Non-Retry | 402463 | 385144 | 398879 | 399644 | 404677
2SS Laptop, TCP Down, HT40, AP Radio Vendor B
Retries are well under 10% of frames
They do not grow
Same behavior with 802.11n AP, different channel width, different direction, different radio manufacturer

## Slide 10: Rate Adaptation Is Normal
Chart: Frames (#)
| 1 | 25 | 50 | 75 | 100
6 Mbps | 149 | 140 | 172 | 106 | 77
12 Mbps | 3261 | 6155 | 9252 | 13987 | 16754
18 Mbps | 3453 | 6758 | 10692 | 16990 | 21182
24 Mbps | 25516 | 42348 | 62174 | 62123 | 68853
39 Mbps | 73 | 107 | 114 | 118 | 117
72 Mbps | 1100 | 906 | 1112 | 820 | 893
78 Mbps | 1058 | 4730 | 7021 | 10311 | 7093
86.5 Mbps | 640 | 474 | 720 | 802 | 1497
104 Mbps | 0 | 0 | 0 | 0 | 0
115.5 Mbps | 0 | 0 | 0 | 0 | 1496
117 Mbps | 1 | 0 | 0 | 0 | 1
130 Mbps | 0 | 2857 | 2940 | 2969 | 1921
Rate adaptation on data frames
NDPs @ 18Mbps
Acks @ 12Mbps
TCP Up, VHT20, AP Radio Vendor A

## Slide 11: Control Frame Growth Is Key Factor
Chart: 
| 1 | 30 | 50 | 75 | 100
Mgmt Packets | 287 | 255 | 266 | 284 | 304
Ctrl Packets | 37118 | 64051 | 72741 | 81445 | 96752
NDP Packets | 306 | 456 | 1246 | 1142 | 1875
CRC Errors | 138 | 3500 | 3861 | 3470 | 3968
Data Packets | 383080 | 348618 | 339766 | 332142 | 314699
Chart: Frames (#)
| 1 | 25 | 50 | 75 | 100
Mgmt Packets | 260 | 260 | 233 | 246 | 234
Ctrl Packets | 28286 | 47517 | 70043 | 74484 | 84231
NDP Packets | 3130 | 6237 | 9448 | 14607 | 17639
CRC Errors | 2096 | 2736 | 4052 | 4768 | 5532
Data Packets | 430598 | 419747 | 358775 | 335397 | 287994
2SS Laptop, TCP Up, VHT20, AP Radio Vendor A
2SS Laptop, TCP Down, HT40, AP Radio Vendor B
Change silicon, PHY, channel width, direction
Data frames drop by 34%
Control frames increase 3X
Control frames increase 2.6X
PS NDP frames increase 5X

## Slide 12: Elevated Power Save Activity (3ms, 16 PS events)
16 STAs attempt PS state in 3.1 ms;
13 succeed

## Slide 13: Average Frame Size Decreases With Load
Chart: Frames (#)
| 1 | 25 | 50 | 75 | 100
<64 | 32061 | 55107 | 82014 | 92934 | 106594
64-127 | 133789 | 145452 | 125347 | 118598 | 101949
128-255 | 347 | 256 | 215 | 255 | 217
256-511 | 289 | 8 | 37 | 7 | 51
512-1023 | 456 | 0 | 4 | 1 | 177
1024-2047 | 297428 | 275674 | 234934 | 217707 | 186642
2048-2346 | 0 | 0 | 0 | 0 | 0
>=2347 | 0 | 0 | 0 | 0 | 0
2SS Laptop, TCP Up, VHT20, Radio Vendor A
TCP Data
TCP Ack
Control Frames
Chart: Frames (#)
| 1 | 25 | 50 | 75 | 100
<64 | 32061 | 55107 | 82014 | 92934 | 106594
64-127 | 133789 | 145452 | 125347 | 118598 | 101949
128-255 | 347 | 256 | 215 | 255 | 217
256-511 | 289 | 8 | 37 | 7 | 51
512-1023 | 456 | 0 | 4 | 1 | 177
1024-2047 | 297428 | 275674 | 234934 | 217707 | 186642
2048-2346 | 0 | 0 | 0 | 0 | 0
>=2347 | 0 | 0 | 0 | 0 | 0

## Slide 14: Control Frame Growth Explained
Chart: 
| 1 | 25 | 50 | 75 | 100
NDP | 3130 | 6237 | 9448 | 14607 | 17639
Request to Send | 7124 | 12385 | 19088 | 20548 | 25098
Clear to Send | 6567 | 11996 | 18023 | 17170 | 17045
Block ACK | 11308 | 16968 | 21661 | 20760 | 20312
Acknowledgment | 3286 | 6168 | 9246 | 13957 | 16614
Block Ack Request | 1 | 0 | 25 | 49 | 162
802.11 Control | 0 | 0 | 0 | 0 | 0
Chart: Frames (#)
| 1 | 25 | 50 | 75 | 100
NDP | 3130 | 6237 | 9448 | 14607 | 17639
RTS | 7124 | 12385 | 19088 | 20548 | 25098
CTS | 6567 | 11996 | 18023 | 17170 | 17045
BA | 11308 | 16968 | 21661 | 20760 | 20312
Ack | 3286 | 6168 | 9246 | 13957 | 16614
BAR | 1 | 0 | 25 | 49 | 162
802.11 Control | 0 | 0 | 0 | 0 | 0
2SS Laptop, TCP Up, VHT20, AP Radio Vendor A
TXOPs increase by 300% over the range
ACKs are for NDPs. Combined total grows from 6.4K  34.2K
NDP
RTS
CTS
BA
Ack
Preceded by SIFS (16usec)
Preceded by full arbitration (43usec AIFS + EDCA CW)

## Slide 15: Same Result Seen With HT on 11n Hardware
Chart: 
| 1 | 30 | 50 | 75 | 100
NDP | 306 | 456 | 1246 | 1142 | 1875
RTS | 8176 | 18558 | 21192 | 24384 | 28752
802.11 Data
CTS | 8107 | 18414 | 20399 | 23190 | 27129
802.11 QoS Data
802.11 QoS Null Data
SNAP
802.11 Control
BA | 20369 | 26207 | 29491 | 32368 | 38452
Ack | 466 | 864 | 1646 | 1502 | 2418
Block Ack Request
802.11 Management
Chart: 
| 1 | 30 | 50 | 75 | 100
NDP | 306 | 456 | 1246 | 1142 | 1875
RTS | 8176 | 18558 | 21192 | 24384 | 28752
802.11 Data
CTS | 8107 | 18414 | 20399 | 23190 | 27129
802.11 QoS Data
BA | 20369 | 26207 | 29491 | 32368 | 38452
802.11 QoS Null Data
SNAP
802.11 Control
Ack | 466 | 864 | 1646 | 1502 | 2418
Block Ack Request
802.11 Management
2SS Laptop, TCP Down, HT40, AP Radio Vendor B
TXOPs increase from 12.2K to 31.4K
PS NDP frames increase 5.6X

## Slide 16: Average Burst Size Is Decreasing
Chart: Data Packet & TXOP Count
| 1 | 25 | 50 | 75 | 100
Data Packets | 430598 | 419747 | 358775 | 335397 | 287994
TXOPs | 8333 | 13783 | 19590.6667 | 19492.6667 | 20818.3333
MPDUs/TXOP | 51.6738 | 30.454 | 18.3136 | 17.2063 | 13.8337
2SS Laptop, TCP Up, VHT20, AP Radio Vendor A
2SS Laptop, TCP Down, HT40, AP Radio Vendor B
Chart: Data Packet & TXOP Count
| 1 | 25 | 50 | 75 | 100
Data Packets | 383080 | 348618 | 339766 | 332142 | 314699
TXOPs | 8141.5 | 18486 | 20795.5 | 23787 | 27940.5
MPDUs/TXOP | 47.0528 | 18.8585 | 16.3384 | 13.9632 | 11.2632
Drops from 45.9 to 115.12
Drops from 47.0 to 11.2

## Slide 17: Contention Premium Summary
Principal mechanism behind the contention premium is MAC layer overhead growing with STA count.
  Decreased A-MPDU packing efficiency
  More TXOPs required to move a given amount of payload
  Airtime efficiency of each TXOP decreases
  Power save NDP/Ack growth due to elevated TXOP activity level
  Amount of time channel spends in arbitration increases
Channel is working harder and harder to move less data
It is an emergent property of 802.11 system implementations
  We hypothesize that the combination of OS, network stack and radio driver implementations on both sides of link leads to this result

## Slide 18: Practical Effects – STAs Per Channel
Contention premium penalty implies that narrower bandwidths (more collision domains) will yield more goodput than wider bandwidths.
Hypothesis was tested and found to be correct.
Each test uses the exact same 80-MHz bandwidth
Each test uses the exact same number of STAs
Both VHT40 BSS will victimize each other with ACI
All four VHT20 BSS will victimize each other

## Slide 19: 80 vs. 40 vs 20 Result (1SS STAs)
Chart: Clients
| 5 | 10 | 25 | 50 | 75 | 100
VHT20x4 Up | 258.0779 | 260.5192 | 252.5646 | 252.6858 | 237.1007 | 228.4046
VHT20x4 Bidirect | 210.9617 | 237.2655 | 236.1488 | 224.2094 | 216.4298 | 203.2414
VHT40x2 Up | 264.1786 | 266.9808 | 257.4673 | 250.7424 | 224.7548 | 179.6216
VHT40x2 Bidirect | 236.4282 | 237.1528 | 229.0685 | 223.1573 | 197.938 | 165.9937
VHT80x1 Up | 272.1902 | 252.3377 | 223.7668 | 171.6998 | 98.1671 | 79.6821
VHT80x1 Bidirect | 188.5019 | 211.4722 | 196.8401 | 162.4567 | 131.7873 | 80.4471
Contention premium for 100 STAs/channel is 50-60%
C.P. for 50 STAs per channel is 10-30%
C.P. for 25 STAs per channel is just 5-10%
2SS Laptop, TCP Up, VHT, Radio Vendor A

## Slide 20: Analysis
11ac MAC spectral efficiency is inversely proportional to the number of STAs contending for the medium
Wide channels are inherently less efficient for a given number of STAs, even with full buffer traffic. It is better to spread over more collision domains.
  This significantly dilutes a key supposed benefit of 802.11ac
The expected benefits of A-MPDU are greatly diminished in high density, high duty-cycle conditions
Full buffer traffic likely overstates channel efficiency as it is not principal traffic type [2] [3] [4]
  Our results are best case because some level of aggregation is still occurring. This may not be true of routine end user traffic types.

## Slide 21: Implications
Recovering capacity lost due to the contention premium effect is another route to 4X area throughput increase!
Existing TGax Box3 simulators pushing full buffer traffic are incomplete
  Small STA counts are less impaired than large STA counts
  PS transition rate is important to channel availability and should be modeled as proportional to offered load
Current 802.11 MAC makes vital assumptions about STA & AP operation and scalability that may not be true (9.13)
LAA fairness mechanism based on channel sensing will become less and less fair as STA count increases

## Slide 22: Questions
What is an acceptable contention premium value at high STA counts in a well-ordered channel?
  20% seems like a good target @ 100 STAs versus 60%
If aggregate client stack latency is materially diluting 802.11 spectral efficiency, is it even possible to tweak the the existing MAC to mitigate?
If large bursts of larger frames are not significant in many deployed networks due to structural issues, should a new HE-MAC be optimized for that instead?

## Slide 23: Next Steps
Continue investigation
  Explain average A-MPDU packing decrease
  Evaluate smaller frame sizes & less aggressive arrival distributions
Assessing optimal resource block width
  Methodology & data for optimal channel bandwidth for typical frame size distributions.
Develop validated traffic models for SS use cases – enterprise, residential, LPV/stadia, outdoor
  Must factor frame size distribution and burst size distribution
  Also by network usage mode – general browsing, cloud sync, social media update, video streaming, VDI, etc.

## Slide 24: References
[1] 14/1513r0 – “Empirical open-air VHT client scaling results for use in validating MAC simulators”, C Lukaszewski, L Liang (Aruba Networks) Nov, 2014
[2] 15/0343r0 - “In Situ Frame Size Measurements”, C Lukaszewski, L Liang (Aruba Networks) Mar, 2015
[3] “Anatomy of WiFi Access Traffic of Smartphones and Implications for Energy Saving Techniques”, International Journal of Energy, Information and Communication (IJEIC), 3(1):1-16. February, 2012.
[4] 14/1144r1, “Simplified Traffic Model Based On Aggregated Network Statistics”, W Carney, K Agardh et al (Sony, Ericsson), Sep 2013