## Slide 1
OFDMA Non-contiguous Channel Utilization
Date: 2015-03-09
Authors:

## Slide 2: Background
OFDMA is adopted as an 802.11ax transmission scheme[1]
OFDMA and channel utilization
  Various new patterns of channel utilization for OFDMA have been discussed [2][3]
    Contiguous flexible & non-contiguous
  Approaches in the past OFDMA related contributions
    Legacy channel utilization for STAs  Low complexity on STAs
    Extended channel utilization for AP
OFDMA channel utilization has not been fully discussed

## Slide 3: OFDMA Channelization
11ac channelization allows predetermined contiguous channel utilization on 5GHz band (except 80+80MHz)
11ax could enhance its performance via allowing new patterns of channel utilization
New options of wider bandwidth operation
  Contiguous flexible channel (e.g., 60MHz, 120MHz, etc)
  Non-contiguous channel (e.g., 20MHz+20MHz, 20MHz+40MHz, etc)
20MHz
40MHz
80MHz
Not allowed
Allowed
Allowed

## Slide 4: OFDMA Channelization (Contiguous)
Contiguous flexible channel [4]
  Better performance for target BSS than 11ac channel utilization
  Need to configure new sub-carrier allocation for new bandwidth
  Or multiple contiguous segments (e.g., contiguous 40+20MHz)
11ac 80MHz
11ax Contiguous 120 MHz
New 11ax 60MHz sub-carrier allocation
11ac 40MHz+11ac 20MHz sub-carrier allocation

## Slide 5: OFDMA Channelization (Non-contiguous)
Non-contiguous channel utilization [4][5][6][7][8]
  Much better performance for target BSS than 11ac channel utilization
Non-contiguous channel utilization might be preferable due to better spectral usage
  There are technical MAC & PHY issues
    e.g., Limitation on number of segments, Channel access schemes, etc.
11ac 40MHz
11ax Non-contiguous 120 MHz

## Slide 6: Non-contiguous channel utilization
Supporting non-contiguous channels
  Legacy 802.11(before ac) utilizes only one frequency segment of certain center frequency
    Frequency segment: a block of contiguous frequency bandwidth which has one center frequency
  802.11ac could utilize 2 frequency segments to utilize 80+80MHz bandwidth of different two center frequency
    VHT operation information element includes each center frequency of two segments
Segment 1
Segment 2

## Slide 7: Issues on Non-contiguous channel
PHY needs to handle non-contiguous bandwidth
  Multiple RF(or multiple IF part) may be required to support non-contiguous channels [5][6][7]
  Each frequency segment may require one IF [7]
  Synchronous non-contiguous channel utilization is feasible [5][6][7]
  Non-contiguous channel utilization could enhances 11ax throughput by increasing opportunity of wideband operation [4][7][8][9]
Digital Signal Process
DAC
DAC
IF
IF
RF
For Segment1
For Segment2

## Slide 8: Issues on Non-contiguous channel
Non-contiguous channel support with PHY restriction might be required
  Utilizing all available channel is burden to PHY and could degrade spectral reuse on dense OBSS scenario
  Therefore, restriction on numbers of segment need to be considered
    11ac considered 2 segments at most
    Complexity and AP/STA capability needs to be considered
Many legacy channel access schemes might be re-defined or enhanced for Non-contiguous channel
  STAs’ capability for non-contiguous channel support might vary
  CCA, contention and back-off and other channel access schemes might be required to be re-defined for non-contiguous channel

## Slide 9: Issues on Non-contiguous channel
Minimizing impacts on non-contiguous channel utilization
  Secondary non-contiguous segment(s) might require a new control channel(s)
  A new control channel utilizes same 11ax channel access schemes (CCA, wideband operation, etc.) as primary channel
  By utilizing new control channel(s) STA does not need to listen to all possible channels
Further performance enhancement with new control channel on non-contiguous segment
  Secondary non-contiguous segment can be utilized even when a primary channel is busy

## Slide 10: Issues on Non-contiguous channel
Resource utilization comparison [9]
  CH1 is Primary Channel
  CH3 is 2nd segment control channel
 | Channel (Colored means busy) |  |  |  | Legacy |  |  |  | All available CH |  |  |  | With 2nd segment control channel |  |  | 
 | CH1 | CH2 | CH3 | CH4 | CH1 | CH2 | CH3 | CH4 | CH1 | CH2 | CH3 | CH4 | CH1 | CH2 | CH3 | CH4
Case1 |  |  |  | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case2 |  |  | Busy |  |  |  |  |  |  |  |  |  |  |  |  | 
Case3 |  | Busy |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Case4 |  | Busy |  | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case5 |  |  | Busy | Busy |  |  |  |  |  |  |  |  |  |  |  | 
Case6 | Busy |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 11: Non-contiguous channel
Non-contiguous channel utilization enhances throughput
Channel usage (=0.7, Max BW = 160MHz)[9]
69%
39%
108%
52%
119%
39%

## Slide 12: Conclusions
Non-contiguous channel utilization may improve 11ax throughput
  All possible non-contiguous methods improve effective channel utilization
Frequency segment might be restricted by PHY capability
  If there are no restriction(using all available channel case), 4 non-contiguous segment need to be supported on 160MHz band
  Numerous frequency segments might not be feasible due to PHY limitations
Channel access schemes need to consider non-contiguous channel utilization
  Allocating control channel to additional frequency segments could be one of possible solutions

## Slide 13: References
[1] IEEE 802.11-15/0132r2 "Specification Framework for TGax"
[2] IEEE 802.11-13/1382r0 "Discussion on OFDMA in HEW"
[3] IEEE 802.11-15/0035r0 "Scalable Channel Utilization"
[4] IEEE 802.11-13/1058r0 "Efficient wider bandwidth operation"
[5] IEEE 802.11-09/1037r0 "Considerations on Multi-Channel in TGac"
[6] IEEE 802.11-09/1022r0 "Multi-channel Transmissions"
[7] IEEE 802.11-10/0103r1 "Gains provided by multichannel transmissions"
[8] IEEE 802.11-10/0385r1 "80MHz and 160MHz channel access modes"
[9] IEEE 802.11-15/0132r2 "DL-OFDMA Procedure in IEEE 802.11ax"

## Slide 14: Straw Poll 1
Do you agree to utilize non-contiguous channels in 802.11ax?
Y
N
ABS

## Slide 15: Straw Poll 2
Do you agree to restrict maximum number of segments (e.g., 2 or more)?
Y
N
ABS