## Slide 1: Numerology for 11ax
Date: 2015-03-09
Authors:

## Slide 2: Number of Available Tones
As an example in [1], number of available tones was discussed for 78.125kHz subcarrier spacing.
  It was shown that up to 230 subcarriers (excluding a single DC tone) can be used and power spectral mask can be met.

## Slide 3: Frequency Resource Allocation Granularity for OFDMA
Depending on the frequency resource granularity for OFDMA, e.g. 1.25 MHz, 2.5 MHz, etc, we will need to divide up 20/40/80/160 MHz into several bandwidth chunks.
  For example, support of 5 MHz resource granularity may require the total number of available tones in a OFDM symbol to be divisible by 4. Therefore, 230 tones should not be chosen for this case.
The following is a table of number of tones candidate in 20 MHz
# of Tones in 20 MHz | 1.25 MHz (divide by 16) | 2 MHz (divide by 10) | 2.5 MHz (divide by 8) | 4 MHz (divide by 5) | 5 MHz (divide by 4) | 10 MHz (divide by 2)
230 | NO | YES | NO | YES | NO | YES
228 | NO | NO | NO | NO | YES | YES
226 | NO | NO | NO | NO | NO | YES
224 | YES | NO | YES | NO | YES | YES
222 | NO | NO | NO | NO | NO | YES

## Slide 4: User Diversity Gain
Frequency selectivity gain simulations
  No MAC protocol overhead assumed (just pure comparison of user diversity gain)
  1 AP, and maximum of 8 STAs in OFDMA
  STAs are uniformly distributed in 25m / 250m radius
  Non-continuous resource allocation was allowed
Gain over 20MHz
10 MHz: 7.1%
5 MHz: 14.7%
2.5 MHz: 21.4%
1.25 MHz: 27.3%
Gain over 20MHz
10 MHz: 1.1%
5 MHz: 2.4%
2.5 MHz: 3.5%
1.25 MHz: 4.0%
ITU NLOS UMi
TGac D

## Slide 5: Number of DC Tones in 20MHz
Number of DC tones in the 12.8us OFDM symbols will depend on the residual frequency offset after CFO compensation from the preamble.
According to 11ac studies [2], residual CFO std. deviation is between 0.07 ~ 0.13 ppm (depending on the integrated phase noise assumption) in indoor channel models of the highest SNR regime.
Unless residual CFO is larger than ½ of the subcarrier spacing (i.e 7.8 ppm in 5GHz), a single DC tone should be sufficient.
  Note that this does not necessary mean we should only have 1 DC tone.
Further simulation check on outdoor environments and in low SNR regime will be needed to determine the number of DC tones.

## Slide 6: Proposed Numerology Baseline for 20 MHz
Choice of frequency resource granularity depends on
  signaling complexity/overhead
  system performance
    Granularity below 2.5 MHz is not necessary
Suggested Candidates for 20 MHz
  Option 1) 230 data/pilot tones + 1 DC tone + (12 + 13) Guard tones
  Option 2) 228 data/pilot tones + 1or 3 DC tone
    If 1 DC tone, (14 + 15) Guard tones
    If 3 DC tone, (12 + 13) Guard tones
  Option 3) 224 data/pilot tones + 1 or 3 DC tone
    If 1 DC tone, (15 + 16) Guard tones
    If 3 DC tone, (14 + 15) Guard tones

## Slide 7: Expansion to 40/80 MHz
Alternative 1
  Direct multiplication of 20 MHz
  No further optimization to use the guard subcarriers between bands
  Ease to scale sub-channel definitions for OFDMA
Alternative 2
    Optimized to use all available spectrum
    sub-channel definitions for OFDMA becomes complicated
20 MHz
20 MHz
40 MHz
Unused
Guard Band Gap:
Approximately 2 MHz of spectrum
5.6% of potential capacity for 40 MHz
8.3% of potential capacity for 80 MHz
40 MHz

## Slide 8: Example of Alternative 1 - based on option 3A (1 DC tone) -
56
56
+240
+16
Data + pilot 224
+496
+16
Data + pilot 448
+112
56
+1
-240
-16
-1
-16
-496
Data + pilot 112
Left Guard Tone 16
Left Guard Tone 15
-112
+240
-240
+272
-272
20MHz
40MHz
80MHz

## Slide 9: Example of Alternative 2 - based on option 3 -
60
62
+240
+1
Data + pilot 240
+496
+1
Data + pilot 496
+112
56
+1
-240
-1
-1
-1
-496
Data + pilot 112
Left Guard Tone 16
Left Guard Tone 15
-112
20MHz
40MHz
80MHz

## Slide 10: Numerology Baseline for 40/80 MHz
Maximum spectral efficiency gains for Alternative 2 is around 6% ~ 11%.
  Actual gains depends on the number of pilots vs data tones.
Although the gains are non-negligible. However, at the cost of complexity in designing OFDMA systems that can scale between 20 MHz ~ 160 MHz.

## Slide 11: Numerology for 160 MHz
Given that 11ac supports 80+80 MHz, where the 80 MHz chunks can be discontinuous in frequency, 11ax should also support 80+80 MHz operations.
To avoid numerous implementation options, we propose to 160 MHz numerology as two 80 MHz operations (same design method as in 11ac)
  This allows the use of the same power spectral mask definitions
160 MHz
80 MHz
80 MHz
DC Tones (not available for data)

## Slide 12: References
[1] Daewon Lee, et. al., “OFDM Numerology for 11ax” IEEE 802.11-15/0079r1
[2] Kai Shi, et. al., “Phase Tracking During VHT-LTF” IEEE 802.11-10/0771r1