## Slide 1
Preamble Auto-Detection in 802.11ax
Date: 2015-03-08
Authors:
Name | Affiliations | Address | Phone | email
Sungho Moon | NEWRACOM | 9008 Research Drive Irvine, CA 92618 | +1-949-390-7111 | aiden.m@newracom.com
Daewon Lee | NEWRACOM |  |  | 
Minho Cheong | NEWRACOM |  |  | 
Heejung Yu | Yeungnam Univ. Newracom |  |  | 

## Slide 2: Introduction
Preamble Auto-Detection for 11n and 11ac
  11n PPDUs have the unique modulation QBPSK in SIG-A1
  11ac PPDUs can be detected in the position of SIG-A2
    QBPSK in SIG-A2 can differentiate 11ac PPDUs with 11a’s
PPDU type | L-SIG | SIG-A1 | SIG-A2 | Data/STF/SIG-A3
11a | BPSK | Data | Data | Data
11n | BPSK | QBPSK | QBPSK | HT-STF
11ac | BPSK | BPSK | QBPSK | VHT-STF
11ax | BPSK | ? | ? | ?

## Slide 3: Design Constraints for HE Auto-Detection
HE PPDUs should not affect any to previous 11a, 11n, and 11ac devices
HE device should detect 11ax PPDU with a reasonable detection probability
HE devices should detect types of PPDU before receiving STF (be ready for AGC).
  At the very least do not require too much buffering for AGC tuning.

## Slide 4: HE SIG-A Modulation for Auto-Detection
Basic assumption
  More priority to use BPSK and QBPSK considering Euclidean distance with existing SIG-A modulations
  Other types of modulations such as 45 degree I/Q can be utilized as a second priority if there is no choice in the BPSK/QBPSK combinations
Therefore, for each symbol position of HE SIG-A
  HE SIG-A1 and SIG-A2 can be BPSK and BPSK, respectively or QBPSK and BPSK unless it increases the false-detection probability for 11n devices
  If three or more symbols of HE SIG-A is agreed, QBPSK could be a better choice for the third HE SIG-A symbols as it does not overlap with STF modulation or Data modulations.

## Slide 5: HE SIG-A Candidates
Option 1: (BPSK, BPSK, QBPSK)
  There might be less impact on the detection in 11n devices since the uniqueness of QBPSK is maintained in the first symbol
  11ax devices can prepare for 11n or 11ac AGC because non-11ax PPDU can be determined during the second SIG-A symbol position
Option 2: (QBPSK, BPSK, QBPSK)
  QBPSK and BPSK in the first and second SIG-A symbols are exclusive to other modulations
  If two symbols of HE SIG-A considered, (QBPSK, BPSK) can be used without the third QBPSK

## Slide 6: Simulation Environment
Wireless channel
  TGac D and ITU UMa channels (for outdoor)
System parameters
  PPDU format : 11ax with Option 1(B, B, Q) and with Option 2(Q, B, Q)
  I/Q decision algorithm : Accumulated energy in I- and Q-axis
  PPDU format detection algorithm : ‘Symbol-by-Symbol’ and ‘Joint’
Performance metrics
  Miss-detection probability in 11ax devices
  False detection probability in 11a, 11n, and 11ac devices
    False detection only occurs if the wrong PPDU format is detected and SIG CRC passes based on the detected PPDU format.

## Slide 7: Mis-Detection & SIG-A Performance
Observations
  Both options have comparable performance with 11ac

## Slide 8: False Detection in 11ax Devices
Observation
  For both detection algorithms, i.e., symbol-by-symbol and joint, reliable false detection probabilities are maintained

## Slide 9: Mis- and False Detections in Outdoor Environments
Observations
  In the outdoor environment, no problem has been seen in our simulation results

## Slide 10: False Detection in 11n Devices
Observation
  If 11n device detects 11n PPDUs in symbol-by-symbol, it results in false format detection of 11ax PPDU. This results in constant 0.4% false detection of 11n regardless of SNR, which is equivalent to the CRC false detection bound (1/28)
Note that 0.4% false detection of 11n may or may not be an issue. Further study on the impact of 11n false detection to system performance is needed.

## Slide 11: False Detection in 11ac Devices
Observation
  No degradation in false detection of 11ac PPDU, but the same problem can occur in 11n PPDU detection

## Slide 12: Conclusion
If three or more symbols for SIG-A is considered, (BPSK, BPSK, QBPSK) can be a reasonable option
  It shows a comparable mis-detection and false detection probabilities with 11ac in both indoor and outdoor environments
  There is no impact on the false detection probability in 11a, 11n, 11ac devices
The modulation starting from (QBPSK, BPSK, ~) can cause undefined operations in 11n devices due to a falsely detected SIG-A in 11n devices in approximately 0.4 % of the time.
  Note that in some cases, L-SIG length may provide the required medium access protection for falsely detected 11ax packets.
If two symbols for SIG-A is considered, further investigation on impact to system performance when false detection of 11ax as 11n is approximately 0.4% will be required.
  If significant problem are found with false detection, other types of auto-detection methods will be required to avoid the above problem

## Slide 13: References
[1] Il-Gu Lee, et. al., 802.11ac preamble for VHT auto-detection, 11-10/0359r0, March 2010.
[2] Hongyuan Zhang, et. al., TGac Preamble Auto-detection Comparisons, 11-10/0549r2, May 2010.
[3] Vish Ponnampalam, et. al., 11ac Auto-Detection Using the VHT-SIG-A Field, 11-10/0750r0, July 2010.
[4] Jaeyoung Song, et. al., Considerations on 11ax Auto-detection Methods, 11-14/0081r1, Jan. 2015.
[5] IEEE Std 802.11ac -2013