## Slide 1: MU Synchronization Requirements for SFD
Date: 2015-03-08
Authors:
Name | Affiliation | Address | Email
Yonggang Fang | ZTE |  | yfang@ztetx.com
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Ke Yao | ZTE |  | ke.yao@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn
Liu Yang | ZTE |  | yang.liu@zte.com.cn
Jiadong Du | CATR |  | dujiadong@catr.cn

## Slide 2: Abstract
The contribution [1] analyzed the impact on OFDM system performance due to residual errors of frequency and timing synchronization between AP and multiple STAs for features like UL OFDMA, UL MU MIMO and CSMA enhancement.
In order to control OFDM system performance, [1] suggests to define requirements of frequency and timing synchronization.
This contribution is to follow up that proposal and recommend to define synchronization requirements in IEEE 802.11 AX specification framework document.

## Slide 3: Overview of UL MU
Multi-User features have been suggested in SFD [2] in IEEE 802.11 San Antonio meeting.
So far some UL MU features [3][4][5] have been discussed in the 802.11 TGax, and recommended in 11ax SFD.
Since OFDM system is sensitive to synchronization error, the contribution [1] suggests to define requirements for frequency and timing synchronization error between AP and multiple STAs so as to keep residual error of synchronizations within a given threshold.

## Slide 4: Overview of UL MU
    Straw Poll Results in [1]
      Do you support to add the requirement about the residual error of frequency synchronization between the carrier frequency of STA and the carrier frequency received from the AP for UL OFDMA and UL MU MIMO?
        Result: 54/2/64
      Do you support to add the requirement about the transmit timing alignment with the symbol boundary of received frame from AP for UL OFDMA and UL MU MIMO?
        Result: 41/5/75

## Slide 5: Proposal - 1
We suggest to add the follow requirements in SFD
  Requirement of Carrier Frequency Accuracy
    For 5GHz band, the accuracy of transmit carrier frequency of STA (and AP) shall be within ±N1 ppm (TBD) for UL MU.
    For the 2.4GHz band, the accuracy of transmit carrier frequency of STA (and AP) shall be within ±N2 ppm (TBD) for UL MU.
  Motion-1
    Do you support to add in SFD the above frequency requirement for UL MU features?
    Move: Second:
    Y/N/A:

## Slide 6: Proposal - 2
We suggest to add following requirements in SFD
  Requirement of Carrier Frequency Synchronization
    For 5GHz band, the carrier frequency synchronization error between the carrier frequency of STA and the carrier frequency of signal received from the AP shall be within ±N3 ppm (TBD)
    For the 2.4GHz band, the carrier frequency synchronization error between the carrier frequency of STA and the carrier frequency of signal received from the AP shall be within ±N4 ppm (TBD)
  Motion-2
    Do you support to add in SFD the above frequency synchronization requirement for UL MU transmission?
    Move: Second:
    Y/N/A:

## Slide 7: Proposal - 3
We suggest to add the follow requirements in SFD
  Timing Synchronization Requirement
    The symbol timing synchronization between the transmit symbol boundary of STA and the received symbol boundary from the AP shall be aligned within M ns (TBD) for a given CP length.
  Motion-3
    Do you support to add in SFD the above timing requirement for UL MU transmission?
    Move: Second:
    Y/N/A:

## Slide 8: References
IEEE 802.11 11-14-0818-01-00ax-requirements-for-synchronization
IEEE 802.11 11-14-1453-02-00ax-spec-framework-proposal
IEEE 802.11 11-13-1388-00-0hew-ul-mu-transmission
IEEE 802.11 11-09-0852-00-00ac-ul-mu-mimo-for-11ac
IEEE 802.11 11-14-0616-00-00ax-CSMA-enhancement-suggestion