## Slide 1: Minimum Resource Granularity in OFDMA
Date: 2015-03-09
Authors:

## Slide 2: Introduction
IEEE 802.11 signal has always occupied at least 20MHz bandwidth. However, 11ax OFDMA may enable a STA to send a signal occupying a sub-band smaller than 20MHz.
For frequency selective scheduling gains, the optimal size of sub-band depends on the coherence bandwidth of the channel models [1][2]. The 2.5MHz sub-band outperformed 5MHz in outdoor channel models [1].
In this contribution, we discuss European regulation issues that may conflict with the utilization of < 5MHz sub-band.

## Slide 3: European requirements on 5GHz unlicensed
The European requirements on 5 GHz unlicensed spectrum deployment are specified in three ETSI harmonized standards [3][4][5].
EN 301 893 [3] applies to 5GHz RLAN equipment used in wireless local area networks in 5150~5350MHz and 5470~5725MHz.
It describes spectrum access requirements to facilitate spectrum sharing with other equipment.
EN 301 893(v1.7.1) was effective from June 2012, and the revised standard (currently draft v1.8.0) will be effective from June 2016 with mandatory compliance from June 2017 [6].

## Slide 4: Bandwidth Access Rules in EN 301 893 (draft v1.8.0) [3]
4.3 Nominal Channel Bandwidth and Occupied Channel Bandwidth
4.3.1 Definition
The Nominal Channel Bandwidth is the widest band of frequencies, inclusive of guard bands, assigned to a single channel.
The Occupied Channel Bandwidth is the bandwidth containing 99 % of the power of the signal. ...
4.3.2 Limits
The Nominal Channel Bandwidth shall be at least 5 MHz at all times.
The Occupied Channel Bandwidth shall be between 80 % and 100 % of the declared Nominal Channel Bandwidth. In case of smart antenna systems (devices with multiple transmit chains) each of the transmit chains shall meet this requirement.
During an established communication, the device is allowed to operate temporarily with an Occupied Channel Bandwidth below 80 % of its Nominal Channel Bandwidth with a minimum of 4 MHz.
Nominal CH BW a 802.11 STA’s operating CH BW (e.g. 20/40/80/160MHz in 11ac)
Occupied CH BW a PPDU’s occupying CH BW >=4MHz
 Therefore, a 802.11 STA shall not send a PPDU occupying less than 4MHz bandwidth.

## Slide 5: Possible options for utilization of < 5MHz Sub-band
If 11ax to utilize <5MHz Sub-band for OFDMA, the following options can be considered.
A. Distributed OFDMA
  Instead of localized subcarrier-based OFDMA, 11ax to adopt distributed subcarrier-based OFDMA.
B. Asymmetric Downlink/Uplink design
  Allow AP to utilize < 5MHz sub-band for downlink, while non-AP STAs to utilize >= 5MHz sub-band for uplink.
C. ETSI Regulation Modification
  Request ETSI TC BRAN to modify the EN 301 893 spec to allow operation with smaller Occupied CH BW.

## Slide 6: Option A. Distributed OFDMA
 | Localized OFDMA | Distributed OFDMA
DL OFDMA DATA TX |  | 
UL OFDMA DATA TX |  | 
STA1
AP
STA2
STA8
STA1
AP
STA2
STA8
STA’s Occupied CH BW=<5MHz (e.g., 2.5MHz)
AP’s Occupied CH BW=20MHz
STA’s Occupied CH BW≈20MHz
. . .
. . .
AP’s Occupied CH BW=20MHz
While Localized OFDMA assigns contiguous subcarriers to each STA, Distributed OFDMA assigns a set of distributed subcarriers to each STA.
11ax may choose the distributed OFDMA so that each STA’s Occupied CH BW spans the Nominal CH BW.
However, we need detailed analysis between two methods in terms of frequency selectivity/diversity gain and scheduling gain, etc.

## Slide 7: Option B. Asymmetric Downlink/Uplink design
Downlink (DL-OFDMA’s Data or UL-OFDMA’s Ack)
  AP can utilize < 5MHz sub-band for Data or Ack transmissions because the multiplexed sub-bands will occupy more than 4MHz
Uplink (DL-OFDMA’s Ack or UL-OFDMA’s Data)
  STAs should not use sub-band based Ack with < 5MHz sub-band among various Ack methods for DL-OFDMA [8][9].
  STAs should use sub-band size of >=4MHz for UL-OFDMA’s Data.
STA1
AP
STAn
...
...
STA1
AP
STAn
...
sub-band
Occupied BW>=4MHz
sub-band=Occupied BW>=4MHz
Downlink
DL-OFDMA’s Data or
UL-OFDMA’s Ack
UL-OFDMA’s Data or
DL-OFDMA’s Ack
Uplink
UL-OFDMA’s Data or
DL-OFDMA’s Ack

## Slide 8: Option C. ETSI Regulation Modification
In last year, 802.11 REG SC requested ETSI TC BRAN to modify the minimum size of the Occupied CH BW to accommodate 11ac’s 160MHz operations that may utilize 20MHz only. It is reflected in the current draft [6][7].
11ax should first decide the size of OFDMA sub-band. If the < 5MHz sub-band is adopted, 11ax need to propose a new work item (or modification request) to ETSI.
However, ETSI TC BRAN is under national voting for the final draft (v1.8.0) with the only remaining WI for LBT section harmonization [6].

## Slide 9: Conclusions
While minimum resource granularity with < 5MHz will provide higher scheduling gains in certain environments, less than 5MHz sub-band can not meet the current EU regulations on 5GHz unlicensed spectrums.
We briefly discussed possible options to utilize < 5MHz sub-band, and those options require further discussions in 11ax.

## Slide 10: References
[1] 11-14/1227r3, OFDMA Performance Analysis
[2] 11-14/1452r0, Frequency selective scheduling in OFDMA
[3] ETSI EN 301 893, Harmonized European Standard, “Broadband Radio Access Networks (BRAN); 5 GHz high performance RLAN”
[4] ETSI EN 302 502, Harmonized European Standard, “Broadband Radio Access Networks (BRAN); 5,8 GHz fixed broadband data transmitting systems”
[5] ETSI EN 302 571, Harmonized European Standard, “Intelligent Transport Systems (ITS); Radio communications equipment operating in the 5 855 MHz to 5 925 MHz frequency band”
[6] 11-15/0149r0, Report from ETSI TC BRAN #81
[7] 11-14/0511r0, ETSI BRAN regulatory test for occupied channel bandwidth and 802.11ac-2013
[8] ETSI TC BRAN(14)0000035, 802.11ac-2013 Partial Use of Bandwidth, Nominal Channel Bandwidth and Maskhttp://www.ieee802.org/11/private/ETSI_documents/BRAN/05-CONTRIBUTIONS/2014/2014_06_23_OR_BRAN%2380/BRAN(14)000035_802_11ac-2013_Partial_Use_of_Bandwidth__Nominal_Channel_Band.doc
[8] 11-14/1211r0, Ack Procedure for OFDMA
[9] 11-14/1436r0, Overhead Analysis for Simultaneous Downlink Transmissions