## Slide 1: FILS HLP Container element format
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | SRC Software | Fukuoka, Japan |  | hmorioka@src-soft.com
Date: 2015-03-10
Authors:

## Slide 2: Abstract
This document describes FILS HLP Container element format.

## Slide 3: Current format
“Source MAC Address” is always equal to non-AP STA’s MAC address in (Re)Association Request.
“Destination MAC Address” is always equal to non-AP STA’s MAC address in (Re)Association Response.
EID
Length
EID
Ext.
Destination MAC Address
Source MAC Address
HLP Packet
1
1
1
6
6
variable

## Slide 4: Single MAC address field format
“MAC Address” field is used for the destination MAC address in (Re)Association Request.
“MAC Address” field is used for the source MAC address in (Re)Association Response.
EID
Length
EID
Ext.
MAC Address
HLP Packet
1
1
1
6
variable

## Slide 5: Straw poll
Which format do you prefer?
  Existing format
  Single MAC address field format
  Don’t care