## Slide 1: OBSS Preamble Error Probability
Date: 2015-05-11
Authors:
Notes: DL and UL

## Slide 2: Background
The OBSS preamble detection probability impacts much on the overall network behavior.
[1, 2] showed that errors on OBSS preambles were very high around even 90% in both 11ax SS1 and SS2 [3] via MAC Simulator.
In this presentation, we provide our initial results about the OBSS preamble error probability in SS1 via Integrated Simulator where we find that the error probability is related closely to the simulation configuration.

## Slide 3: Simulation Scenario – 11ax SS1
Standard 11ax SS1 –Residential [3]
  5 floor, 20 rooms per floor
  10 STAs per room
  1*1 antenna
  20MHz Channel at 5GHz, Reuse 3 (randomly)

## Slide 4: Simulation Parameters
PHY parameters | 
Preamble model | [4, 5]
CCA-ED | -62dBm/20MHz (measured after large-scale fading)
Rx sensitivity/CCA-SD | -82dBm/20MHz (a packet with lower rx power is dropped)
Link Adaption | SINR feedback
Channel estimation | ideal
PHY abstraction | RBIR, BCC
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps
MPDU size | 1540 Bytes (1472 Data + 28 IP header + 40 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, with immediate BA], Max aggregation: 64 or 2 MPDUs with 4-byte MPDU delimiter
Max number of retries | 10
Beacon | Disabled
RTS/CTS | ON or OFF

## Slide 5: Preamble Model
The receiver will be locked by the first-arrived packet with signal strength above -82 dBm, and later-arrived packets are considered as interference[4,5].
    The receiver should be in IDLE status to detect an incoming preamble
    Preamble decoding modeled as a sub-frame decoding
    The packet length is calculated based on the assumption of 3-byte/4us (MCS0)
    Box0 PHY abstraction of SINR-to-PER is used [6]
    Preamble error% = 1-Total successfully decoded OBSS preambles/Total attempted decodes of OBSS preambles [2]
Signal Detect
Preamble Error Detect
Preamble
PPDU

## Slide 6: Error Probability
 | 64MPDU |  |  |  | 2MPDU
Case | RTS On |  |  | RTS Off | RTS On
 | DL Only | UL Only | DL & UL | DL & UL | DL & UL
Error % | 38.30% | 55.89% | 57.52% | 87.33% | 22.24%
64MPDU
2MPDU

## Slide 7: Observation
Without RTS/CTS, the preamble error increases significantly.
DL preamble could be more reliably detected than UL preamble.
Aggregation level of MPDU also impacts the preamble detection.

## Slide 8: Summary
We checked OBSS preamble error probability via our integrated SLS and we see that
  The error probability is not as much high as shown in [1,2]
  Error probability varies with different simulation cases
    Further observation will be get via more evaluation
Further and thorough evaluation of this problem is required.

## Slide 9: References
[1] 11-14/1420r1 The Impact of Preamble Error on MAC System Performance
[2] 11-15/0367r0 OBSS Preamble Detection
[3] 11-14/0980r10 Simulation Scenarios
[4] 11-14/1523r5 Offline Discussion Minutes of SLS Calibration
[5] 11-14/0571r8 Evaluation Methodology
    [6] 11-14/1176r1 PHY abstraction tables for 11ax system level simulation