## Slide 1: Non-Uniform Constellations for 1024-QAM
Date: 2015/05/11
Authors:

## Slide 2: Motivation
1024-QAM discussed as potential technology for ax to increase peak data rate (indoor and in-room), e.g. [1,2]
  25% increase in spectral efficiency compared to 256-QAM
  1Gbit/s with 1 spatial stream (160MHz, code rate 5/6, short GI)
Non-uniform constellations (NUCs) show increased performance compared to uniform constellations (UCs) [2]
  Especially for higher order QAMs
  1024-QAM:
    gain up to 0.7dB for 1D NUC
    gain up to 0.9dB for 2D NUC
  Moderate (2D) or no (1D) increase in demapper complexity
1-D NUC: 16-QAM
2-D NUC: 16-QAM

## Slide 3: Outline
Details on the proposed NUCs for 1024-QAM
Performance Results
  AWGN channel with and without phase noise

## Slide 4: Proposed NUCs for 1024-QAM
1-dimenionsal (1D) NUCs
  Good trade-off between performance gain and demapper complexity [2]
  Demapper has basically the same complexity as for uniform constellations
Different NUCs for each code rate
  Optimized for operating point of FEC with specific code rate
Optimized bit labeling
  Matches optimally to existing .11 WLAN system
    No changes at FEC or other blocks required
    No need for a dedicated bit interleaver

## Slide 5: Proposed NUCs for 1024-QAM
Figure shows example for code rate 2/3
I/Q symmetry
pos. / neg. symmetry
NUC defined by amplitudes ( assumed)
Details on amplitudes and bit labeling see Appendix

## Slide 6: Simulations: Parameters
Regular UC and NUC
1024-QAM
FEC: LDPC
Message Length: 1000bytes
Channel: AWGN
RF impairments: with and without phase noise
  Phase noise model according to evaluation methodology [3]
Gain compared to UC evaluated at FER=10-2
1D and 2D NUC
modulation | bit/symbol | coderate
1024-QAM | 10 | 2/3
1024-QAM | 10 | 3/4
1024-QAM | 10 | 5/6

## Slide 7: Simulations: Results Influence of phase noise
NUCs have similar degradation as UC under phase noise influence

## Slide 8: Simulations: Results Influence of phase noise
NUC gain is independent on phase noise

## Slide 9: Conclusions
Investigation of non-uniform constellations (NUCs) for 1024-QAM
  1-dimensional NUCs
    Up to 0.6dB gain compared to uniform constellation
  2-dimensional NUCs
    Up to 0.9dB gain compared to uniform constellation
Simulations in the presence of phase noise
  NUC gain is maintained
Basically same complexity as uniform constellations (1D NUC)

## Slide 10: References
11-14-0624-00-00ax Investigation on 1024 QAM feasibility in 11ax
11-15-0048-00-00ax Non-uniform Constellations for higher Order QAMs
11-09-0451-15-00ac-tgac Functional requirements and evaluation methodology

## Slide 11: APPENDIX

## Slide 12: NUC: 1-D vs 2D
1-D NUC
  I/Q symmetry
  1-D demapping as for uniform constellations (UC), i.e. same order of demapping complexity
2-D NUC
  Symmetric quadrants
  Higher gain compared to 1-D NUC
  2-D demapping required
1-D NUC: 16-QAM
2-D NUC: 16-QAM

## Slide 13: Example: How to get the bit labeling
Identify amplitude levels of real and imaginary part of a particular signal point
Consider mapping table (see next slide)
Identify both partial bit sequences & arrange as indicated
= (1 1 1 1 1 1 0 0 0 0)
  correspond to real
  correspond to imag
Real part:
= (1 1 1 1 1 1 0 0 0 0)
Imag. part:

## Slide 14: Example: How to get the bit labeling (cont.)
b1 b2 b3 b6 b7 | 0 0 0 0 0 | 1 0 0 0 0 | 1 0 1 0 0 | 0 0 1 0 0 | 0 0 1 0 1 | 1 0 1 0 1 | 1 0 0 0 1 | 0 0 0 0 1 | 0 1 0 0 1 | 1 1 0 0 1 | 1 1 1 0 1 | 0 1 1 0 1 | 0 1 1 0 0 | 1 1 1 0 0 | 1 1 0 0 0 | 0 1 0 0 0 | 
Re(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b1 b2 b3 b6 b7 | 0 1 0 1 0 | 1 1 0 1 0 | 1 1 1 1 0 | 0 1 1 1 0 | 0 1 1 1 1 | 1 1 1 1 1 | 1 1 0 1 1 | 0 1 0 1 1 | 0 0 0 1 1 | 1 0 0 1 1 | 1 0 1 1 1 | 0 0 1 1 1 | 0 0 1 1 0 | 1 0 1 1 0 | 1 0 0 1 0 | 0 0 0 1 0 | 
Re(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC
b0 b4 b5 b8 b9 | 0 0 0 0 0 | 1 0 0 0 0 | 1 1 0 0 0 | 0 1 0 0 0 | 0 1 0 1 0 | 1 1 0 1 0 | 1 0 0 1 0 | 0 0 0 1 0 | 0 0 0 1 1 | 1 0 0 1 1 | 1 1 0 1 1 | 0 1 0 1 1 | 0 1 0 0 1 | 1 1 0 0 1 | 1 0 0 0 1 | 0 0 0 0 1 | 
Im(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b0 b4 b5 b8 b9 | 0 0 1 0 1 | 1 0 1 0 1 | 1 1 1 0 1 | 0 1 1 0 1 | 0 1 1 1 1 | 1 1 1 1 1 | 1 0 1 1 1 | 0 0 1 1 1 | 0 0 1 1 0 | 1 0 1 1 0 | 1 1 1 1 0 | 0 1 1 1 0 | 0 1 1 0 0 | 1 1 1 0 0 | 1 0 1 0 0 | 0 0 1 0 0 | 
Im(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC
real part
imaginary part

## Slide 15: NUC for code rate 2/3
b1 b2 b3 b6 b7 | 0 0 0 0 0 | 1 0 0 0 0 | 1 0 1 0 0 | 0 0 1 0 0 | 0 0 1 0 1 | 1 0 1 0 1 | 1 0 0 0 1 | 0 0 0 0 1 | 0 1 0 0 1 | 1 1 0 0 1 | 1 1 1 0 1 | 0 1 1 0 1 | 0 1 1 0 0 | 1 1 1 0 0 | 1 1 0 0 0 | 0 1 0 0 0 | 
Re(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b1 b2 b3 b6 b7 | 0 1 0 1 0 | 1 1 0 1 0 | 1 1 1 1 0 | 0 1 1 1 0 | 0 1 1 1 1 | 1 1 1 1 1 | 1 1 0 1 1 | 0 1 0 1 1 | 0 0 0 1 1 | 1 0 0 1 1 | 1 0 1 1 1 | 0 0 1 1 1 | 0 0 1 1 0 | 1 0 1 1 0 | 1 0 0 1 0 | 0 0 0 1 0 | 
Re(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC
Amplitude level | 
 | 1
 | 2.0047
 | 3.9822
 | 5.1633
 | 7.0998
 | 8.5600
 | 10.4887
 | 12.2428
 | 14.2618
 | 16.3225
 | 18.5947
 | 21.0696
 | 23.8248
 | 26.9139
 | 30.4303
 | 34.5872
Amplitude level | 
 | 1
 | 2.0047
 | 3.9822
 | 5.1633
 | 7.0998
 | 8.5600
 | 10.4887
 | 12.2428
 | 14.2618
 | 16.3225
 | 18.5947
 | 21.0696
 | 23.8248
 | 26.9139
 | 30.4303
 | 34.5872
b0 b4 b5 b8 b9 | 0 0 0 0 0 | 1 0 0 0 0 | 1 1 0 0 0 | 0 1 0 0 0 | 0 1 0 1 0 | 1 1 0 1 0 | 1 0 0 1 0 | 0 0 0 1 0 | 0 0 0 1 1 | 1 0 0 1 1 | 1 1 0 1 1 | 0 1 0 1 1 | 0 1 0 0 1 | 1 1 0 0 1 | 1 0 0 0 1 | 0 0 0 0 1 | 
Im(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b0 b4 b5 b8 b9 | 0 0 1 0 1 | 1 0 1 0 1 | 1 1 1 0 1 | 0 1 1 0 1 | 0 1 1 1 1 | 1 1 1 1 1 | 1 0 1 1 1 | 0 0 1 1 1 | 0 0 1 1 0 | 1 0 1 1 0 | 1 1 1 1 0 | 0 1 1 1 0 | 0 1 1 0 0 | 1 1 1 0 0 | 1 0 1 0 0 | 0 0 1 0 0 | 
Im(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC
real part
imaginary part

## Slide 16: NUC for code rate 3/4
Amplitude level | 
 | 1
 | 2.9667
 | 4.9871
 | 7.0015
 | 9.0819
 | 11.1960
 | 13.3951
 | 15.6735
 | 18.0691
 | 20.5980
 | 23.2914
 | 26.1728
 | 29.2806
 | 32.6657
 | 36.4161
 | 40.7366
Amplitude level | 
 | 1
 | 2.9667
 | 4.9871
 | 7.0015
 | 9.0819
 | 11.1960
 | 13.3951
 | 15.6735
 | 18.0691
 | 20.5980
 | 23.2914
 | 26.1728
 | 29.2806
 | 32.6657
 | 36.4161
 | 40.7366
real part
imaginary part
b3 b4 b5 b8 b9 | 0 0 0 0 0 | 1 0 0 0 0 | 1 0 1 0 0 | 0 0 1 0 0 | 0 1 1 0 0 | 1 1 1 0 0 | 1 1 0 0 0 | 0 1 0 0 0 | 0 1 0 0 1 | 1 1 0 0 1 | 1 1 1 0 1 | 0 1 1 0 1 | 0 0 1 0 1 | 1 0 1 0 1 | 1 0 0 0 1 | 0 0 0 0 1 | 
Re(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b3 b4 b5 b8 b9 | 0 0 0 1 1 | 1 0 0 1 1 | 1 0 1 1 1 | 0 0 1 1 1 | 0 1 1 1 1 | 1 1 1 1 1 | 1 1 0 1 1 | 0 1 0 1 1 | 0 1 0 1 0 | 1 1 0 1 0 | 1 1 1 1 0 | 0 1 1 1 0 | 0 0 1 1 0 | 1 0 1 1 0 | 1 0 0 1 0 | 0 0 0 1 0 | 
Re(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC
b0 b1 b2 b6 b7 | 0 0 0 0 0 | 1 0 0 0 0 | 1 0 1 0 0 | 0 0 1 0 0 | 0 1 1 0 0 | 1 1 1 0 0 | 1 1 0 0 0 | 0 1 0 0 0 | 0 1 0 1 0 | 1 1 0 1 0 | 1 1 1 1 0 | 0 1 1 1 0 | 0 0 1 1 0 | 1 0 1 1 0 | 1 0 0 1 0 | 0 0 0 1 0 | 
Im(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b0 b1 b2 b6 b7 | 0 0 0 1 1 | 1 0 0 1 1 | 1 0 1 1 1 | 0 0 1 1 1 | 0 1 1 1 1 | 1 1 1 1 1 | 1 1 0 1 1 | 0 1 0 1 1 | 0 1 0 0 1 | 1 1 0 0 1 | 1 1 1 0 1 | 0 1 1 0 1 | 0 0 1 0 1 | 1 0 1 0 1 | 1 0 0 0 1 | 0 0 0 0 1 | 
Im(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC

## Slide 17: NUC for code rate 5/6
Amplitude level | 
 | 1
 | 2.9902
 | 5.0100
 | 7.0446
 | 9.1283
 | 11.2570
 | 13.4588
 | 15.7417
 | 18.1292
 | 20.6379
 | 23.2916
 | 26.1151
 | 29.1412
 | 32.4176
 | 36.0267
 | 40.1583
Amplitude level | 
 | 1
 | 2.9902
 | 5.0100
 | 7.0446
 | 9.1283
 | 11.2570
 | 13.4588
 | 15.7417
 | 18.1292
 | 20.6379
 | 23.2916
 | 26.1151
 | 29.1412
 | 32.4176
 | 36.0267
 | 40.1583
real part
imaginary part
b0 b3 b5 b7 b8 | 0 0 0 0 0 | 1 0 0 0 0 | 1 0 1 0 0 | 0 0 1 0 0 | 0 0 1 0 1 | 1 0 1 0 1 | 1 0 0 0 1 | 0 0 0 0 1 | 0 1 0 0 1 | 1 1 0 0 1 | 1 1 1 0 1 | 0 1 1 0 1 | 0 1 1 0 0 | 1 1 1 0 0 | 1 1 0 0 0 | 0 1 0 0 0 | 
Re(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b0 b3 b5 b7 b8 | 0 1 0 1 0 | 1 1 0 1 0 | 1 1 1 1 0 | 0 1 1 1 0 | 0 1 1 1 1 | 1 1 1 1 1 | 1 1 0 1 1 | 0 1 0 1 1 | 0 0 0 1 1 | 1 0 0 1 1 | 1 0 1 1 1 | 0 0 1 1 1 | 0 0 1 1 0 | 1 0 1 1 0 | 1 0 0 1 0 | 0 0 0 1 0 | 
Re(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC
b1 b2 b4 b6 b9 | 0 0 0 0 0 | 0 0 0 0 1 | 0 0 0 1 1 | 0 0 0 1 0 | 0 1 0 1 0 | 0 1 0 1 1 | 0 1 0 0 1 | 0 1 0 0 0 | 1 1 0 0 0 | 1 1 0 0 1 | 1 1 0 1 1 | 1 1 0 1 0 | 1 0 0 1 0 | 1 0 0 1 1 | 1 0 0 0 1 | 1 0 0 0 0 | 
Im(zq) | -31 | -29 | -27 | -25 | -23 | -21 | -19 | -17 | -15 | -13 | -11 | -9 | -7 | -5 | -3 | -1 | Uniform
 | ‑u15 | ‑u14 | ‑u13 | ‑u12 | ‑u11 | ‑u10 | ‑u9 | ‑u8 | ‑u7 | ‑u6 | ‑u5 | ‑u4 | ‑u3 | ‑u2 | ‑u1 | -1 | NUC
b1 b2 b4 b6 b9 | 1 0 1 0 0 | 1 0 1 0 1 | 1 0 1 1 1 | 1 0 1 1 0 | 1 1 1 1 0 | 1 1 1 1 1 | 1 1 1 0 1 | 1 1 1 0 0 | 0 1 1 0 0 | 0 1 1 0 1 | 0 1 1 1 1 | 0 1 1 1 0 | 0 0 1 1 0 | 0 0 1 1 1 | 0 0 1 0 1 | 0 0 1 0 0 | 
Im(zq) | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | Uniform
 | 1 | u1 | u2 | u3 | u4 | u5 | u6 | u7 | u8 | u9 | u10 | u11 | u12 | u13 | u14 | u15 | NUC