## Slide 1
Multi-STA Block ACK Protection
Date: 2015-05-12
Authors:

## Slide 2: Introduction
UL-OFDMA and UL-MU-MIMO are key enabling technologies to enhance the performance in dense environment in 11ax.
Multi-STA Block ACK was adopted in SFD to handle UL-MU transmission[1][2].
Multi-TID Block ACK frame is reused as a Multi STA Block ACK[1][2].
Multi-STA Block ACK frame has variable size depending on number of users and Block ACK mode [1][2].
  Block ACK mode requires Block ACK sequence and Block ACK Bitmap fields

## Slide 3: Multi-STA BA[2]
B0-B10= AID
B11= ACK/BA
Multi-STA BA may have 11a frame format
Multi-STA BA frame has variable length due to variable number of users
Multi-STA BA could have variable MCS in 11a

## Slide 4: EIFS operation for ACK protection
11 devices need to defer EIFS duration before transmitting a frame when previously received frame contains an error or is undecodable.
EIFS duration
  SIFS+Maximum_ACK_duration+DIFS
EIFS operation needs to consider fairness among STAs[3]
EIFS prevents collision on ACK from hidden STAs’ transmission

## Slide 5: EIFS and various ACK types
Legacy hidden STAs’ transmission could interfere Multi-STA BA transmission
EIFS operation could not guarantee Multi-STA BA reception

## Slide 6: EIFS duration for BA
MCS 0 ACK duration
  44us
EIFS duration
  SIFS+Maximum ACK duration(MCS0)+DIFS
  16us+44us+34us = 94us on 11a, 11n(5GHz), 11ac
MCS 0 BA duration
  68us
  SIFS+Maximum BA duration(MCS0)
  16us+68us = 84us
  No collision but fairness problem between hidden and non-hidden STAs

## Slide 7: EIFS duration for Multi-STA BA
Multi-STA BA duration
  11a preamble duration+(22+N_STA*12)bytes/rate (BA mode for all STAs)
  At least 196us is required to avoid collision in 8 STA, MCS 0 case
  EIFS is still 94us
  Back-off value below 12 slots may cause collision on Multi-STA BA
    1 slot have 9us duration

## Slide 8: Several approaches to protect Multi-STA BA transmission
Higher MCS Multi-STA BA for Multiuser
  Restrict number of users based on MCS level
L-SIG protection
  PHY level protection for Multi-STA BA
Restriction on using Multi-STA BA
  RTS/CTS case
  TXOP guaranteed case only (e.g., Power Saving Multi Poll)

## Slide 9: Higher MCS Multi-STA BA for Multiuser
Restrict Multi-STA BA air time<78us
  20us+(22+N_STA*12)bytes/rate
  Assume all STAs employ BA mode (Includes Block ACK Sequence Control field and Bitmap Field)
Rate | N_STA | N_STA(Integer)
6 | 1.791667 | 1
9 | 3.604167 | 3
12 | 5.416667 | 5
18 | 9.041667 | 9
24 | 12.66667 | 12
36 | 19.91667 | 19
48 | 27.16667 | 27
54 | 30.79167 | 30

## Slide 10: L-SIG protection (1)
Using L-SIG protection to protect Multi-STA BA
UL-MU STAs need to transmit common L-SIG
Hidden STAs have disadvantage of unfair contention due to EIFS duration
  Non-hidden STAs differ DIFS(or AIFS) after ACK transmission, but hidden STAs differ EIFS after ACK transmission

## Slide 11: L-SIG protection (2)
For fair contention, reduced L-SIG protection to provide fairness to hidden STAs
  All STAs differ DIFS after ACK transmission

## Slide 12: Restriction on using Multi-STA BA
MAC level NAV setting is required for Multi-STA BA transmission
Use Multi-STA BA only when TXOP is guaranteed
  In PSMP scenario, using Multi-STA BA for UTT
  RTS-CTS case
    RTS-CTS may set NAV to all hidden STAs

## Slide 13: StrawPoll
Do you agree to add to the TG Specification Frame work document?
  x.y.z. 802.11ax needs to provide a mechanism for Multi-STA BA to be protected from hidden node STAs.
    Y
    N
    A

## Slide 14: References
[1] IEEE 802.11-15/0132r4 "Specification Framework for TGax"
[2] IEEE 802.11-15/0366r2 "Multi-STA Acknowledgement"
[3] IEEE 802.11-14/1211r0 "ACK procedure for OFDMA"