## Slide 1: Preliminary Simulation Results on AoA Accuracy in 2.4 GHz and 5 GHz bands
Date: 2015-05-12
Authors:

## Slide 2: Background
NGP goals include
  Improving positioning accuracy (relative to FTM)
  Reducing number of frame exchanges required to arrive at a useful location fix
  Mechanisms to enable new use cases where a coarse (but quick) location fix is needed first (if needed followed by a background refinement to a more accurate fix)
Some of the earlier discussions indicate that Angle of Arrival could be used to obtain a location fix quickly (which could be followed by a refinement procedure, if needed to render a (more) accurate fix).
This presentation discusses Antenna Array configurations, and achievable AoA accuracies in the 2.4 and 5GHz bands based on a set of simulations. More simulations are planned to refine the simulation parameters to match typical Use Cases scenarios.
Ganesh Venkatesan (Intel Corporation)

## Slide 3: Learning from studies/observations in the 60 GHz band
Use of Antenna Arrays
Angle of Arrival estimates
  Based on simulations and some real life observations (with .11ad implementations)
  Precise AoA can be determined and hence used to determine range and/or relative position
If we can demonstrate that precise AoA estimates can be determined with 2.4/5GHz bands, then we could design an NGP protocol that applies to all common Wi-Fi bands (i.e. 2.4/5/60 GHz)
Ganesh Venkatesan (Intel Corporation)

## Slide 4: Simulation Setup/Approach/Terminology
Signal waveform known to the receiver.
  Power per sample normalized to 1.
Noise power:
Antenna separation in the array:
  fmax=2472 MHz / 5805 MHz
Actual emitter signal is TX’d at fmin=2412 MHz / 5180 MHz
  Slight loss of aperture
Array Configuration
Emitter-Receiver Configuration
=
Ganesh Venkatesan (Intel Corporation)
q

## Slide 5: Simulation Results N=32, M=4
Maximum Likelihood AoA estimation for single emitter with known waveform using 32 OFDM symbols
Ganesh Venkatesan (Intel Corporation)
-20
-10
0
10
20
30
10
-1
10
0
10
1
10
2
10
3
RMSE [
o
]
SNR [dB]
AOA RMSE
CRLB
M = 4, N = 32, q= 43.85°, fc_nom = 2472MHz, fc_actual = 2412MHz
M = 4, N = 32, q= 43.85°, fc_nom = 5805MHz, fc_actual = 5180MHz
-20
-10
0
10
20
30
10
-1
10
0
10
1
10
2
10
3
RMSE [
o
]
SNR [dB]
AOA RMSE
CRLB

## Slide 6: Simulation Results N=64, M=4
Maximum Likelihood AOA estimation for single emitter with known waveform using 64 OFDM symbols.
Ganesh Venkatesan (Intel Corporation)
-20
-10
0
10
20
30
10
-1
10
0
10
1
10
2
RMSE [
o
]
SNR [dB]
AOA RMSE
CRLB
-20
-10
0
10
20
30
10
-1
10
0
10
1
10
2
RMSE [
o
]
SNR [dB]
AOA RMSE
CRLB
M = 4, N = 64, q= 43.85°, fc_nom = 2472MHz, fc_actual = 2412MHz
M = 4, N = 64, q= 43.85°, fc_nom = 5805MHz, fc_actual = 5180MHz

## Slide 7: Summary/Recommendations
Accurate AoA estimates can be easily obtained in 2.4 & 5GHz using known techniques (from our experience in the 60GHz band)
  AoA estimates with manageable antenna array form-factor and standard implementations for 2.4/5GHz can help in the determination of accurate location <to be quantified>.
With the augmentation of AoA to the parameter set (which is ToD, ToA at present), we can improve the positioning accuracy.
Achieve faster geo-location while meeting NGP goals to minimize/maintain medium usage and power requirements
Ganesh Venkatesan (Intel Corporation)

## Slide 8: Next Steps
Assuming that we agree that AoA is a compelling candidate to include in our data set for positioning,
We intend to bring additional results
  Repeat simulation for various angle values and identify where AoA estimation is best/worst
  How can we combine AoA with ToA/ToD for
    more accurate location estimation, and
    Minimizing or eliminating errors due to NLoS path(s) in harsh environments
    Reducing the number of frames required to obtain an acceptable location estimate
Ganesh Venkatesan (Intel Corporation)