## Slide 1
Reference Box5 Calibration Assumptions and Parameters
Date: 2015-07-12
Authors:

## Slide 2
Authors (continued):

## Slide 3: Background
So far we have achieved a lot of agreements with Box5 calibration [1] and the basic procedure of packet reception and preamble detection concluded from [1] has been accepted in the appendix 4 of 11ax EMD [2].
  Also some simplifications of and TBD parameters in appendix 4 [2] were listed in the subsection “Box 5” in section “System Simulation Calibration” in [2].
    One of the most important calibration assumptions there is: the receiver will be locked by the first-arrived packet, and later-arrived packets are considered as interference.
In the May meeting, the 11ac SS6 [3] was approved formally as an easy-to-start scenario used for Box5 calibration [4] where step-by-step calibration with simulation parameters defined in [5] was accepted.
During offline calibration, we found that it is helpful to further clarify a few parameters in [4,5] which are highlighted in red in this presentation.
The latest calibration result is shown in [6] where we have got very similar STA throughput of 1-BSS case.

## Slide 4: PHY Parameters
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Primary channel | Aligned primary 20MHz channel for each co-80MHz-channel BSS; The detection of preamble and BA should only focus on primary 20MHz
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 or 0 dB standard deviation) per link
Preamble type | Control: legacy 20us; Data: 11ac (20us+20us for 1antenna case)
Legacy control frame rate | Basic 6Mbps rate for RTS/CTS/ACK/BA (MCS0) [1]
AP/STA TX Power | 20/15 dBm per antenna
Power Spectral density | Scaled to 80 MHz
number of antennas at AP /STA | 1/1
AP /STA antenna gain | 0/-2 dBi
Noise Figure | 7dB
CCA-ED threshold | -56 dBm (measured across the entire bandwidth after large-scale fading)
Rx sensitivity/CCA-SD | -76 dBm (a packet with lower rx power is dropped)
Link Adaption | Fixed MCS =5 for 11ac SS6 and TBD for 11ax SS1-4
Channel estimation | Ideal unless otherwise specified
PHY abstraction | RBIR, BCC (see appendix 1&3 in [2])
Symbol length | 4us with 800ns GI per OFDM symbol

## Slide 5: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps Random start time during a 10ms interval
MPDU size | 1544 Bytes (1472 Data + 28 IP header + 8 LLC header + 30 MAC header + 4 delimiter + 2 padding)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, immediate BA without explicit request], Max aggregation: 32 MPDUs
Max number of retries | 10
Beacon | Disabled unless otherwise specified
RTS/CTS | OFF unless otherwise specified
Running time | >= 10s per drop
Output metric | -CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time) -PER of all AP/STA (1 - # of success subframes / # of transmitted subframes)

## Slide 6: 11ac Scenario 6 – OBSS Enterprise [3]
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association

## Slide 7: 11ac SS6 Traffic Flow Model
DL/UL traffic assigned for each STA
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow

## Slide 8: Step-by-Step Calibration of 11ac SS6
1 BSS (upper-right corner BSS B)
  DL only case
  UL only case
    1 STA: each STA-AP
    2 STAs: 3+9, 3+15, 3+27
    3 STAs: 3+9+15, 3+9+27
    5 STAs
  DL & UL case
2 BSS (A+B)
  Both DL only
  Both UL only
  A DL and B UL
  B UL and A DL
3 BSS
  DL only
  UL only
  Mixed DL & UL
Note:
No shadowing is assumed
For 2 BSS and 3 BSS cases, traffic flow model is defined as in slide 7.

## Slide 9: Summary
We further clarified certain assumptions used in the joint calibration.
The latest 1-BSS result is shown in [6].
Next we will continue to calibrate more complicated 2-BSS and 3-BSS cases.

## Slide 10: Reference
[1] 11-14/1523r5 Offline Discussion Minutes of SLS Calibration
[2] 11-14/0571r9 Evaluation Methodology
[3] 11-09/0451r16 TGac Functional Requirements and Evaluation Methodology
[4] 11-14/0980r12 Simulation Scenarios
[5] 11-15/0680r1 Reference Box5 Calibration Assumptions and Parameters
[6] 11-15/0802r0 Box5 Calibration Results of SS6