## Slide 1
SIG-B Field for HEW PPDU
Date: 2015-07-13
Authors:

## Slide 2: Background
In our previous contribution [1], we analyzed and proposed SIG field structure for HE UL PPDU, which proposes:
  UL MU PPDU does not need to include HE-SIG-B field if it is sent as an immediate response to a Trigger frame sent by an AP.
  UL SU PPDU does not need to include HE-SIG-B field.
In this contribution, we extend the similar concept of SIG-B field to cover both UL and DL cases.

## Slide 3: SIG Field Information
Common control information
  Information needed not only for target receiver but also 3rd party STAs and common information to all scheduled STAs, such as
    Allocated bandwidth
    Packet duration/GI/N_LTF
    COLOR/PAID/GID/TXOP_PS
    SIG-B field structure
  May be included in L-SIG and HE-SIG-A fields.
Resource allocation information
  Required only for MU transmission or partial band transmission such as
    Resource allocation structure (map)
    Which STA is scheduled in which subband/spatial_stream
  May be included in either HE-SIG-A or HE-SIG-B field.
User-specific information
  Information for each STA to decode the payload, such as
    MCS/NSTS
    STBC/Beamformed
  May be included in HE-SIG-B field.

## Slide 4: Requirements for each Frame Type
SU transmission
  Full band transmission
    As every resource is occupied by a single STA, there’s no need to indicate additional resource allocation information.
  Partial band transmission
    As not all resource is occupied by the transmitter, resource allocation information is needed for the receiver to properly decode the payload.
MU transmission
  DL MU
    As every participating STA needs to know its allocated resource, resource allocation information shall be included.
  UL MU
    As target receiver (AP) already knows allocated resource, resource allocation information is not needed.
    User specific information is not needed if AP decides user specific information and indicates in the Trigger frame.

## Slide 5: SIG Field Structure
Depending on frame type, several information may not need to be included in the SIG field.
 | SU |  | MU
 | Full Band | Partial Band | 
DL | CC/US | CC/RA/US | CC/RA/US
UL | CC/US | CC/RA/US | CC/US*(?)
CC: Common Control information
RA: Resource Allocation information
US: User Specific information
* As mentioned in [1], If US is separately encoded, it can exist.

## Slide 6: Proposal
SU partial band transmission can be considered as assigning single STA in MU frame format (OFDMA PPDU) .
  Therefore, at least resource allocation information is not needed for non-OFDMA tone plan (Also called OFDM PPDU or SA PPDU).
  For non-OFDMA tone plan , HE-SIG-A may be enough to indicate common control and user specific information similar to 11ac.
Resource allocation information is not needed in UL MU transmission if it is an immediate response to a Trigger frame.
  Similar to our previous proposal [1], user-specific information decided by AP and indicated in the Trigger frame is more efficient than allowing each STA to decide its own user-specific information.

## Slide 7: Proposal
 | SU (OFDM) format | MU (OFDMA) format | 
 | SU Full Band | SU Partial Band | MU
DL | SIG-A: CC/US SIG-B: NONE | SIG-A: CC SIG-B: RA/US | SIG-A: CC SIG-B: RA/US
UL | SIG-A: CC/US SIG-B: NONE | SIG-A: CC SIG-B: RA/US | SIG-A: CC SIG-B: NONE
CC: Common Control information
RA: Resource Allocation information
US: User Specific information

## Slide 8: Proposal
Based on these aspects, we propose
  UL MU PPDU (OFDMA PPDU) does not include HE-SIG-B field if it is sent as an immediate response to a Trigger frame sent by an AP.
  SU PPDU (OFDM PPDU) does not include HE-SIG-B field for both DL and UL transmission.
  Single user partial bandwidth transmission uses MU PPDU format.

## Slide 9: SP 1
Do you agree to add to the TG Specification Framework:
  3.y.z HE SU PPDU shall not include HE-SIG-B field.

## Slide 10: SP 2
Do you agree to add to the TG Specification Framework:
  3.y.z UL MU PPDU shall not include HE-SIG-B field if it is sent as an immediate response to a Trigger frame sent by an AP.

## Slide 11: References
[1] 11-15/0574r0, “SIG Structure for UL PPDU”.