## Slide 1
Name | Affiliation | Address | Phone | Email
Lin Yang | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Zoong Doan |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ddoan@qti.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Alice Chen |  | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
11ax OFDMA Tone Plan
Leftover Tones and Pilot Structure
Date: 2015-07-13

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com

## Slide 3: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Wookbong Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | wookbong.lee@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Introduction
11ax OFDMA tone plan was decided in IEEE May 2015 meeting [1] except the location of leftover tones
  8 leftover tones within each 242 tone block, except in 20MHz PPDU 4 spare tones are already used for DC protection in OFDMA
11ax Pilot design and structure
  [2] provides some thoughts on 11ax pilot tone placement
  [3] addresses the pilot design in the 11ax data section
  This presentation will cover
    Pilot design for HE-LTF
    Pilot structure in 11ax: the location of pilot tones
Lin Yang, Bin Tian (Qualcomm)

## Slide 10: Leftover Tones
Possible usage of leftover tones
  Separator between different RUs, especially smaller size RUs, to reduce leakage from adjacent block
  Additional edge protection from pulse shaping filter, adjacent blocker, etc.
No power transmitted on the leftover tones
In the following slides, we propose the OFDMA tone structures that implement the possible usage of leftover tones in a balanced way
Lin Yang, Bin Tian (Qualcomm)

## Slide 11: Proposed Location of Leftover Tones (in orange color)
HE80
12 Edge
12 Edge
12 Edge
12 Edge
13
13
13
13
13
13
13
13
11 Edge
11 Edge
11 Edge
11 Edge
11 Edge
7
DC
7
DC
7
DC
7
DC
12 Edge
996 usable tones +5 DC
HE40
12 Edge
12 Edge
12 Edge
12 Edge
11 Edge
11 Edge
11 Edge
11 Edge
5
DC
5
DC
5
DC
5
DC
242
26
26
26
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
242
26
26
26
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
242
242
26
26
52
102+4
102+4
2
2
26
52
26
26
52
26
102+4
102+4
26
26
26
26
26
26
52
1
1
26
1
26
52
2
1
2
1
1
1
26
26
2
52
1
1
2
26
2
26
52
1
2
1
26
26
26
26
2
52
1
1
2
1
1
1
1
2
1
242
242
26
26
52
102+4
102+4
2
2
26
52
26
26
52
26
102+4
102+4
26
26
26
26
26
26
52
1
1
26
1
26
52
2
1
2
1
1
1
26
26
2
52
1
1
2
26
2
26
52
1
2
1
26
26
26
26
2
52
1
1
2
1
1
1
1
2
1
7
DC
26
26
26
26
26
26
26
52
52
52
52
26
242 + 3 DC
102+4 pilots
102+4 pilots
1
1
1
1
13
1
1
1
1
13
13
13
5 Edge
5 Edge
5 Edge
5 Edge
6 Edge
6 Edge
6 Edge
6 Edge
7
DC
13
13
7
DC
HE20 with 7DC for OFDMA
Lin Yang, Bin Tian (Qualcomm)

## Slide 12: Pilot Design for HE-LTF
11ac introduced single stream pilots (SSP) to correct residual phase drift (CFO) in VHT-LTF
In 11ax, 2x and 4x HE-LTF were adopted
  Longer LTF makes 11ax more sensitive to phase drift than 11ac
Phase tracking in channel estimation for UL MU MIMO has been discussed in [4]
  Per stream orthogonal LTF was adopted to track per user CFO
  No pilots in HE-LTF
In this presentation we will tackle phase tracking for SU, DL and UL OFDMA and DL MU-MIMO cases.
  Only one clock error source (per RU for UL OFDMA) needs to be tracked
Lin Yang, Bin Tian (Qualcomm)

## Slide 13: CFO Accuracy Requirement for SU Transmission
The following plot shows how sensitive SU MIMO to CFO in HE-LTF
MCS | MCS1 | MCS3 | MCS5 | MCS7 | MCS9
SNR for 10%PER (dB) | 9 | 16 | 23.9 | 27.4 | 32.7
CFO (Hz) | >1000 | 742 | 337 | 256 | 127
Lin Yang, Bin Tian (Qualcomm)

## Slide 14: Improving CFO Tracking in 11ax Preamble
Two possible ways to meet the required CFO sensitivity
  Phase tracking during HE-LTF (discussed in the following slides)
  Improve CFO estimation before HE-LTF
    No pilots is needed during HE-LTF
    At least 4 symbols (L-SIG, RL-SIG, 2 HE-SIG-A) can be used for data-aided phase tracking
    Performance issue
      Significantly worse than SSP (11ac) based approach.
      Challenging to meet the CFO requirements for large number of SS, even with added complexity from data-aided CFO estimation
Our preference: phase tracking during HE-LTF
  Better performance, more tolerance for HW impairments like LO bouncing
  Phase tracking in LTF
20MHz SNR | 1% Residual CFO after L-LTF | 1% Residual CFO with Data-aided up to SIGA | HE-LTF 1% residual CFO (with 8 SSP)
30 dB | 1.6KHz | 270Hz | 41Hz
20 dB | 2.7KHz | 400Hz | 125Hz
10dB | 7.6KHz | 1.1KHz | 360Hz
Lin Yang, Bin Tian (Qualcomm)

## Slide 15: Phase Tracking in HE-LTF
Options for phase tracking in LTF
  Without pilots: using orthogonal per stream LTF (as in [4]) like in UL MU MIMO
    Pros
      No pilots needed in LTF
      More accumulation gain from larger number of LTF tones comparing to the pilot tones in LTF
      Less channel interpolation loss
      Consistent design with UL MU MIMO
    Cons
      Assumption for this approach is the Nss adjacent subcarriers share the same channel
      Additional complexity from spreading/despreading LTF sequence with different streams
  With pilots: assuming SSP as 11ac
    Pros
      Existing feature in 11ac
      Easy tracking
    Cons
      May have channel interpolation loss
      Need to remember pilot location, especially for 2x LTF
Lin Yang, Bin Tian (Qualcomm)

## Slide 16: Phase Tracking Performance
Observation (details in Appendix):
SSP provides much better phase tracking performance than orthogonal LTF for MIMO transmission in frequency selective channel at medium to high SNR
Performance of orthogonal LTF case is limited by channel frequency selectivity
Performance is very close between 8 SSP and 6 SSP in 20 MHz
Lin Yang, Bin Tian (Qualcomm)

## Slide 17: Channel Interpolation Loss
Notes:
2x LTF. Assuming noise and CFO free to study the interpolation loss
Edge tone and tones around pilots have higher interpolation/extrapolation loss for channel estimation
Lin Yang, Bin Tian (Qualcomm)

## Slide 18: Impact of Channel Interpolation Loss
Notes:
2x LTF
CFO is set to zero to decouple its effect
Practical timing, phase tracking is on in data symbol, smoothing is on
Observation: Interpolation loss at pilot position has no noticeable impact to PER performance
Lin Yang, Bin Tian (Qualcomm)

## Slide 19: Discussion on Phase Tracking Approaches
SSP performs significantly better than orthogonal LTF in CFO estimation in frequency selective channel (e.g. DNLOS)
  E.g. 20MHz 6 or 8 SSP can meet the CFO requirements
For SSP, channel interpolation loss around pilot tones does not have noticeable impact on PER performance due to limited pilot density and low interpolation loss level
Our preference: single stream pilot (11ac alike) in HE-LTF
Lin Yang, Bin Tian (Qualcomm)

## Slide 20: 11ax Pilots in HE-LTF
For 4x LTF, we can use the same SSP tone plan as in data (always 4x)
  Same number of pilots and pilot tone location as in data
  Similar to 11ac processing
For 2x LTF
  New pilot tone location needs to be defined
    2x LTF only populates every other tone in 4x OFDM symbol
    In current 4x data symbol, not all pilot tones have even indices
  Prefer to move all the pilot tones to even index in 4x OFDM symbol
    Same number of pilot tones in 4x data and 2x HE-LTF symbol
    Pilot index in 2x HE-LTF = Pilot index in 4x data /2
Lin Yang, Bin Tian (Qualcomm)

## Slide 21: Pilot Structure for 26 Tone RU
Keep relative pilot position close to what is defined in 11ah
  11ah symmetric pilot structure of [6P12P6]: pilot indices are one even and one odd.
In 11ax, regardless of leftover tone allocation plan, there are three variations of pilot tone position within 26 tone RU
  Pos1: 26 tone RU having left most tone starting from even index may need structure of [6P13P5]
  Pos2: left most tone starting from odd index may need structure of [5P13P6]
  Pos3: center 26 tone RU, pilot structure would be [6P6 6P6]
To ensure all pilots with even tone indices, relative pilot location within 26 tone RU has to be varied for different 26 tone RUs
0 6 19 25
0 6 20 25
1 6 20 26
-16 -10 -4
DC
4 10 16

## Slide 22: Fixed Pilot Structure Independent of Resource Allocation
11ax has to define new pilot positions for all RUs
  Legacy pilot design have pilots at odd indices
Relative pilot position within a RU is not fixed
  Need to reduce HW burden on memorizing many variations of pilot positions
Phase tracking performance is not sensitive to specific pilot distribution
  As far as all pilot tones are reasonably separated for frequency diversity
Proposal: Fixed absolute pilot position per PPDU BW, independent of resource allocation
  Keep relative pilot position close to legacy design, when possible
  Align pilots of different RU size: use pilot puncture when needed
Lin Yang, Bin Tian (Qualcomm)

## Slide 23: Pilot Structure for RU >26 tones
52 tone RU
  Existing legacy pilot structure: half even half odd indices
  After moving to even index, perfectly align with pilots in the corresponding two 26 tone RUs
106 tone RU
  Prefer to use available pilots in corresponding two 52 tone RUs with pilot puncturing
    106 tones have 4 pilots while 2 x 52 have 8
    Puncturing is performed in a mirror symmetric way within 242 tones to make it more evenly spread within 996 tone RU in 80MHz.
242 tone RU
  Same number of pilots as two 106 RUs
  Align with pilots in corresponding two 106 tone RUs
7
DC
242 + 3 DC
102+4 pilots
102+4 pilots
13
13
5 Edge
5 Edge
6 Edge
6 Edge
26
26
26
26
26
26
26
52
52
52
52
26
1
1
1
1
13
1
1
1
1
13
5 Edge
5 Edge
6 Edge
6 Edge
7
DC
13
13
7
DC
-116 -90 -48 -22 22 48 90 116
-102 -76 -62 -36 -10 10 36 62 76 102
pilot tone index
0 5 19 32 46 51
11a 52-tone pilot structure
HE20 pilot structure
11ax 52-tone pilot structure with aligning to pilots in 26-tone RU
0 6 20 32 46 51
0 6 20 25
26 32 46 51
Lin Yang, Bin Tian (Qualcomm)

## Slide 24: Proposed Pilot Locations
HE80
12 Edge
12 Edge
12 Edge
12 Edge
13
13
13
13
13
13
13
13
11 Edge
11 Edge
11 Edge
11 Edge
11 Edge
7
DC
7
DC
7
DC
7
DC
12 Edge
996 usable tones +5 DC
242
242
26
26
52
102+4
102+4
2
2
26
52
26
26
52
26
102+4
102+4
26
26
26
26
26
26
52
1
1
26
1
26
52
2
1
2
1
1
1
26
26
2
52
1
1
2
26
2
26
52
1
2
1
26
26
26
26
2
52
1
1
2
1
1
1
1
2
1
242
242
26
26
52
102+4
102+4
2
2
26
52
26
26
52
26
102+4
102+4
26
26
26
26
26
26
52
1
1
26
1
26
52
2
1
2
1
1
1
26
26
2
52
1
1
2
26
2
26
52
1
2
1
26
26
26
26
2
52
1
1
2
1
1
1
1
2
1
7
DC
26
26
26
26
26
26
26
52
52
52
52
26
242 + 3 DC
102+4 pilots
102+4 pilots
1
1
1
1
13
1
1
1
1
13
13
13
5 Edge
5 Edge
5 Edge
5 Edge
6 Edge
6 Edge
6 Edge
6 Edge
7
DC
13
13
7
DC
HE20
-116 -90 -48 -22 22 48 90 116
-102 -76 -62 -36 -10 10 36 62 76 102
pilot tone index
HE40
12 Edge
12 Edge
12 Edge
12 Edge
11 Edge
11 Edge
11 Edge
11 Edge
5
DC
5
DC
5
DC
5
DC
242
26
26
26
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
242
26
26
26
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
102+4
26
52
26
1
1
26
52
26
1
2
1
2
1
1
-238 -212 -170 -144 -104 -78 -36 -10
pilots tone index
-224 -198 -184 -158 -130 -116 -90 -64 -50 -24
10 36 78 104 144 170 212 238
24 50 64 90 116 130 158 184 198 224
pilot tone index
-494 -426 -360 -292 -252 -184 -118 -50
-468 -400 -334 -266 -226 -158 -92 -24
-480 -454 -440 -414 -386 -372 -346 -320 -306 -280 -238 -212 -198 -172 -144 -130 -104 -78 -64 -38 -10
24 92 158 226 266 334 400 468
10 38 64 78 104 130 144 172 198 212 238 280 306 320 346 372 386 414 440 454 480
50 118 184 252 292 360 426 494
Lin Yang, Bin Tian (Qualcomm)

## Slide 25: Summary
A balanced leftover tone placement plan is proposed for OFDMA tone plan
Different CFO tracking approaches in 11ax preamble are compared and the solution of using single stream pilots (like in 11ac) in HE-LTF is recommended
Fixed pilot structure is proposed, with the following salient benefits
  All pilots are placed at even tones for any RUs, such that 2x LTF and 4x LTF/data can use same set of pilots
  Fixed pilot location independent of resource allocation, making OFDMA processing simpler
  Pilot locations are aligned in all RUs, more implementation friendly
Lin Yang, Bin Tian (Qualcomm)

## Slide 26: Straw Poll 1
Do you agree to add the following to the 11ax SFD:
The left over tones location for 20/40/80 MHz tone plan are shown in the diagrams as in slide 11?
Note: Leftover tones have zero energy
Y/N/A
Lin Yang, Bin Tian (Qualcomm)

## Slide 27: Straw Poll 2
Do you agree to add the following to the 11ax SFD:
Single stream pilot (like 11ac) in HE-LTF shall be used for SU, DL and UL OFDMA as well as in DL MU-MIMO transmissions
Y/N/A
Lin Yang, Bin Tian (Qualcomm)

## Slide 28: Straw Poll 3
Do you agree to add the following to the 11ax SFD:
All pilot tones in 4x data OFDMA symbol are at even indices
If pilots present in 4x HE-LTF, their tone indices shall be the same as those pilots in 4x data symbol
If pilots present in 2x HE-LTF, their tone indices shall be the same as the indices of those pilots in 4x data symbol divided by 2
Y/N/A
Lin Yang, Bin Tian (Qualcomm)

## Slide 29: Straw Poll 4
Do you agree to add the following to the 11ax SFD:
The pilot location for 20/40/80MHz bandwidth are as shown in the diagrams in slide 24
  Note: 80MHz pilot positions are enumerated below for reference
    RU-26 pilots: ±10, ±24, ±38, ±50, ±64, ±78, ±92, ±104, ±118, ±130, ±144, ±158, ±172, ±184, ±198, ±212, ±226, ±238, ±252, ±266, ±280, ±292, ±306, ±320, ± 334, ±346, ±360, ±372, ±386, ±400, ±414, ±426, ±440, ±454, ±468, ±480, ± 494
    RU-106/242/484 pilots: ±24, ±50, ±92, ±118, ±158, ±184, ±226, ±252, ±266, ±292, ±334, ±360, ±400, ±426, ±468, ±494
    RU-996 pilots: ±24, ±92, ±158, ±226, ±266, ±334, ±400, ±468
The pilot locations for 160MHz or 80+80 use the same structure as 80MHz for each half of the BW
Y/N/A
Lin Yang, Bin Tian (Qualcomm)

## Slide 30: Reference
[1] IEEE 802.11-15/0330r4 OFDMA Numerology and Structure
[2] IEEE 802.11-16/0577r1 Pilot Design for 11ax
[3] IEEE 802.11-15/0812r0 Pilot Design for Data Section
[4] IEEE 802.11-15/0602r2 HE-LTF Sequence for UL MU-MIMO
Lin Yang, Bin Tian (Qualcomm)

## Slide 31: Appendix
Lin Yang, Bin Tian (Qualcomm)

## Slide 32: Simulation Setup
20MHz 8x8 D NLOS, 1x1 UMi NLOS
11ac CSD: [0 -400 -200 -600 -350 -650 -100 -750]ns
SNR and CFO
  20dB SNR with 1KHz CFO
  10dB SNR with 3KHz CFO
  6 dB SNR with 6KHz CFO
2x LTF
Testing phase estimation approaches in LTF stage
  [1]-like Nss orthogonal LTF sequences for Nss streams
  SSP based: Using Same Number of Pilots in 2x LTF as in 4x LTF – 8 pilots in 256FFT
  SSP based: Using 2x Numerology in 2x LTF for Pilots – 6 pilots in 128FFT
Testing metrics
  CCDF of frequency estimation error
  MSE of channel interpolation error
Lin Yang, Bin Tian (Qualcomm)