## Slide 1: Considerations on HE-SIG-A/B
Date: 2015-07-12
Authors:

## Slide 2: Abstract
This submission shows the following considerations on HE-SIG-A and HE-SIG-B for DL-OFDMA:
#1 Possible contents for HE-SIG-B
#2 HE-SIG-B configurations
#3 Possible decoding optimization

## Slide 3: Consideration #1: MCS per OFDMA Resource Unit
We agreed some patterns for OFDMA building blocks at May 2015 meeting. [2]
It is preferable for each resource unit to use different MCS for better efficiency. Combination of resource units also should be identified for each transmission.
e.g. Combination of resource units
16 OFDMA assignments in 80MHz BSS (ref: slide 30 of 15/330r5)
Proposal #1:
Resource unit assignment and MCS for respective resource unit will be contents in HE-SIG-B.

## Slide 4: Consideration #1: e.g. Expression of HE-SIG-B
Bits:
RU QTTY
8
RU Info #1
8
RU Info #2
8
RU Info #n
8
….
RU
width
MCS
Bits:
3
4
RU width:
0: SU
1: 26 tones
2: 52 tones
3: 106 tones
4: 242 tones
5: 484 tones
MCS:
MCS index for 11ac are 0~9.
1
reserved
It can be expressed in 3 bits.
4 bits will be enough.
This is just an example.
It can be optimized more.
RU = Resource Unit

## Slide 5: Consideration #2: Possible Configurations of HE-SIG-B [3][4]
HE-
SIG-A
...
HE-
SIG-B
variable
Dup.
HE-
SIG-A
Dup.
HE-
SIG-B
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-
SIG-B
Dup.
HE-
SIG-A
Dup.
HE-
SIG-B
Dup.
L-Part
Dup.
L-Part
Primary
20MHz
HE-
SIG-A
...
HE-
SIG-B
1
variable
Dup.
HE-
SIG-A
HE-
SIG-B
2
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
HE-
SIG-B
3
Dup.
HE-
SIG-A
HE-
SIG-B
4
Dup.
L-Part
Dup.
L-Part
Primary
20MHz
HE-
SIG-A
...
variable
Dup.
HE-
SIG-A
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-
SIG-A
Dup.
L-Part
Dup.
L-Part
HE-
SIG-B
Primary
20MHz
Option-A. Duplicated HE-SIG-B per 20MHz
Option-B. Non-duplicated HE-SIG-B per 20MHz
Option-C. Entire-channel HE-SIG-B
HE- SIG-A
HE-SIG-B
HE-SIG-B
HE- SIG-A
HE-SIG-B
4µs per OFDM Symbol
16µs per OFDM Symbol
…
…
…
time
frequency
10MHz
10MHz
20MHz
Option-D. HE-SIG-B per resource unit
HE-SIG-A needs to have segment information of resource units.  It’s not feasible.
That big information will not fit in HE-SIG-A.

## Slide 6: Consideration #2: Required OFDM Symbols
BW | Max. QTTY of RU | Max. size of HE-SIG-B (required bits) | Required OFDM symbols for HE-SIG-B (64FFT) * |  | 
 |  |  | A | B | C
20M | 9 | 80 | 4 | 4 | 4
40M | 18 | 152 | 7 | 4 | 4
80M | 37 | 304 | 13 | 4 * | 4
160M | 74 | 600 | 25 | 4 * | 4
Note-1) HE-SIG-B structure on Slide-4 is assumed.
Note-2) 48 available subcarriers and coding rate = 1/2 are assumed per 20MHz.
* It’s subject how to express the resource units across two 20MHz. (next slide)
Option-A isn’t efficient. It may not be practical.
Proposal #2:
HE-SIG-B should not be duplicated in every 20MHz as Option-A.

## Slide 7: Consideration #2: An Issue on Option-B
Some resource units are across two 20MHz sub-bands.
 How can we express these resource units in Option-B case??

## Slide 8: Consideration #3: Decoding Issue for DL-OFDMA??
Definitive destination address will be acquired from decoded MAC frame.
A receiving STA has to decode all resource units to pick up a desired MAC frame.
HE-
SIG-A
...
HE-
SIG-B
1
Dup.
HE-
SIG-A
HE-
SIG-B
2
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
HE-
SIG-B
3
Dup.
HE-
SIG-A
HE-
SIG-B
4
Dup.
L-Part
Dup.
L-Part
Primary
20MHz
HE-
SIG-A
...
Dup.
HE-
SIG-A
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-
SIG-A
Dup.
L-Part
Dup.
L-Part
HE-
SIG-B
Primary
20MHz
: Minimum required portion for decoding
Option-B.
Option-C.
It may be complicated for a receiving STA to decode the entire DL-OFDMA frame of multi-resource units with various MCSs and resource segmentations.

## Slide 9: Consideration #3: Possible Optimization for Decoding Schemes
When HE-SIG-A has an indication for sub-band selection, a receiving STA may be able to limit decoding portion just for a specific 20MHz.
That indication will be with Multi-Access (MA) group ID. (Need further studies)
HE-
SIG-A
...
HE-
SIG-B
1
Dup.
HE-
SIG-A
HE-
SIG-B
2
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
HE-
SIG-B
3
Dup.
HE-
SIG-A
HE-
SIG-B
4
Dup.
L-Part
Dup.
L-Part
Primary
20MHz
HE-
SIG-A
...
Dup.
HE-
SIG-A
L-Part
Dup.
L-Part
Dup.
HE-
SIG-A
Dup.
HE-
SIG-A
Dup.
L-Part
Dup.
L-Part
HE-
SIG-B
Primary
20MHz
: Minimum required portion for decoding
Option-B.
Option-C.
Not well-optimized
This optimization may reduce required processing power to decode DL-OFDMA frame on a receiving STA.  I’m not sure if this is true.
Figures below are examples that are indicated in HE-SIG-A as 2nd 20M to be decoded.
Indication for
sub-band selection

## Slide 10: Consideration #3: Issues
MA Group Indication:
  How to make up the group for each sub-band?
Resource units across two 20MHz sub-bands:
  The same issue as Slide-7
Others?

## Slide 11: Conclusion
Some contents of HE-SIG-B are proposed for DL-OFDMA PPDU.
    Resource unit assignment (RU QTTY,RU width)
    MCS per RU
HE-SIG-B should not be duplicated on every 20MHz sub-band for better efficiency.
Sub-band selection measure in HE-SIG-A was proposed as a potential optimization.
    It may possibly reduce required processing power to decode DL-OFDMA PPDU on a receiving STA.

## Slide 12: Straw Poll #1
Do you agree to add the following text into 11ax SFD?
3.2.3 HE-SIG-B
HE-SIG-B includes resource unit assignment and MCS per resource unit for DL-OFDMA PPDU.
Y/N/A =

## Slide 13: Straw Poll #2 (not for Motion)
Do you think that a sub-band selection measure at reception of DL-OFDMA PPDU will help to reduce required processing power on a receiving STA?
Y =
N =
Interesting, but need more studies =
I don’t care =

## Slide 14: References
[1] doc. 11-15/132r5, “Specification Framework for TGax”
[2] doc. 11-15/330r5, “OFDMA Numerology and Structure”
[3] doc. 11-15/621r2, “Design Principles for HE Preamble”
[4] doc. 11-15/557r0, “Preamble Structure in 802.11ax”