## Slide 1
Simulation Results for Box5 Calibration
Date: 2015-07-12
Authors:

## Slide 2: Abstract
During IEEE 802.11 May meeting, the agreement on Box5 detail simulation parameters was presented in [1].
Based on the agreed simulation conditions, we provide the two set of test results from the Box5 test cases;
  Results of max 64 MPDU per A-MPDU to be presented in the contribution;
  Results of max 32 MPDU per A-MPDU was combined into the joint-contribution 11-15/0802
Single BSS results comparison with partners’ show good alignment;

## Slide 3: PHY Parameters

## Slide 4: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps Random start time during a 10ms interval
MPDU size | 1544 Bytes (1472 Data + 28 IP header + 8 LLC header + 30 MAC header + 4 delimiter + 2 padding)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, immediate BA without explicit request], Max aggregation: 32 or 64 MPDUs
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Running time | 200s per drop, 30 drops per data
Output metric | -CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time) -PER of all AP/STA (1 - # of success subframes / # of transmitted subframes)

## Slide 5: 11ac Scenario 6 – OBSS Enterprise
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association

## Slide 6: 11ac SS6 Traffic Flow Model
DL/UL traffic assigned for each STA
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow

## Slide 7: Test Cases for Step-by-Step Calibration of 11ac SS6
1 BSS (upper-right corner BSS B)
  DL only case
  UL only case
    1 STA: each STA-AP
    2 STAs: 3+9, 3+15, 3+27
    3 STAs: 3+9+15, 3+9+27
  DL & UL case
2 BSS (A+B)
  Both DL only
  Both UL only
  A DL and B UL
  B UL and A DL
3 BSS
  DL only
  UL only
  Mixed DL & UL

## Slide 8: Single BSS Simulation Results (max 64 MPDU per A-MPDU)
 | STA#3 |  | STA#9 |  | STA#15 |  | STA#21 |  | STA#27 |  | Sum (Mbps)
 | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | 
DL | 41.12 | 0.00 | 42.03 | 0.00 | 41.16 | 0.00 | 42.05 | 0.00 | 42.03 | 0.00 | 208.39
UL - One STA Only | 99.97 | 0.00 |  |  |  |  |  |  |  |  | 99.97
 |  |  | 99.98 | 0.00 |  |  |  |  |  |  | 99.98
 |  |  |  |  | 99.78 | 0.00 |  |  |  |  | 99.78
 |  |  |  |  |  |  | 97.94 | 0.00 |  |  | 97.94
 |  |  |  |  |  |  |  |  | 99.78 | 0.00 | 99.78
UL - Two STA | 98.64 | 0.10 | 97.38 | 0.11 |  |  |  |  |  |  | 196.02
 | 98.75 | 0.10 |  |  | 97.65 | 0.10 |  |  |  |  | 196.40
 | 98.80 | 0.10 |  |  |  |  |  |  | 97.34 | 0.11 | 196.14
UL - 3 STA | 60.00 | 0.17 | 60.63 | 0.17 | 60.19 | 0.17 |  |  |  |  | 180.82
 | 65.71 | 0.17 | 62.83 | 0.17 |  |  |  |  | 60.23 | 0.18 | 188.77

## Slide 9: 2 BSS (A+B) Simulation Results DL-Only (Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 3.8015 | 5.421 | 5.5914 | 5.8565 | 5.7369 | 5.0447 | 5.4455 | 5.4581 | 5.8885 | 5.3023 | 5.5832 | 5.7196 | 4.6846 | 4.5872 | 4.8941 | 4.259 | 5.3694 | 4.9026 | 5.7243 | 5.6633 | 20.3859 | 20.7335 | 20.5534 | 18.4745 | 20.9635
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.0865 | 0.1037 | 0.0355 | 0.0794 | 0.0555 | 0.0684 | 0.027 | 0.0736 | 0.0222 | 0.087 | 0.0865 | 0.0614 | 0.0418 | 0.0129 | 0.0301 | 0.0503 | 0.0452 | 0.0867 | 0.0398 | 0.0404 | 0.0923 | 0.0772 | 0.026 | 0.0679 | 0.0688

## Slide 10: 2 BSS (A+B) Simulation Results UL-Only(Max.64 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.3919 | 0.3491 | 0.5313 | 0.4292 | 0.4887 | 0.3895 | 0.3818 | 0.3904 | 0.3798 | 0.3912 | 0.4248 | 0.3933 | 0.4424 | 0.3869 | 0.3604 | 0.3561 | 0.4554 | 0.3368 | 0.3022 | 0.3876 | 0.6012 | 0.2856 | 0.2421 | 0.2866 | 0.2482
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 6.1882 | 6.8789 | 3.8044 | 6.6454 | 3.5044 | 3.3981 | 4.7517 | 6.4258 | 5.3567 | 6.9773 | 5.8586 | 6.4745 | 4.6294 | 7.8107 | 3.9047 | 6.4658 | 5.3331 | 8.1168 | 10.6558 | 5.8202 | 1.3138 | 5.8505 | 9.3517 | 14.8746 | 10.3731

## Slide 11: 2 BSS (A+B) Simulation Results A-DL / B – UL (Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 1.2537 | 1.72 | 1.5215 | 1.0782 | 1.4753 | 1.8849 | 1.0654 | 1.8312 | 1.2789 | 1.5862 | 1.8033 | 1.871 | 1.5434 | 1.8143 | 1.6213 | 0.8611 | 1.3842 | 1.8825 | 1.7835 | 1.5273 | 27.066 | 30.306 | 30.9663 | 36.2375 | 26.267
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.0974 | 0.1157 | 0.0026 | 0.044 | 0.0594 | 0.1245 | 0.0297 | 0.0969 | 0.0007 | 0.1513 | 0.1055 | 0.0628 | 0.0124 | 0.0298 | 0.0366 | 0.1147 | 0.0566 | 0.1751 | 0.0249 | 0.0774 | 0.2805 | 0.2504 | 0.2388 | 0.2206 | 0.285

## Slide 12: 2 BSS (A+B) Simulation Results A-UL / B - DL(Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 9.7156 | 5.9542 | 4.5627 | 5.8725 | 9.3237 | 11.9791 | 4.6926 | 8.4824 | 6.8449 | 8.2375 | 6.7346 | 10.1448 | 5.5517 | 5.0129 | 7.5777 | 7.7979 | 6.5398 | 9.187 | 6.8897 | 6.0149 | 2.1431 | 1.9439 | 1.7984 | 1.6403 | 2.2348
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.2962 | 0.3849 | 0.4934 | 0.3913 | 0.2912 | 0.2679 | 0.4603 | 0.3374 | 0.4036 | 0.3429 | 0.3428 | 0.3338 | 0.4164 | 0.4479 | 0.3871 | 0.3611 | 0.4017 | 0.3078 | 0.3809 | 0.4102 | 0.1004 | 0.1535 | 0.0224 | 0.1239 | 0.1564

## Slide 13: 3 BSS DL-Only Simulation Results (Max.64 MPDU)
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 2.5567 | 2.7754 | 2.2783 | 3.0028 | 2.4571 | 2.6398 | 2.4233 | 2.4337 | 2.7537 | 2.9554 | 2.8232 | 2.9336 | 1.7775 | 2.654 | 2.913 | 2.7131 | 2.7669 | 2.8147 | 15.7863 | 18.3877 | 17.3374 | 18.2098 | 24.5447 | 24.4214 | 21.2226 | 20.4709
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.0887 | 0.0662 | 0.0654 | 0.0615 | 0.0961 | 0.1043 | 0.0204 | 0.1178 | 0.0628 | 0.0852 | 0.1478 | 0.0938 | 0.0306 | 0.0271 | 0.0758 | 0.1135 | 0.1041 | 0.0407 | 0.0454 | 0.085 | 0.0261 | 0.0461 | 0.0217 | 0.0592 | 0.0474 | 0.0545

## Slide 14: 3 BSS UL-Only Simulation Results (Max.64 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.487 | 0.3297 | 0.3263 | 0.4209 | 0.4797 | 0.3707 | 0.3799 | 0.3698 | 0.3634 | 0.3963 | 0.3515 | 0.4018 | 0.4748 | 0.1773 | 0.1805 | 0.1513 | 0.5126 | 0.1991
Chart: Throughput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 2.5692 | 5.2225 | 9.3174 | 5.5864 | 4.3532 | 6.8856 | 10.4201 | 6.4995 | 1.9538 | 2.327 | 4.96 | 6.1681 | 13.0057 | 41.3708 | 37.3064 | 56.0041 | 6.7443 | 32.8282

## Slide 15: Result Comparison Single BSS Operation - DL
Chart: 
| STA #3 | STA #9 | STA #15 | STA #21 | STA #27 | SUM
Huawei | 39.583 | 39.626 | 39.448 | 38.629 | 38.277 | 195.563
Intel | 39.73 | 38.61 | 39.13 | 38.02 | 40.28 | 195.78
Sony | 39.76 | 39.745 | 39.027 | 38.071 | 38.775 | 195.378
NTT | 38.885 | 38.866 | 38.811 | 38.96 | 38.799 | 194.322
LG | 41.64 | 41.57 | 41.45 | 41.79 | 42.04 | 208.49
Marvell | 39.73 | 39.87 | 40.596 | 39.816 | 39.109 | 199.121
ZTE | 38.95 | 40.62 | 40.19 | 40.61 | 38.95 | 199.32
MTK | 40.542 | 40.427 | 40.056 | 39.468 | 38.914 | 199.407

## Slide 16: Result Comparison Single BSS Operation - UL
Chart: 
| 3 | 9 | sum
Huawei | 93.628 | 93.378 | 187.006
Intel | 93.77 | 93.12 | 186.89
Sony | 93.455 | 93.077 | 186.532
NTT | 92.669 | 92.638 | 185.308
LG | 93.83 | 93.24 | 187.07
Marvell | 94.865 | 93.602 | 188.467
ZTE | 93.32 | 93.764 | 187.24
MTK | 99.815 | 99.826 | 199.641
Chart: 
| 3 | 15 | sum
Huawei | 92.578 | 93.683 | 186.261
Intel | 93.13 | 95.62 | 188.75
Sony | 93.358 | 93.221 | 186.579
NTT | 93.048 | 92.82 | 185.869
LG | 92.89 | 94.63 | 187.52
Marvell | 91.947 | 99.84 | 191.787
ZTE | 94.4 | 92.59 | 186.99
MTK | 99.906 | 99.797 | 199.703
Chart: 
| 3 | 27 | sum
Huawei | 93.284 | 93.546 | 186.83
Intel | 93.63 | 93.35 | 186.98
Sony | 93.338 | 93.298 | 186.636
NTT | 93.111 | 92.795 | 185.905
LG | 93.76 | 93.01 | 186.77
Marvell | 91.115 | 94.695 | 185.81
ZTE | 92.83 | 93.99 | 186.82
MTK | 99.841 | 99.737 | 199.578
Chart: 
| 3 | 9 | 15
Huawei | 59.894 | 60.183 | 61.125
Intel | 60.46 | 59.23 | 61.47
Sony | 59.451 | 61.18 | 58.941
NTT | 58.37 | 61.447 | 59.484
LG | 57.09 | 60.59 | 61.65
Marvell | 56.335 | 55.552 | 73.321
ZTE | 63.58 | 63.99 | 63.48
MTK | 70.928 | 63.202 | 59.371
Chart: 
| 3 | 9 | 27
Huawei | 59.942 | 61.198 | 58.862
Intel | 54.62 | 63.26 | 63.21
Sony | 59.944 | 59.3 | 60.256
NTT | 60.373 | 59.324 | 60.034
LG | 63.94 | 65.41 | 48.62
Marvell | 59.035 | 63.844 | 57.143
ZTE | 63.36 | 64.31 | 63.65
MTK | 63.196 | 68.249 | 62.656

## Slide 17: Conclusion
In this submission we have provided:
  Integrated SLS Box-5 test results
  Results comparison with some other companies’ show good alignment in single BSS;

## Slide 18: Reference
[1] 11-15/0680r2 Reference Box5 Calibration Assumptions and Parameters
[2]

## Slide 19: Backup - Intel Results of max 32 MPDU per A-MPDU

## Slide 20: Single BSS Simulation Results (max 32 MPDU per A-MPDU)
 | STA#3 |  | STA#9 |  | STA#15 |  | STA#21 |  | STA#27 |  | Sum (Mbps)
 | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | 
DL | 39.73 | 0.00 | 38.61 | 0.00 | 39.13 | 0.00 | 38.02 | 0.00 | 40.28 | 0.00 | 195.76
UL - One STA Only | 99.78 | 0.00 |  |  |  |  |  |  |  |  | 99.78
 |  |  | 99.78 | 0.00 |  |  |  |  |  |  | 99.78
 |  |  |  |  | 99.77 | 0.00 |  |  |  |  | 99.77
 |  |  |  |  |  |  | 98.03 | 0.00 |  |  | 98.03
 |  |  |  |  |  |  |  |  | 99.77 | 0.00 | 99.77
UL - Two STA | 93.77 | 0.11 | 93.12 | 0.11 |  |  |  |  |  |  | 186.89
 | 93.13 | 0.11 |  |  | 95.62 | 0.09 |  |  |  |  | 188.75
 | 93.63 | 0.11 |  |  |  |  |  |  | 93.35 | 0.11 | 186.98

## Slide 21: Single BSS Simulation Results (cont.) (max 32 MPDU per A-MPDU)
 | STA#3 |  | STA#9 |  | STA#15 |  | STA#21 |  | STA#27 |  | Sum (Mbps)
 | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | Tput (Mbps) | PER | 
UL - 3 STA | 60.46 | 0.17 | 59.23 | 0.17 | 61.47 | 0.16 |  |  |  |  | 181.16
 | 54.62 | 0.17 | 63.26 | 0.17 |  |  |  |  | 63.21 | 0.16 | 181.09

## Slide 22: 2 BSS (A+B) Simulation Results DL-Only (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 4.3654 | 4.728 | 5.0249 | 5.0181 | 5.7784 | 5.0286 | 5.5498 | 4.9123 | 5.2162 | 5.5084 | 4.1471 | 5.4269 | 5.9561 | 5.0966 | 4.6475 | 3.8906 | 4.1763 | 4.4948 | 4.3701 | 4.9613 | 19.2428 | 19.9425 | 18.6107 | 19.3507 | 20.3305
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.0709 | 0.0963 | 0.0322 | 0.0679 | 0.0455 | 0.0899 | 0.0153 | 0.0888 | 0.0174 | 0.0912 | 0.0852 | 0.0676 | 0.039 | 0.0223 | 0.0483 | 0.0714 | 0.0687 | 0.1075 | 0.0609 | 0.0479 | 0.0883 | 0.0627 | 0.0168 | 0.0923 | 0.0953

## Slide 23: 2 BSS (A+B) Simulation Results UL-Only(Max.32 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.3924 | 0.3914 | 0.4437 | 0.4357 | 0.4491 | 0.4047 | 0.3883 | 0.368 | 0.4367 | 0.3877 | 0.3727 | 0.4187 | 0.4339 | 0.4426 | 0.4043 | 0.4161 | 0.3885 | 0.3529 | 0.4198 | 0.3668 | 0.5351 | 0.4348 | 0.2134 | 0.2704 | 0.2795
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 6.7485 | 6.4227 | 2.8557 | 3.8862 | 2.9077 | 4.641 | 6.5025 | 6.4279 | 4.6724 | 5.2735 | 6.5685 | 5.9308 | 4.072 | 5.0862 | 6.1547 | 5.1601 | 7.0662 | 7.8132 | 4.7314 | 7.7273 | 2.6258 | 4.4643 | 16.0388 | 16.7342 | 13.3583

## Slide 24: 2 BSS (A+B) Simulation Results A-DL / B – UL (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 2.6575 | 2.4434 | 2.3155 | 2.2555 | 2.1297 | 1.7233 | 2.2135 | 2.0597 | 1.9291 | 2.1241 | 1.8077 | 1.9219 | 2.3655 | 2.3789 | 2.2776 | 2.3806 | 2.8449 | 2.1012 | 2.0025 | 2.2224 | 25.0768 | 24.3469 | 28.7782 | 32.1669 | 23.9718
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.113 | 0.0962 | 0.0139 | 0.076 | 0.038 | 0.0781 | 0.0124 | 0.0977 | 0.0135 | 0.1125 | 0.1113 | 0.0595 | 0.0109 | 0.0027 | 0.0092 | 0.0892 | 0.0714 | 0.1818 | 0.038 | 0.0837 | 0.2778 | 0.2812 | 0.2392 | 0.2205 | 0.2702

## Slide 25: 2 BSS (A+B) Simulation Results A-UL / B - DL(Max.32 MPDU)
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 0.3529 | 0.3772 | 0.4092 | 0.4354 | 0.4269 | 0.4096 | 0.4125 | 0.3867 | 0.4275 | 0.4389 | 0.3609 | 0.3522 | 0.4165 | 0.464 | 0.4102 | 0.3981 | 0.4099 | 0.3776 | 0.4241 | 0.4676 | 0.1529 | 0.1729 | 0.0257 | 0.2806 | 0.1128
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27
 | 8.6849 | 8.3079 | 7.1105 | 5.8768 | 6.3024 | 6.8015 | 6.377 | 7.5445 | 6.3234 | 5.3432 | 8.8186 | 7.5343 | 7.1357 | 5.0529 | 6.4172 | 7.8613 | 5.7698 | 8.1308 | 6.0904 | 5.1276 | 2.5213 | 2.0636 | 3.9354 | 2.5253 | 1.9546

## Slide 26: 3 BSS DL-Only Simulation Results (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 3.3176 | 3.3856 | 3.5366 | 2.9365 | 2.5657 | 3.6503 | 3.4515 | 3.505 | 3.5554 | 3.5554 | 3.0132 | 3.2708 | 3.6273 | 3.1524 | 3.4996 | 2.2911 | 3.1105 | 3.2816 | 14.576 | 19.3549 | 19.2546 | 19.1336 | 18.5144 | 15.418 | 14.5838 | 17.1099
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.1023 | 0.1029 | 0.0686 | 0.0709 | 0.079 | 0.1381 | 0.0166 | 0.1096 | 0.0638 | 0.1198 | 0.0779 | 0.0783 | 0.0753 | 0.0246 | 0.1005 | 0.1032 | 0.0722 | 0.0501 | 0.0491 | 0.0744 | 0.0216 | 0.0799 | 0.0415 | 0.0577 | 0.1067 | 0.0847

## Slide 27: 3 BSS UL-Only Simulation Results (Max.32 MPDU)
Chart: Thoughtput (Mbps)
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 7.3638 | 4.5858 | 8.4145 | 9.717 | 3.0691 | 5.8898 | 5.2393 | 6.9682 | 7.5678 | 4.1387 | 5.7887 | 7.8612 | 22.3888 | 18.0633 | 30.6298 | 41.1647 | 6.4727 | 24.6282
Chart: PER
| 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29 | 3 | 9 | 15 | 21 | 27 | 6 | 12 | 18 | 24 | 30
 | 0.3896 | 0.4037 | 0.4437 | 0.357 | 0.5387 | 0.3557 | 0.4262 | 0.4866 | 0.4583 | 0.4435 | 0.4874 | 0.3769 | 0.364 | 0.2992 | 0.2155 | 0.2224 | 0.643 | 0.2587