## Slide 1: Extensible Preamble Format Design
Date: 2015-07-12
Authors:

## Slide 2: Summary
Every time a new amendment requiring a new PHY preamble format, a new preamble format autodetection needs to be defined. While the method we used since 11n to 11ac is extensible, its efficiency is very low.
We propose to create a new preamble format that is straightforward extensible for future PHY ammendments (i.e. encode the preamble format in the SIG field).
To do this, the first step is to have a way to distinguish the new preamble format from the old preamble format. The rest is simply looking at the encoded format bits.

## Slide 3: Proposal- Develop an extensible new preamble format
START
STEP 1:
New Format?
11ac Autodetection
Step 2:
11ax and future format detection
N
Y
Step 1: Isolate the New Preamble Format
Step 2: Define an extensible encoding for 11ax
and future extensions

## Slide 4: Step 1: Isolating the new preamble format
BPSK
BPSK
BPSK
1. By using BPSK in the 2 symbols after L-SIG, we quickly narrow down the option to
  11ax+
  Legacy with BPSK modulated data
To rule out Legacy with BPSK, several approaches can be made [1-2].
  CRC check
  Service Field Check
  Additional QBPSK symbol at the end of HE-SIG2
  Special patterns in HE-SIG1 (Repeated L-SIG, Signatures)
HE-SIG2
HE-SIG1
L-STF
L-LTF
L-SIG
TBD

## Slide 5: Step 2: Define an extensible format to separate 11ax+ preamble formats
HE-SIG2
HE-SIG1
L-STF
L-LTF
L-SIG
BPSK
BPSK
BPSK
TBD
TBD (actual 11ax-SIG bits)
11ax indicator
1
Note: 11bx, 11cx, etc. are future extensions
TBD (actual 11bx-SIG bits)
0
1
11bx indicator
TBD (actual 11cx-SIG bits)
0
0
11cx indicator
1
Propose a Prefix code for encoding the format

## Slide 6: Benefits of Proposed Step 2
With Step 1, 11ax devices can readily distinguish its packet from 11ac and earlier packet formats. However with Step 2, it can also distinguish itself from future extensions.
Step 2 can either serve as an additional check for detecting 11ax preambles or a built in spoofing method that can be used by future ammendments.
3. Once the received frame is judged to be of the new format, detections of the future extensions have
Accuracy - Equal to the BER of the L-SIG (or HE-SIG). This already has very good accuracy due to the Viterbi decoder.
Extensibility- Only one bit overhead for 11ax. Additional bit per future extension.
3. By using a prefix code based encoding, we don’t need to allot any bits for extensions that doesn’t exist yet.

## Slide 7: References
[1] 11-15/0579, “Preamble design and auto-detection,” Hongyuan Zhang (Marvell)
[2] 15/0081, “Considerations on 11ax Auto-detection Methods,” Jaeyoung Song (KAIST)

## Slide 8: Strawpoll
Do you support the idea of having a new extensible preamble format where 11ax devices can detect future 802.11 extensions.
Y/N/A:

## Slide 9: Strawpoll
Do you agree to add the following to 11ax SFD:
The HE PPDU shall include a TBD number of format indication bits in HE-SIG-A Field.
Y/N/A: