## Slide 1: Follow up Discussion on The Receiver Behavior
Date: 2015-07-13
Authors:

## Slide 2: Abstract
This is a follow up presentation to the “Receiver Behavior for DSC/CCAC with BSS Color” (11-15-0595-02) which we presented in the May 2015 session.
In order to improve the spectrum efficiency in dense environments, it is important to recognize whether the received signal is from the same BSS or not.
In this document, we would like to discuss some basics of the receiver behavior to evaluate DSC/CCAC technique.

## Slide 3: Requirements on the Receiver Behavior
The receiver behavior relevant to the minimum sensitivity:
The start of a valid OFDM transmission at a receive level equal to or greater than the minimum modulation and coding rate sensitivity (–82 dBm for 20 MHz channel spacing, –85 dBm for 10 MHz channel spacing, and –88 dBm for 5 MHz channel spacing) shall cause CS/CCA to indicate busy with a probability > 90% within 4 μs for 20 MHz channel spacing, 8 μs for 10 MHz channel spacing, and 16 μs for 5 MHz channel spacing.
If the preamble portion was missed, the receiver shall hold the CCA signal busy for any signal 20 dB above the minimum modulation and coding rate sensitivity (–62 dBm for 20 MHz channel spacing, –65 dBm for 10 MHz channel spacing, and –68 dBm for 5 MHz channel spacing).
In order to improve the spectrum efficiency in OBSS environments, we may need to consider a new threshold to allow transmission

## Slide 4: Identification of the received signal
Upon detection of a signal:
  A STA identifies whether the received signal is from the same BSS or not.
    There will be some ways to identify whether the signal is from the BSS or not, but details will be the next step of discussion.
  If the signal is from the same BSS:
    The STA needs to defer its transmission in order not disturb on going transmission.
  If it is not:
    The STA shall be allowed to start its transmission if certain conditions are met.

## Slide 5: Evaluation
DSC simulation scenario agreed in 15/0652r1
UL full-buffer traffic
No DSC (CCAC or Rx sensitivity control)
Max 32 MPDUs aggregated
1472 byte for L4 payload
AP1
STA1
AP2
STA2
35m
3m
3m

## Slide 6: Simulation Results
Throughput can be doubled by allowing transmission even when a STA detects signal from the other BSS.
Chart: 
| w/o BSS indicator | w/ BSS indicator
 | 193.2879 | 364.0521
x 1.9

## Slide 7: Summary
In order to improve the spectrum efficiency, CCA needs to be modified to consider if the signal is from the same BSS or not.
Simulation results show potential benefit of this technique.
Transmission criteria needs to be investigated to combine this technique with DSC.

## Slide 8: References
[1] Matthew Fischer, “CID 205 BSSID Color Bit,” doc.: IEEE 802.11-13/1207r1
[2] Masahito Mori, “Performance Analysis of BSS Color and DSC,” doc.: IEEE 802.11/14-1403r0
[3] Graham Smith, “Dynamic Sensitivity Control Practical Usage,” doc.: IEEE 802.11-14/0779r2
[4] Nihar Jindal, “Performance Gains from CCA Optimization,” doc.: IEEE 802.11-14/0889r3
[5] Koichi Ishihara, “Consideration of asynchronous interference in OBSS environment,” IEEE 802.11-14/1148r1
[6] Takeshi Itagaki, “Performance Analysis of BSS Color and DSC,” doc.: IEEE 802.11-15/0045r0
[7] John Son, “Legacy Fairness Issues of Enhanced CCA,” doc.: IEEE 802.11-15/0085r1
[8] Yasu Inoue, “Receiver Behavior for DSC/CCAC with BSS Color”, IEEE 802.11-15/0595r2