## Slide 1: Multiple BSSID element
Date: 2015-08-01
Authors:

## Slide 2: Abstract
Submission [1] proposes the use of the Multiple BSSID element with 802.11ax. The submission was presented during the July 2015 meeting but attendees asked for more time to review the principles of the Multiple BSSID element. The present submission intends to provide further explanations about the Multiple BSSID element.

## Slide 3: Multiple SSIDs/BSSIDs
Traditionally, 802.11 assumes a concept of “one AP, one BSS”
This concept evolved with the need for separate WLANs for different sets of users
Many vendors offer Virtual AP (VAP) capabilities where a single, physical AP pretends to be multiple APs
  Some products support up to 32 VAPs
With n VAPs n beacon frames are needed, causing huge airtime consumption

## Slide 4: Typical VLAN use
Today’s Ethernet deployments heavily rely on Virtual LANs (VLANs)
  Even the most simple deployment will use two or more VLANs
Virtual APs reflect this network design
  One hardware AP imitates to be multiple APs (VAPs)

## Slide 5: Functionally equivalent
Pretending to be multiple APs means that all management functionality is multiplied
  Each virtual AP sends its own beacon frame
  This is functionally equivalent to having multiple hardware APs collocated

## Slide 6: Example
In 2.4 GHz, we observe a typical beacon size of 250 B
  [4] reports about typical beacon size in the order or 1000 B (!)
  Many deployments provide DSSS access assuming 1 Mb/s data rate for management frames
    Beacon frame duration is 2 ms then
  With 3 APs collocated and each AP implementing 4 VAPs, every beacon interval (102.4 ms) consists of 3 × 4 × 2 ms = 24 ms beacon airtime
Without considering medium access overhead 23.4% of airtime can be easily consumed by beacon frames in this example

## Slide 7: Multiple BSSID element
The Multiple BSSID element collapses information for multiple BSSIDs (= SSIDs) into one single beacon frame
  If not otherwise needed, this avoids sending the same information elements (e.g. EDCA parameter set etc.) several times
The Multiple BSSID element is defined in 802.11v-2011

## Slide 8: 802.11v-2011 – Source of the Multiple BSSID element
802.11v-2011 provides means for Wireless Network Management
  The project had seven letter (LBs) and nine sponsor ballots (SBs)
  The PAR was approved 2004-12-08
  The final amendment was approved 2011-02-09
The final draft had 98% approval rate
  During the final LB [2] no commenter [3] addressed the Multiple BSSID element

## Slide 9: What about legacy clients?
A chicken and egg problem
  Most legacy clients cannot interpret the Multiple BSSID element, thus, most APs do not support it
    Most clients do not implement the Multiple BSSID element because few APs support it
    Most APs do not support the Multiple BSSID element as few clients support it

## Slide 10: Why implement it in 802.11ax?
Mixed operation of 802.11ax and non-802.11ax clients relies on VAPs
  Legacy client see only “main” SSID
W/o legacy clients, 802.11ax APs can solely rely on the Multiple BSSID element
  Save multiple beacon frame transmissions
  AP sharing becomes easier
We observe professional deployments to turn off support for certain legacy implementations/features
  A similar transitioning will occur with 802.11ax
  Then, the market will benefit from the Multiple BSSID element
It seems likely that mandatory support for the Multiple BSSID element in 802.11ax will stipulate implementation with legacy products too

## Slide 11: Chicken and eggs …
Once we overcome the chicken and egg problem, the implementation of the Multiple BSSID element will make sense
  802.11ax has the necessary momentum to push the market to the right direction
  Vendors backport 802.11ac (performance relevant) solutions from 5 GHz to 2.4 GHz (802.11n)
    If 802.11ax implements the Multiple BSSSID element as mandatory feature, new 802.11n and 802.11ac products will use it too
  Let’s do not leave this chance unused

## Slide 12: Straw Poll

## Slide 13: Straw Poll
Do you agree to add the following to the IEEE 802.11 TGax Specification Framework?
  Add to the end of Clause 6 (MAC): “HE STAs shall support the Multiple BSSID Set.”

## Slide 14: Motion
Transform successful straw poll into a motion

## Slide 15: Motion
Moved to add to the end of Clause 6 (MAC) of the IEEE 802.11 TGax Specification Framework:
  “HE STAs shall support the Multiple BSSID Set.”
  Moved by:
  Seconded:

## Slide 16: References
G. R. Hiertz et al., “Efficiency enhancement for 802.11ax,” Jul. 2015. [Online]. Available: https://mentor.ieee.org/802.11/dcn/15/11-15-0871
D. Stanley and E. Qi, “TGv Letter Ballot Comment Resolutions,” Sep. 2009. [Online]. Available: https://mentor.ieee.org/802.11/dcn/09/11-09-0929
“Voters List for Recirculation Letter Ballot 155 (TGv Draft 7.0) And previous Ballots: 140, 146 and 150,” [Online]. Available: http://www.ieee802.org/11/LetterBallots/LB155v/LB155_voters_list.xls
M. Fischer, “A Possible Solution to the Beacon Length Problem,” May 2015. [Online]. Available: https://mentor.ieee.org/802.11/dcn/15/11-15-0531