## Slide 1: NAV Consideration for UL MU Response to Trigger frame
Date: 2015-09-13
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chittabrata Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com

## Slide 2: Authors (continued)
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea | +82-1023566164 | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi’an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple | Cupertino, CA | +1-408-974-5967 | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Yuichi Morioka | Sony Corporation | 1-7-1 Konan Minato-ku, Tokyo 108-0075, Japan |  | Yuichi.Morioka@jp.sony.com
Masahito Mori |  |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 9: Abstract
Trigger frame [1], used in UL MU, creates a unique contention procedure. Specifically, the transmission from the STA is initiated by the AP rather than the STA.
As a result, when AP sends trigger frame, AP does not consider the NAV setting at the triggered STAs, and the transmissions from the triggered STAs may disrupt existing transmissions protected by NAV.
We discuss the NAV consideration for the responding STAs polled by a trigger frame for UL MU transmission.

## Slide 10: Current Rule of Considering NAV for Response Frame
Current 802.11 [2] specifies that
When a STA receives a frame addressed to it that requires an immediate response, except for RTS, it shall transmit the response independent of its NAV
For RTS frame, the response rule [2] is
A STA that receives an RTS frame addressed to it considers the NAV in determining whether to respond with CTS, unless the NAV was set by a frame originating from the STA sending the RTS frame

## Slide 11: Consideration for UL MU
If we follow the current rule, then STA does not consider NAV when responding to trigger frame.
When multiple STAs respond to trigger frame for UL MU transmission, existing transmissions protected by NAV may be disrupted with high probability.
  Propose to consider NAV when responding to trigger frame
  Simulation shows that considering NAV when responding to trigger frame is beneficial for existing transmission protected by NAV (See Appendix)

## Slide 12: Exception
As described before, when responding to RTS frame, a STA does not need to consider NAV when the NAV was set by a frame originating from the STA sending the RTS frame
Propose to follow this rule when responding to trigger frame
  a STA does not need to consider NAV when the NAV was set by a frame originating from the AP sending the trigger frame

## Slide 13: Consideration for ACK/BA
The frame in response to the trigger frame may contain ACK or BA due to MU-BAR [3] or cascading TXOP structure [4,5]
  In current spec, ACK/BA is always responded when the frame is correctly received.
  ACK/BA is important.
    Without responding ACK/BA when the frame is correctly received, the correct reception is lost, and the error recovery protocol on the transmitter side such as MCS selection is affected
  However, ACK/BA response may be long due to aggregation with other MPDUs [4,5]
  Propose to take ACK/BA and the duration of UL MU transmission into consideration
  Not consider NAV when the response contains ACK/BA, and the duration of the UL MU transmission is below a TBD threshold

## Slide 14: Conclusion
We discuss the NAV consideration for UL MU response to trigger frame
  Propose to consider NAV when responding to trigger frame
  Propose not to consider NAV when the NAV was set by a frame originating from the AP sending the trigger frame
  Propose not to consider NAV when the response contains ACK/BA, and the duration of the UL MU transmission is below a TBD threshold

## Slide 15: Straw Poll #1
Do you agree to add to the TG Specification Frame work document?
  x.y.z. A STA that is polled from a trigger frame for UL MU transmission considers the NAV in determining whether to respond unless one of the following conditions is met
    the NAV was set by a frame originating from the AP sending the trigger frame
    the response contains ACK/BA and the duration of the UL MU transmission is below a TBD threshold
    Other condition TBD
Yes:
No:
Abstain

## Slide 16: Reference
11-15-0365-00, UL MU Procedure
IEEE P802.11-REVmcTM/D4.0
11-15-1053-00, Multi-User Block ACK Request (MU-BAR)
11-15-0841-01, Cascading Structure
11-15-0831-02, Broadcast and Unicast (Trigger) in DL MU
11-14-0980-14, Simulation Scenarios

## Slide 17
Appendix

## Slide 18: Simulation Setting - Scenario 3
19 BSS and 9 STAs per BSS
Carrier Frequency: 2.4 G
Bandwidth: 20MHz
9 STAs in center BSS uses contention for transmission with RTS/CTS
Other BSSs use trigger based transmission, i.e., AP sends trigger to solicit UL OFDMA transmission,
  TX Bandwidth for each triggered STA: 2MHz
Detailed parameters follow the setting in simulation scenario [3]
Trigger based UL MU Transmission
Contention based UL Transmission

## Slide 19: Simulation Results
Without considering NAV, the throughput of legacy BSS, which has NAV protection, is affected
By considering NAV for response, the throughput of legacy BSS improves, and the throughput of AX BSSs is not significantly affected
 | Average STA throughput (Mbps) in center BSS | Average STA throughput (Mbps) in other BSSs
AX STAs do not consider NAV for trigger response | 0.3902 | 0.6796
AX STAs Consider NAV for trigger response | 0.4505 | 0.6658