## Slide 1: Considerations on PHY Padding and Packet Extension in 11ax
Date: 2015-09-14
Authors:

## Slide 2: Abstract
HE PHY padding and Packet Extension is proposed for 11ax [1].
  Receiver must finish processing of the frame within SIFS .
  4x OFDM symbol numerology may require faster processing speed and/or die area size increase in order to process data within SIFS.
We discuss consideration aspects to the proposal.

## Slide 3: Overview of Proposed PHY Padding in [1]
Pre-FEC Padding with a-factor segment boundary in the last mSTBC OFDM symbol
  Padding performed before encoding
Post-FEC Padding up to the end of the last mSTBC OFDM symbol
  Padding inserted after encoding but before interleaving
Packet Extension appended after the last OFDM symbol
  Two constellation thresholds (threshold8, threshold16,) per {BW, NSS}
  3 group of PE capability with 0 µs, Max PE 8µs and Max PE 16µs for each STA
Example of non-STBC with a = 1 based on Max PE 16 µs mode
Freq.
Time
…
a-factor set to 1
OFDM Symbol
Last OFDM Symbol
Excess info bits + Pre FEC padding
Packet Extension
Post FEC Padding

## Slide 4: Overview of Proposed PHY Padding in [1] (cont.)
Focused on relaxation of LDPC decoding processing time.
  Proposed padding scheme is not optimized for BCC.
  BCC has a inherently different processing flow (e.g. bit level interleaving) and proposed PHY padding in [1] may not be suitable for relaxing decoding processing time.
Only NDBPS.short (excess info bits and Pre-FEC padding bits) and the first a×NSD.short are taken for LDPC encoder and LDPC decoder, respectively.
  NSD.short is roughly chosen as ¼ number of tones from each RU size
Post-FEC padding bits are not processed for LDPC.
RU size | 26 | 52 | 106 | 242 | 484 | 996 | 996×2
NSD.short | 6 | 12 | 24 | 60 | 120 | 240 | 492

## Slide 5: LDPC Implementation Considerations
Time required to correctly decode LDPC encoded bits depend on several implementation factors.
  Receiver architecture
  Target number of iterations
    A tradeoff between processing speed vs. packet error rate
  Clock speed
    A tradeoff between processing speed vs. power consumption
  Die area size
    A tradeoff between processing speed, power consumption vs. implementation cost
  Number of codewords to process in an unit time period
Each vendor will optimize speed, power, and die area size according to their needs. Difficult to mandate a particular design in 802.11 standards.
Number of codewords plays an important role in estimating/determining decoding processing time. 802.11 LDPC is a block encoding scheme and bits are processed in units of codeword.

## Slide 6: Simplified Rx Processing Diagram
Example of Timing Relationships (BCC-nonSTBC)
Nth OFDM symbol
(N-1)th OFDM symbol
(N-2)th OFDM symbol
…
TPE
N-1
Required processing time for a = 4
a = 4
TSIFS
TSIFS
TPost-FEC
a = 2
TPE
…
TFFT+Eq+BCC interlever WR
TBCC interleaver RD
TBCC decoding
Required processing time for a = 2
N
N-1
N-2
N-2
N-1
N
N-2
N-1
N-1
N
N
N
N
N

## Slide 7: Simplified Rx Processing Diagram (cont’d)
Nth OFDM symbol
(N-1)th OFDM symbol
(N-2)th OFDM symbol
…
TPE
N-1
N
Required processing time for a = 4
Two TLDPC decoder of (N-1)th and Nth after the last OFDM symbol are important to claim the proper value of Max TPE for each STA.
Ncw, LLDPC and NSYM are a function of length of PSDU, NSS, NSD, constellation and R.
Example of Timing Relationships (LDPC-nonSTBC)
a = 4
TSIFS
TSIFS
TPost-FEC
a = 2
TPE
…
TFFT+Eq+LLR+Tone mapper WR
TTone mapper RD
TLDPC decoding
Required processing time for a = 2
N
N
N
N
N
N
N-1
N-1
N-1
N-2
N-2
N-2

## Slide 8: Simplified Rx Processing Diagram (cont’d)
Example of Timing Relationships (LDPC-STBC)
Nth OFDM symbol
(N-1)th OFDM symbol
(N-2)th OFDM symbol
…
TPE
N-1
Required processing time for a = 4
a = 4
TSIFS
TSIFS
TPost-FEC
a = 2
TPE
…
Required processing time for a = 2
Paired two OFDM symbols
a = 4
(N-3)th OFDM symbol
Paired two OFDM symbols
(N-3) & (N-2)
a = 2
N-3
N-2
(N-3) & (N-2)
N-1
N
(N-1) & N
N-3
N-2
N-1
N
(N-1) & N
(N-3) & (N-2)
(N-3) & (N-2)
(N-3) & (N-2)
(N-3) & (N-2)
TFFT+Eq+Tone mapper WR
TTone mapper RD
TLDPC decoding
TFFT+Eq+STBC+LLR+Tone mapper WR

## Slide 9: Analysis of LDPC Codeword Mapping
Main factors in determining required processing time for LDPC is number of codewords to process.
  At the end of the transmission, receiver must process all the codewords in the last OFDM symbol & any unprocessed (leftover) codewords from the 2nd last OFDM symbol.
  In case of STBC, the codewords in the last four OFDM symbols may effect required processing time.
Example) Both case 1 and case 2 require almost similar processing time, even though case 1 has Post-FEC padding to reduce bits (smaller a-factor).
  Although transmitted codeword length between two case is different (from shorting / puncturing / repetition), LDPC decoder processes 1944 bit block per codeword.
Example of non-STBC with a-factor set to 3
…
NCBPS
NCBPS.SHORT
Last OFDM symbol NCBPS
…
Case 1
Case 2
APEP_Length = 5150 bytes,
NSS = 2, NSD = 980,
MCS=8, LCW = 1944
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
LCW,1
LCW,2 > LCW,1
APEP_Length = 6150 bytes,
NSS = 4, NSD = 468,
MCS=9, LCW = 1944
Based on [1]

## Slide 10: Analysis of LDPC Codeword Mapping (cont’d)
Example of non-STBC with a-factor set to 3
In some cases the number of LDPC codewords is identical regardless of following 11ac padding rules (i.e. always a=4) or following padding rules proposed in [1] (i.e. a-factor 2 or 3).
  Especially when codeword density is less than four codewords per OFDM symbol.
…
Last OFDM symbol NCBPS
NCBPS.SHORT
NCBPS
codeword
codeword
codeword
codeword
codeword
APEP_Length = 37250 bytes,
NSS = 2, NSD = 468,
MCS=7, LCW = 1944
codeword
codeword
codeword
codeword
codeword
…
Based on [1]
Based on 11ac rules
LCW,1
LCW,2 > LCW,1

## Slide 11: STBC
In BCC/LDPC, one of the TPost-FEC is wasted and is required to process twice the number of bits/codewords at the end of the last OFDM symbol.
  STBC is rate 1 scheme, therefore received bits/symbols are processed in pair of OFDM symbol (i.e. two OFDM symbol). Therefore, receiver must buffer twice the amount of received bits before being able to process them.
Last 2 OFDM symbol in STBC
a = 2:
TPE
Excess Info
bits
Pre-FEC
Padding
bits
Post-FEC
Padding bits
Packet Extension
Excess Info
bits
Pre-FEC
Padding
bits
Post-FEC
Padding bits
…
Tpost-FEC
Tpost-FEC

## Slide 12: Some Finding on a-factor Configuration
There are instants where using a-factor 3 (or sometimes even a-factor 2) doesn’t reduce the number of codewords to be processed by LDPC. Some examples in the table below.

## Slide 13: Some Finding on a-factor Configuration (cont’d)
The 4us (or 8us) extra decoding relaxation time (TPost-FEC) thought to be available from use of a-factor 3 (or a-factor 2) may not exist depending on PSDU size, number of spatial stream, MCS, and RU size.
Excess Info bits
last OFDM symbol (non-STBC)
Pre-FEC
padding bits
a = 3:
Post-FEC
padding bits
Packet Extension
Required processing time
Secured processing time
Secured processing time
Processing time thought to have saved

## Slide 14: Summary
Depending on receiver design, SIFS (16us) may not be enough to fully process all received bits.
Relaxing decoding processing time, with use of Post-FEC padding requires further analysis.
  BCC/LDPC receiver is a complex system and reduction in processing time by use of a-factor cannot be linearly modeled by reduction in number of encoded bits in the last OFDM symbol.
We encourage members and vendors to further check implementation consideration aspects for PHY padding methodology proposed in [1] before agreeing on concepts therein.

## Slide 15: References
[1] 11-15-0810r0, HE PHY Padding and Packet Extension